3GPP TSG-RAN WG3 Meeting #113-e	R3-214227

16 – 26 August 2021

Online

Agenda Item:	23.2.2

Source:	Ericsson

Title:	Signaling Transport - Summary of offline discussion

Document for:	Discussion and Decision

# 1	Introduction

The scope of the email discussion has been captured as followed:

CB: # eNBarchEvo3_CPUPTransport - HW: Update the note in section 7 with that each instance of gNB-CU-CP could be treated as ng-eNB-CU-CP or eNB-CP, and each instance of gNB-CU-UP could be treated as ng-eNB-CU-UP or eNB-UP, for ng-eNB or eNB CP/UP separation respectively - E///: NR user plane protocol for E-UTRA PDCP will support at least functions already supported by X2 interface user plane protocol (TS 36.425) RAN3 to discuss and decide what are the additional functions from NR user plane protocol to be supported for E-UTRA PDCP Update TS 38.425 by dropping “NR” from the “NR PDCP” references in TS38.425 for functions to be supported for E-UTRA PDCP and keep the NR reference to functions that are only supported for NR PDCP - Chair: Discuss and decide the additional functions from NR user plane protocol to be supported for E-UTRA PDCP Check details and provide TPs if agreeable (E///- moderator) Summary of offline disc in R3-214227

This contribution captures the email discussion.

# 2	For the chairman’s notes

To be captured later

# 3	Email discussion – Phase 1

During RAN3#111-e and RAN3#112-e, the following agreements were taken:

Use SCTP as transport bearer for AP signaling

Reuse the E1 signaling bearer protocol stack for the new interface

The same functions as specified for E1 signaling bearer should also be supported over the new interface

DTLS over SCTP should be supported

Multiple SCTP endpoints per CP/UP pair should be supported

The first SCTP association could be triggered either by CP or by UP, but the additional SCTP associations should be initiated by UP

SCTP multi-homing should also be supported

RAN3#112e:

For sec 1, add new sentences including the new logical names

For section 3, add only references to definitions

No changes needed to secs. 4 and 5

For section 6, add the new eNB logical entities names (agreed in CB 48) to each occurrence of the gNB-CU-CP and gNB-CU-UP

For section 7, add a note establishing the equivalence between all the CP logical entities and between all the UP logical entities

Continue to discuss if anything is missing

## 3.1 Signaling transport (TS 38.462)

In [1], the proposal is to modify the note added to section 7 to:

Note: The transport layer structure and mechanism specified in this section are also used between ng-eNB-CU-CP and ng-eNB-CU-UP or between eNB-CP and eNB-UP, unless stated otherwise. With this understanding, in this section each instance of gNB-CU-CP could be treated as eNB-CP or ng-eNB-CU-CP, and each gNB-CU-UP could be treated as eNB-UP or ng-eNB-CU-UP, for eNB or ng-eNB CP/UP separation respectively.

Question 1.1: Do you agree in updating the note as proposed in [2]?

| Company | Response |
| --- | --- |
| Ericsson | Yes |
| Samsung | Yes |
| Huawei | Yes |
| Deutsche Telekom | Yes |
| Nokia | Yes |
| ZTE | Yes |

## 3.2 Transport of UP data (TS 38.425)

In [3] and [4], the proposal is to capture the usage of E-UTRA PDCP into TS 38.425. This is dependent to CB: # eNBarchEvo2_General and the confirmation of the WA, but the discussion below may be started, under the assumption that the WA is confirmed.

The first question could be very general:

Question 2.1: Is it necessary to explicitly capture E-UTRA PDCP into TS 38.425?

| Company | Response |
| --- | --- |
| Ericsson | Yes. Even if this is with a simple note at the very beginning of the specification, it is necessary to capture that E-UTRA can be applied to TS 38.425 |
| Samsung | Yes. It is necessary to capture E-UTRA PDCP in TS 38.425. |
| Huawei | Yes. We also think such a note is beneficial. |
| Deutsche Telekom | Yes. It should be explicitly stated to avoid any misinterpretation. |
| Nokia | Yes |
| ZTE | Yes |

During phase 1 of the discussion, it is worth discussing the following principles:

- Functions with impact on E-UTRA PDCP or on LTE in general shall not be supported

- Functions with no impact on E-UTRA PDCP or on LTE in general should be supported

Question 2.2: Do you agree with the above principles in order to identify the functions and frame elements which can be applied to E-UTRA PDCP?

| Company | Response |
| --- | --- |
| Ericsson | Yes |
| Samsung | Yes |
| Huawei | Yes |
| Deutsche Telekom | Yes |
| Nokia | Yes |
| ZTE | Yes |

Phase 1 of this email discussion can start identifying the functions which cannot be supported for E-UTRA PDCP. Phase 2 may identify additional ones, and conclude on the frame elements which cannot be applied to E-UTRA PDCP.

Question 2.3: Which functions of TS 38.425 cannot be applied if E-UTRA PDCP is used?

| Company | Response |
| --- | --- |
| Ericsson | Assistance Information for PDCP duplication |
| Samsung | PDCP duplication related and Delay measurement related information would not be used for E-UTRA PDCP. In addition, the Caue Value seems not be used for E-UTRA PDCP. We need to further check the radio quality assistance information. |
| Huawei | Agree the above |

In [3], 2 solutions to capture E-UTRA PDCP are discussed:

- Capture an overall statement stating “that NR PDCP also mean E-UTRA PDCP unless specified”

- Functions where the frame elements and associated functions are to be supported for E-UTRA PDCP will be referenced to 38.425 by dropping the “NR” from the “NR PDCP”

Question 2.4: Which solution should be used to capture E-UTRA PDCP into TS 38.425?

| Company | Preferred solution | Comment |
| --- | --- | --- |
| Ericsson | 2 (slightly) | Solution 2 will bring a more elegant result but will need a much higher impact on the specifications. Maybe it’s worth asking the rapporteur for its opinion. However, figures for PDU types 0 and 1 should not be impacted. Solution1 is preferred in that case. |
| Samsung |  | We have no strong opinion, but solution 2 is ok. |
| Huawei | 1 (slightly) | In fact we slightly prefer option 1, as the second option will lead to too many changes on the current specification. |
| Deutsche Telekom | 2 (slightly) | Both are feasible. |

# 4	Conclusion

Result of the email discussion to be captured here

# 5	References

[1] R3-213333 - Further discussions on signalling transport for the new interface (Huawei)

[2] R3-213334 - (TP for BL CR TS 38.462) Signalling transport to the new interface (Huawei)

[3] R3-213876 - Transport of UP data for LTE CP/UP split in E-UTRAN (Ericsson)

[4] R3-213877 - Transport of UP data - Introduction of E-UTRA PDCP in NR UP protocol (Ericsson)