3GPP TSG-RAN WG3 #113-e							   R3-214236

16-26 Aug 2021

Online

Agenda Item:	13.3.2

Source:	ZTE (moderator)

Title:	                 Summary of Offline Discussion on CB: # 1306_IAB_Multi-hop

Document for:	Approval

# Introduction

# 1306_IAB_Multi-hop

-Discuss the following solutions for avoiding source IP filtering issue in Inter Donor DU re-routing:

- Opt1: The target IAB-donor-DU is provided with the source IP address of re-routed packets.

- Opt4: a tunnel between source Donor-DU and target Donor-DU. The tunnel may be dynamic or static, pending further discussion.

- A static tunnel between source CU and target donor DU

- Any other solution?

-Shall a wide-scope solution be considered, e.g. for both inter-donor-DU rerouting and inter-donor routing scenarios?

(ZTE - moderator)

Summary of offline disc in R3-214236

This discussion has two phases:

Phase 1: Down-select an option for inter-donor-DU re-routing.

Phase 2: Discuss the specification impact.

The deadline for Phase 1 is Thursday, August 19, 23:59:59 UTC. This allows the moderator to prepare some proposals on Friday for Monday’s online session.

The deadline for Phase 2 is the same as for all email discussions, i.e., Tuesday, August 24, 12:00 UTC.

# For the Chairman’s Notes

# Discussion

## Issue 1   Solutions for avoiding source IP filtering issue

In last RAN3 meeting, inter-donor-DU re-routing was discussed in the CB #41_IAB_MultiHopPerf. And the following agreements were achieved.

Further evaluate following solutions to address the source IP filtering issue during inter-Donor-DU re-routing:

Opt1: The target IAB-donor-DU is provided with the source IP address of re-routed packets.

Opt4: a tunnel between source Donor-DU and target Donor-DU. The tunnel may be dynamic or static, pending further discussion.

In addition, another CB, i.e. CB# 37_IAB_InterDonorMigrationDetails discussed the inter-donor topology transport mechanism with the aim of not affecting descendant node(s), which also involves the source IP filtering issue. To avoid affecting descendant nodes, the following six options to resolve the source IP filtering issue were presented and discussed.

Option 1: Disabling of IP address filtering.

Option 2: IP-based tunneling between source CU and boundary node.

Option 3: IP address rewriting at boundary node.

Option 4: IP-based tunneling between source and target donor DU.

Option 5: Same as option 3 but applied by target donor DU rather than boundary node.

Option 6: IP-based tunneling between source CU and target donor DU.

Apparently, the same issue is discussed in two separate email discussions, but the discussion progress of these two emails are misaligned with each other. If we follow the above agreement on inter-donor-DU re-routing, the solutions are restricted to Opt1 and Opt4. However, Opt1 may be useless because the routers between the Donor-DU and donor CU may also perform ingress filtering and discard re-routed packets. For Op4, there may be significant specification impact since a new interface between donor-DUs needs to be designed by RAN3. What’s more, contribution ([1], [2] and [5]) proposed to consider option 6, i.e. IP-based tunneling between source CU and target donor DU, which was not discussed in the inter-donor-DU re-routing session. So, moderator suggests RAN3 to re-discuss the inter-donor-DU re-routing mechanism by considering the above 6 options.

Since inter-donor-DU re-routing can be used in different scenarios, e.g. intra/inter-CU migration, intra/inter-CU RLF and intra/inter-CU topology redundancy, moderator refines the 6 options to achieve a universal expression.

Option 1: Disabling of IP address filtering.

Option 2: IP-based tunneling between IAB-donor-CU and boundary node.

Option 3: IP address rewriting at boundary node.

Option 4: IP-based tunneling between old IAB-donor-DU and new IAB-donor-DU.

Option 5: IP address rewriting at the new IAB-donor-DU.

Option 6: IP-based tunneling between IAB-donor-CU and new IAB-donor-DU.

Here, the old IAB-donor-DU refers to the IAB-donor-DU the UL packet should have been delivered to. The new IAB-donor-DU refers to the IAB-donor-DU the UL packet is re-routed to.

Companies are invited to provide their views on the above options.

Q1: Please share your view and preference on the above 6 options to address the source IP filtering during inter-Donor-DU re-routing.

| Company | Option(s) | Comment |
| --- | --- | --- |
| ZTE | 6 | Option 1 looks simple, but is actually useless since IP filtering also works in transport network nodes other than IAB-donor-DU. Option 2 requires the boundary node to support IP header addition/removing, which is not aligned with Rel-16 protocol stack. Option 3 and option 5 require the boundary node or donor-DU to support IP header replacing, which is not aligned with Rel-16 protocol stack, either. Option 4 requests data transfer between DUs and new interface may be needed to enable data transfer between donor-DUs, which is not supported in NR. In our view, option 6 has less specification impact and does not require new interface since CU-UP directly communicates with DU via IP transfer is already supported in NR. So, it is suggested that option 6 is adopted to resolve the inter-donor-DU re-routing. |
| Samsung | Opt 1& Opt 4 as a package | As indicated in our contribution, no matter of which solution is applied, the target donor DU should disable the source IP filtering for the old IP address of migrated IAB node/descendant node. On the other hand, the target donor DU should be aware which IP packets should be routed via the static IP tunnel between source donor DU and target donor DU. The reason we select Opt 4 rather than Opt 6 is that Opt 6 may need more signaling since the IP tunnel should be established between target donor DU and multiple UPs. On the other hand, Opt 4 seems to open the door to allow the inter-DU data transmission, which may need more discussions on how to achieve this. One possible way is to define the signaling to indicate the tunnel endpoint information at the source donor DU to the target donor DU. This means that Rel-17 IAB WI allows the inter-DU tunnel, and such functionality can be applied to non-IAB case. This may not be a good way since whether inter-DU tunnel is supported or not need involve more people (e.g., F1 experts in each company) rather than only in IAB community. Another possible way is to only introduce stage-2 impact, and how to establish such IP tunnel becomes an implementation issue. At this moment, for option 4, we prefer to only introducing stage-2 impact and the establishment of IP tunnel becomes an implementation issue. |
| Nokia | Option 4 | Option 1 does not solve the problem, since transport routers may still perform filtering. Option 2 and 3 necessitates IP awareness at the boundary node. RAN2/RAN3 chose against it in the inter donor routing discussion, so it should not be considered any longer. Option 5 does not work if SEG implementation uses source IP address (together with SPI) for security association identification. Option 6 does not work with external security GWs (SEG). With the SEG the secure tunnel is established between the IAB node and SEG. The donor DU – CU tunnel would use the CU’s address as a destination address of the tunnel header in UL. The donor DU operates in an untrusted transport IP domain, whereas CU’s IP address belongs to trusted IAB operators IP domain, which may not be routable in a transport IP domain. Even if the packets would be routed to the CU, direct donor DU -CU tunnel would bypass the SEG, which means that CU is not able to decode encrypted inner packets. The Option 4 seem to be only viable solution. Being a just U-plane extension, unlike introduction above states, the donor DU – donor DU tunnel does not introduce a new RAN interface. Regarding to Samsung’s comment, the inter-Donor-DU tunnel can be defined only for IAB, e.g. just like the current IAB related F1/E1 procedures that does not affect normal DU. so we do not see the issue. If it is implementation issue, how to ensure IOT? |
| Ericsson | Opt4 or Opt6 | These two options should be taken for further consideration. As we explained in CB #1302 on Inter-donor Migration, our understanding is that the same solution can be used for UL inter-donor-DU local rerouting and all the other scenarios involving inter-donor routing (e.g., partial migration, for both DL and UL), as explained in CB #1302. Moreover, please note the following agreement from RAN3#111-e: One common inter-donor topology transport mechanism should be defined for all scenarios where traffic between a donor and an IAB DU traverses the network under another donor; FFS whether it is possible to achieve a common signaling design for all scenarios |
| Qualcomm | Option 4 | We agree with Nokia’s analysis. The tunnel is based on implementation since the tunneling conditions are static. |
| Lenovo | Option 1 | For option 3 and option 5, IP header rewriting solutions can be deprioritized firstly which need too much standard impacts. For option 2, since IP addresses cannot be seen by the boundary IAB node, and this option can be also excluded. While for the option 4 and option 6, the IP addresses need to be informed to the target donor, to differentiate between the rerouted UL packets and the normal UL packets. And rerouted UL IP packets need to be encapsulated with another outer IP header with the source IP address of target IAB-donor-DU. With the provided IP addresses in option 4 and 6, option 1 can work well via update the filtering configuration to avoid discard of the rerouting UL packets. While for source IP filter in the transport network nodes between target IAB-donor-DU and IAB-donor-CU, it can be resolved by implementation. |

Contribution ([2]) proposes that a statically configured IP tunnel between old IAB-donor-DU and new IAB-donor-DU, which forward packets based on source-IP-address, will certainly work. There is no reason why this tunnel needs to be dynamically configured. It also mentions the tunnel is statically configured between IAB-donor-CU and new IAB-donor-DU in option 6.

Contribution ([4]) thinks, in option 4, the statically configured tunnel does not scale well because the per-DU pair tunnel need to be pre-configured.

Q2: Please share your view on the establishment of the tunnel between old IAB-donor-DU and new IAB-donor-DU in option 4, whether static or dynamic.

| Company | Comment |
| --- | --- |
| ZTE | Prefer statically configured tunnel |
| Samsung | Static |
| Nokia | A static tunnel works, but it is inefficient (e.g. requiring OAM configuration, and does not scale well). It is better to be dynamic, but this can be discussed later once Option 4 is selected. |
| Ericsson | We can discuss this in the next step, because we had a different understanding of “static” than some other companies. |
| Qualcomm | This is astatic tunnel since the condition to enter a packet into an inter-donor-DU tunnel is static: If packet’s SRC IP address is anchored at donor-DU x ( Use tunnel x We don’t understand ZTE’s and Nokia’s replies, i.e., what non-static information a dynamic configuration would include and why this would be more efficient. |
| Lenovo | It can be discussed later if Option 4 is selected. |

Q3: Please share your view on the establishment of the tunnel between IAB-donor-CU and new IAB-donor-DU in option 6, whether static or dynamic.

| Company | Comment |
| --- | --- |
| ZTE | Prefer statically configured tunnel |
| Samsung | Not support option 6 |
| Nokia | No Option 6. There are some issues as we commented in Q1 |
| Ericsson | We support Option 6, and we think it requires further discussion, along with Option 4. We can discuss static vs. dynamic in the next step, because we had a different understanding of “static” than some other companies. |
| Qualcomm | We agree with Nokia. Option 6 does not work for IPsec tunnel mode due to presence of the SeGW. For these reasons, we should not consider it here. |
| Lenovo | It can be discussed later if Option 6 is selected. |

Contribution ([8]) proposes that, in any option, it is important to avoid the re-routed packets being discarded at the target donor DU first. So the target IAB-donor-DU should be aware of the source IP address(es) to be used by the re-routed packets before receiving any re-routed packets. Otherwise, the target IAB-donor-DU will still perform the source IP filtering to the received re-routed packets during the process in IP layer, and these re-routed packets will be discarded.

Q4: Do you agree that the source IP address(es) need to be sent to the new IAB-donor-DU no matter which option is selected?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Maybe no | For option 4 and 6, the new IAB-donor-DU should be configured with the information of the re-routed UL packets. Upon receiving a UL packet with such information, the new IAB-donor-DU shall deliver it to old IAB-donor-DU or IAB-donor-CU via the IP-based tunneling. In our view, if the UL packet is forwarded via the IP-based tunneling, the new IAB-donor-DU shall not perform the source IP filtering. RAN3 needs to discuss the configuration for the new IAB-donor-DU to differentiate between the re-routed UL packets and the normal UL packets. |
| Samsung | Yes | In our understanding, the new IAB-donor-DU anyway needs know the source IP address of the re-routed UL packets with the following two usages: The target donor DU can disable source IP filtering to the re-routed UL packets The target donor DU can identify the packets to be sent via static IP tunnels. |
| Nokia | Yes with comments | In Option 4, Target Donor-DU need to identify the applicable UL packets to be forwarded via the tunnel. Using the source IP address can be an option. |
| Ericsson | Not necessarily | As pointed out by Nokia’s contribution, a packet going into the tunnel may be a BAP or an IP packet, so the options should be considered first. |
| Qualcomm | No | Tunnel selection is solely based on the match between the packet’s SRC IP address and the donor-DU’s IP address pool. If SRC IP address from this donor-DU ( No tunneling If SRC IP address from donor-DU x ( Select tunnel x The static IP address pool of the donor-DUs does not change. We haven’t seen a single reason why inter-donor-DU rerouting needs to be dynamically enabled/disabled. |
| Lenovo | Yes | In order to differentiate between the rerouted UL packets and the normal UL packets, the IP addresses of the rerouted UL packets need to be informed to the target IAB-donor-CU. Additionally, the relation between the IP addresses and donor-DU also needs to be informed for option 4. Alternatively, if we use some other information, e.g. BAP routing IDs, to replace the IP addresses, it may cause reroute mistakenly some normal UL packets with the same BAP routing ID with the rerouted UL packets. |

## Issue 2  BAP routing towards the target IAB-donor-DU

Contribution ([5]) mentioned BAP header rewriting (based on BAP routing ID) is supported as a solution to enable inter-donor routing. The same solution (i.e., BAP header modification) can also be adopted for BAP routing towards the target IAB-donor-DU. In other words, a unified solution for both inter-donor-DU rerouting and inter-donor routing scenarios should be agreed.

In moderator’s view, this is about how to enable the re-routed packets being routed to the target IAB-donor-DU, when the destination BAP address in the BAP routing ID of the re-routed packets does not correspond to target IAB-donor-DU. However, how to enable the routing of the re-routed packets is RAN2’s work, and the issue has already been discussed by RAN2 in the [Post114-e][075][eIAB] Open Issues on Re-routing. So moderator suggests RAN3 to wait for RAN2’s progress.

Q5: Do you agree that RAN3 discuss the enhancement related to BAP routing towards the target IAB-donor-DU, after RAN2 make a decision?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes |  |
| Samsung | Yes | Wait for RAN2 progress. |
| Nokia | Yes | RAN3 discuss it after the RAN2 decision. |
| Ericsson | OK |  |
| Qualcomm | Yes | We don’t agree with the moderator’s observation that inter-donor-DU rerouting and inter-topology transport are one and the same thing. If that was the case, all IAB-nodes would be boundary nodes. |
| Lenovo | Yes |  |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-213208	Discussion on inter-Donor-DU re-routing in IAB (ZTE)

R3-213259	Inter-donor-DU local rerouting for IAB (Qualcomm Incorporated)

R3-213330	Inter-donor-DU re-routing (CATT)

R3-213534	Inter donor-DU re-routing (Nokia, Nokia Shanghai Bell)

R3-213602	The avoidance of UL Packet Discarding due to Local Re-routing (Ericsson)

R3-213693	Discussion on UL packet discarding for inter-donor-DU re-routing (Lenovo, Motorola Mobility)

R3-213700	Discussion on inter-donor-DU rerouting for Rel-17 IAB (Samsung)

R3-213936	Inter-donor re-routing for IAB and unnecessary transmission during topology update (Huawei)