3GPP TSG-RAN WG3 #114-e	R3-215932

01 – 11 Nov, 2021

Agenda Item:	9.3.6.1

Source:	Radisys (moderator)

Title:	Summary of Offline Discussion on CB # 104_F1Setup_Removal

Document for:	Approval

# Introduction

This contribution is to kick off the following discussion.

CB: # 104_F1Setup_Removal

- Check the necessity of the changes, signaling handling between logical nodes

- Capture common understanding if any

(Radisys - moderator)

Summary of offline disc R3-215932

The deadline is Thursday, November 4th, 23:00 UTC.

# For the Chairman’s Notes

For Second Round Discussion -

F1 Setup:

Moderator’s Proposal 1:

The understanding of the term “node” is different for different companies. Hence we think clarification is needed in the above sentence for the term “node” for RAN sharing and Non-sharing case. Instead of the “note” proposed in the CR R3-214762 & R3-214795, may be a small clarification in the current text (highlighted in yellow) might help better understanding for the readers of the specification.

Proposed Text from Radisys -

“This procedure erases any existing application level configuration data in the two nodes for a F1-C Interface Instance and replaces it by the one received. This procedure also re-initialises the F1AP UE-related contexts (if any) and erases all related signalling connections in the two nodes like a Reset procedure would do. “

Proposed Text from Lenovo -

The purpose of the F1 Setup procedure is to exchange application level data needed for the gNB-DU and the gNB-CU to correctly interoperate on the F1 interface instance’.

F1 Removal:

Moderator’s Proposal 2: Second round of discussion is needed to understand the purpose of F1, Xn, and EN-DC X2 Removal for Shared and Non-Shared TNLA case.

# Discussion [2nd Round]

F1 Setup:

Based on the 1st round of discussion few companies think clarification is needed for F1 Setup procedural text and few thinks not needed. Hence there are two proposed text changes to the current text in TS38.473 as highlighted in yellow below.

From 38.473 Clause 8.2.3.1

Proposed Text 1 from Radisys -

“This procedure erases any existing application level configuration data in the two nodes for a F1-C Interface Instance and replaces it by the one received. This procedure also re-initialises the F1AP UE-related contexts (if any) and erases all related signalling connections in the two nodes like a Reset procedure would do. “

Proposed Text 2 from Lenovo -

“The purpose of the F1 Setup procedure is to exchange application level data needed for the gNB-DU and the gNB-CU to correctly interoperate on the F1 interface instance’.

Companies are requested to provide feedback on the proposed text changes 1 and 2 as shown above in 2nd round of discussion

## Which of the proposed text changes from above do the companies prefer?

Please companies share your view and comment.

| Company | Comment |
| --- | --- |
| Radisys | We prefer proposed text 1 as it clarifies the meaning of node for Shared TNLA case. However we do not oppose proposed text 2 from Lenovo too. |
| Ericsson | we prefer the changes for the Removal procedures as shown in the Annex of this SoD. |
| InterDigital | Agree with Ericsson (see my comments in other sections) |

F1 Removal:

Based on 1st round of discussion, the intention of the F1, X2 and Xn Removal procedure for Shared TNLA and non-shared TNLA case is unclear. Hence second round of discussion is proposed to clarify the intent of F1, X2 and Xn Removal procedures and to propose appropriate text changes in the respective specification.

## What is the intent of F1, Xn and EN-DC X2 Removal procedures in case of Non-Shared TNLA?

| Company | Comment |
| --- | --- |
| Radisys | The intent is to remove the TNL association (signalling connection) and erase application data between two RAN Nodes. |
| Ericsson | the intent of the removal procedures do not differ between shared or non-shared TNLA, for both cases the procedure removes the interface instance. the only thing the receiving node needs to take care is that in case of shared TNLA another interface instance may still need the TNLA. |
| InterDigital | Agree with Ericsson. The intent of the removal is to remove the instance, before we made these changes in R3#104, there was one-to-one equivalency between instance and TNLA. If there is only one instance, then everything is removed. Now this is not the case for shared TNLA (shown in the note added in the F1 removal). I agree that we didn’t remove all of the ambiguity (thus we support the annex change) but since this F1 Removal procedure was added by the CRs to implement this change it is clear that this was the intention. |

## What is the intent of F1, Xn and EN-DC X2 Removal procedures in case of Shared TNLA (RAN Sharing)? Is it to remove a particular interface instance or a signaling connection (TNLA) between two RAN nodes

| Company | Comment |
| --- | --- |
| Radisys | Even in the case of Shared TNLA, the purpose of the F1, Xn and EN-DC X2 Removal is to remove a TNL association between a pair of RAN Nodes. This is also clear from the “note” added in the specification for Shared TNLA case as shown below. Similar note is also available in TS36.423 and TS 38.423 for X2 and Xn Removal procedures NOTE: In case the signalling transport is shared among several F1-C interface instances, and the TNL association is still used by one or several F1-C interface instances, the initiating node should not initiate the removal of the TNL association. F1 Removal procedural text is the only exception which talks about removal of F1-C interface instance in few places, and removal of signaling connection is few others |
| Ericsson | see above |
| InterDigital | See above |

If companies think F1, Xn and EN-DC X2 Removal procedures in case of Shared TNLA is it to remove a particular interface instance, then the Interface Instance Indication IE in Xn and X2 Removal message will help the peer node to identify which interface instance is requested to be removed.

However in case of F1, Transaction ID IE is used for dual purposes – to identify a parallel transaction and to identify an Interface Instance. TS 38.473 Clause 9.3.1.23 says –

“NOTE:	If F1-C signalling transport is shared among multiple interface instances, the Transaction ID is allocated so that it can be associated with an F1-C interface instance. The Transaction ID may identify more than one interface instance.”

When a Transaction ID IE is passed in F1 Removal procedure how will a CU know if it’s a parallel transaction or identification of a F1-C interface instance? This issue is unique to F1 Removal procedure as rest of the Interface Management Procedures have PLMN information in the message through which CU can identify the RAN sharing. F1 Removal procedure alone in Interface Management Procedures does not have PLMN information for CU to differentiate between Parallel transaction and RAN Sharing case.

## If companies think F1, Xn and EN-DC X2 Removal procedures in case of Shared TNLA, removes a particular interface instance - how can a gNB-CU identify that the Transaction ID IE in F1 Removal message is indicating a parallel transaction or identifying a particular F1-C Interface Instance

| Company | Comment |
| --- | --- |
| Radisys | We think this issue is specific to F1 interface. In X2 and Xn, there is no parallel transaction, hence no Transaction ID. X2 and Xn also has Interface Instance Indication IE to identify a particular Interface Instance during Setup and Removal procedures. In case of F1, since Transaction ID is used for dual purposes, it complicates the Removal procedure. A common OAM is needed between CU and DU for CU to know the Transaction ID range allocated for different F1-C interface instances. Else just with Transaction ID and without any PLMN information, CU will not know which F1-C interface instance to be removed. Also it is not possible for CU to differentiate between a parallel F1 Removal and the first F1 Removal procedure to remove a F1-C Interface Instance based on Transaction ID IE So, we think the best way to move forward is to align the F1 Removal procedural text with the rest of the interfaces X2 and XN and allow removal of TNLA via F1 Removal for Shared TNLA case. Else we may need to introduce PLMN information in F1 Removal message to identify a F1-C interface instance to be removed and also have procedural text clarification across 38.473, 38.423 and 36.423 to indicate Interface Instance Removal. |
| Ericsson | this is not a matter of believe or “thinking”, this is about current specification. There is no additional information needed to identify an interface instance. |
| InterDigital | Since I lead the offline discussion when we agreed on this (RAN3#104), I have a few comments - we decided to add Interface Instance Indication IE in X2 and Xn (structured like Transaction ID in F1AP), however we did not find a reason why transaction ID ranges couldn’t be used to distinguish interface instances, so we decided that we didn’t need to add Interface Instance Indication IE (III) to F1AP since it would be redundant (for example see the summary of discussion R3-195932). So, in F1AP the transaction id uses ranges in place of the III. There was discussion and a proposal (submitted to the meeting I believe, if not just came up in the discussion) to add transaction id to X2 and XNAP but ultimately it was agreed to use III. |

# Discussion [1st Round]

According to [1] statement in 38.473 states that subsequent F1 Setup procedures will erase existing application-level configuration data in two nodes. Another statement for Shared TNLA states that several F1 Setup procedures may be issued via the same TNLA

“This procedure erases any existing application-level configuration data in the two nodes and replaces it by the one received. This procedure also re-initialises the F1AP UE-related contexts (if any) and erases all related signalling connections in the two nodes like a Reset procedure would do. “

The above statement is common for Shared TNLA case and non-Shared TNLA case. The meaning of the term “node” for Shared TNLA and non-Shared TNLA case is not clear.

## What does nodes in the above statement mean for Shared TNLA case and Non-Shared TNLA case?

Please companies share your view and comment.

| Company | Comment |
| --- | --- |
| Radisys | Based on the usage of the term “nodes” in 38.473 specification, assumption is that a “node” means gNB-CU or gNB-DU. Since the above statement is common for Shared TNLA and non-Shared TNLA case, it indicates that multiple F1 Setup procedures issued over Shared TNLA will erase the previous application-level data. Hence for Shared TNLA case where multiple F1 Setup procedures are issued for different F1-C interface instance, the statement is not clear whether F1 setup from one F1-C interface instance will clear the application-level data from another F1-C interface instance. |
| Ericsson | Maybe it is beneficial to first look at the scenario which utilizes shared TNLA. As can be read in 38.401, the option only applies for RAN sharing with multiple Cell ID broadcast, where each cell ID broadcast in SIB1 corresponds to a different logical gNB, hence different pairs of gNB-CU/DUs. As the term “node” refers to the two logical nodes between which an interface instance is established (as the moderator confirms), it is clear that the F1 Setup procedure cannot concern those logical nodes which are about to be connected via a different interface instance, but have only the shared TNLA in common. This is conveyed by the word 'related' ('...and erases all related signalling connections in the two nodes...'), which refers to only those two nodes concerned by that specific interfaces instance. Therefore, it cannot happen that F1 Setup signaling on one interface instance has an effect on application level data on another interface instance. Note, that the entity that distributes the payloads sent via the that are transmitted via the shared TNLA distinguishes the interface instances by observing the “Transaction ID” in a way described for that IE in F1AP (§9.3.1.23). |
| Nokia | In our understanding, the term node is referring to logical gNB-CU and logical gNB-DU respectively. Hence, an F1 Setup corresponding to a F1-instance between two logical nodes will not affect the data of a different F1-instance. |
| Samsung | Same understanding as Ericsson and Nokia. “node” is referring to a logical node, i.e., logical gNB-CU/gNB-DU. And F1 setup is for the interface instant between logical gNB-CU and logical gNB-DU. |
| ZTE | In TS38.473, section 8.2.3.1, the description is given as below: NOTE: If F1-C signalling transport is shared among multiple F1-C interface instances, one F1 Setup procedure is issued per F1-C interface instance to be setup, i.e. several F1 Setup procedures may be issued via the same TNL association after that TNL association has become operational. The same TNL association could not be shared by multiple nodes, which should be used by two nodes (one CU-DU pair). With the description above, multiple F1 Setup procedures may be issued via the same TNLA, which means that multiple F1-C interface instances could exist between two nodes. As there is no explicit description to indicate the node is the logical node, We think it is reasonable to add the Note. |
| Lenovo, Motorola Mobility | In the F1AP, it is state that ‘The purpose of the F1 Setup procedure is to exchange application level data needed for the gNB-DU and the gNB-CU to correctly interoperate on the F1 interface’. The ‘F1 interface’ is not described from logical interface point of view. If possible, it would be better to change ‘F1 interface’ to ‘F1 interface instance’ to avoid any confusion. |

## Do you agree for a clarification in the above sentence for Shared TNLA case?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Radisys | Yes | The statement needs a clarification between Shared and Non-Shared TNLA case like other “Note” in the textual description of F1 Setup Procedure. |
| Ericsson | No | as explained above |
| Nokia | No | In our view the existing statement in the specification should not lead to an incorrect behavior. |
| Samsung | No |  |
| ZTE | Yes | As explain in 3.1, the clarification is needed. |
| Lenovo, Motorola Mobility | Yes | As explained in section 3.1, it would be better to change ‘F1 interface’ to ‘F1 interface instance’ to avoid any confusion. |

Summary:

3 companies think the term “node” in the F1 Setup procedural text refers to logical node for RAN Sharing case

3 companies think the term “node” in the F1 Setup procedural text refers to gNB-CU or gNB-DU for both Shared and Non-Shared TNLA case

Moderator’s Proposal 1:

The understanding of the term “node” is different for different companies. Hence we think clarification is needed in the above sentence for the term “node” for RAN sharing and Non-sharing case. Instead of the “note” proposed in the CR R3-214762 & R3-214795, may be a small clarification in the current text (highlighted in yellow) might help better understanding for the readers of the specification. We propose this for second round of discussion.

Radisys proposed text -

“This procedure erases any existing application level configuration data in the two nodes for a F1-C Interface Instance and replaces it by the one received. This procedure also re-initialises the F1AP UE-related contexts (if any) and erases all related signalling connections in the two nodes like a Reset procedure would do. “

Lenovo proposed text –

The purpose of the F1 Setup procedure is to exchange application level data needed for the gNB-DU and the gNB-CU to correctly interoperate on the F1 interface instance’.

Let have a second round of discussion on the proposed text changes from Radisys and Lenovo

According to [1] for F1 removal procedure the terms “removal of interface instance” and “removal of signaling connection” are used interchangeably in the textual description of F1 Removal. Based on understanding from X2AP and XNAP specifications which also supports Shared TNLA, F1 removal means removal of F1-C signaling connection between gNB-DU and gNB-CU.

Also, Transaction ID over F1 interface is re-used to identify a F1-C interface instance along with identifying parallel transactions. This is different as compared to XN and X2 Shared TNLA case, where an Interface Instance Identifier is allocated to identify an interface instance for a Shared TNLA.

## Do you agree that for a Shared TNLA case, F1 Removal procedure is to remove a F1-C signaling connection between gNB-DU and gNB-CU like XNAP Removal and ENDC X2AP Removal and not to remove a particular F1-C interface instance?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Radisys | Yes | F1 Removal procedure removes all the application data for multiple F1-C interface instances over a Shared TNLA. Since Transaction ID is used for dual purposes in F1 interface, when a Transaction ID is passed in F1 Removal, gNB-CU cannot identify a particular F1-C interface instance to be removed, as there is no other accompanying cell related information in the F1 Removal procedure. |
| Ericsson | no | The intended function is that in general it is the interface instance and not the TNLA that is removed. The TNLA is only removed if it is not used anymore by an interface instance. |
| Nokia | No | In our understanding, the intention of this function is to remove only the concerned interface instance, and not the whole shared transport connection. Removing the whole shared transport connection would result in that, removing a single interface instance ends up affecting all other instances, which is not the intended functionality. |
| Samsung | No | We understand such function is intended to remove interface instance rather than the transport connection. |
| ZTE | Yes | In current 8.2.8.2, only the removal of the TNL association is given in the textual description, which is not aligned with the description in 8.2.8.1. Successful F1 Removal, gNB-DU initiated The gNB-DU initiates the procedure by sending the F1 REMOVAL REQUEST message to the gNB-CU. Upon reception of the F1 REMOVAL REQUEST message the gNB-CU shall reply with the F1 REMOVAL RESPONSE message. After receiving the F1 REMOVAL RESPONSE message, the gNB-DU may initiate removal of the TNL association towards the gNB-CU, if applicable, and may remove all resources associated with that signaling connection. The gNB-CU may then remove all resources associated with that interface instance. The purpose of the F1 Removal procedure is to remove the interface instance and all related resources between the gNB-DU and the gNB-CU in a controlled manner. If successful, this procedure erases any existing application level configuration data in the two nodes. Therefore, we propose to align the description with XnAP and X2AP. One issue for the transaction ID is that whether this IE could identify the different interface instance. |
| Lenovo, Motorola Mobility | Yes | We shared the same view with ZTE. In current 8.2.8.2, it is clearly stated that the TNL association is removed. In the section 8.2.2.1, there is a NOTE NOTE: In case the signalling transport is shared among several F1-C interface instances, and the TNL association is still used by one or several F1-C interface instances, the initiating node should not initiate the removal of the TNL association. The NOTE also implies that the TNL association is removed bu the F1 Removal procedure. |

## Do you agree to align the F1 Removal textual description similar to X2 and EN-DC X2 Removal procedures?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Radisys | Yes | If not reworded, it causes Interop issues. |
| Ericsson | No | It seems that there are indeed some updates necessary. If we do anything, we should rather correct all TSs, where applicable, as outlined in our answer to Q3.3. |
| Nokia | No |  |
| Samsung |  | Some rewording may be needed. For example, in TS38.473, we have “After receiving the F1 REMOVAL RESPONSE message, the gNB-DU may initiate removal of the TNL association towards the gNB-CU, if applicable, and may remove all resources associated with that signaling connection. The gNB-CU may then remove all resources associated with that interface instance”. We guess the two highlighted parts are actucally referring to interface instance. |
| ZTE | Yes | It is reasonable to align with the other interfaces |
| Lenovo, Motorola Mobility | Yes | We need to align the spec to avoid confusion. Some places the signalling connection is used which in other places interface instance is used. |

Summary:

5 companies think some updates are needed in F1 Removal procedural text.

1 company think no update is needed.

Based on the discussion, it is not clear if F1 removal procedure is to remove a F1-C interface instance or a signaling connection (i.e TNLA).

From 38.473 Clause 8.2.8.1

“NOTE:	In case the signalling transport is shared among several F1-C interface instances, and the TNL association is still used by one or several F1-C interface instances, the initiating node should not initiate the removal of the TNL association.”

“After receiving the F1 REMOVAL RESPONSE message, the gNB-DU may initiate removal of the TNL association towards the gNB-CU, if applicable, and may remove all resources associated with that signaling connection.”

From the above statements, it shows that F1 Removal is to remove a TNL association and not a particular F1-C interface instance.

This understanding also aligns with Xn Removal and X2 removal as shown below –

38.423 Clause 8.4.6.1

“ The purpose of the Xn Removal procedure is to remove the signaling connection between two NG-RAN nodes in a controlled manner “

36.423 Clause 8.3.14.1

“ The purpose of the Xn Removal procedure is to remove the signaling connection between two NG-RAN nodes in a controlled manner “

Moderator’s Proposal 2: Second round of discussion is needed to understand the purpose of F1, Xn, and EN-DC X2 Removal for Shared and Non-Shared TNLA case.

# Conclusion, Recommendations [if needed]

If needed

# References

R3-214761, Clarification on F1 Setup-Removal Procedure for RAN Sharing	discussion

R3-214762, Correction on F1 Setup-Removal Procedure for RAN Sharing in Rel-15	Rel15 CR

R3-214795, Correction on F1 Setup-Removal Procedure for RAN Sharing in Rel-16	Rel16 CR

# Annex A (input from Ericsson): suggested changes to various TSs:

## A.1 F1AP

### 8.2.8	F1 Removal

#### 8.2.8.1	General

The purpose of the F1 Removal procedure is to remove the interface instance and all related resources between the gNB-DU and the gNB-CU in a controlled manner. If successful, this procedure erases any existing application level configuration data in the two nodes.

NOTE:	In case the signalling transport is shared among several F1-C interface instances, and the TNL association is still used by one or several F1-C interface instances, the initiating node should not initiate the removal of the TNL association.

The procedure uses non-UE-associated signaling.

#### 8.2.8.2	Successful Operation

Figure 8.2.8-1: F1 Removal, gNB-DU initiated, successful operation

Figure 8.2.8.2-2: F1 Removal, gNB-CU initiated, successful operation

Successful F1 Removal, gNB-DU initiated

The gNB-DU initiates the procedure by sending the F1 REMOVAL REQUEST message to the gNB-CU. Upon reception of the F1 REMOVAL REQUEST message the gNB-CU shall reply with the F1 REMOVAL RESPONSE message. After receiving the F1 REMOVAL RESPONSE message, the gNB-DU may initiate removal of the TNL association towards the gNB-CU, if applicable, and may remove all resources associated with that interface instance. The gNB-CU may then remove all resources associated with that interface instance.

Successful F1 Removal, gNB-CU initiated

The gNB-CU initiates the procedure by sending the F1 REMOVAL REQUEST message to the gNB-DU. Upon reception of the F1 REMOVAL REQUEST message the gNB-DU shall reply with the F1 REMOVAL RESPONSE message. After receiving the F1 REMOVAL RESPONSE message, the gNB-CU may initiate removal of the TNL association towards the gNB-DU, if applicable, and may remove all resources associated with that interface instance. The gNB-DU may then remove all resources associated with that interface instance.

#### 8.2.8.3	Unsuccessful Operation

Figure 8.2.8.3-1: F1 Removal, gNB-DU initiated, unsuccessful operation

Figure 8.2.8.3-2: F1 Removal, gNB-CU initiated, unsuccessful operation

Unsuccessful F1 Removal, gNB-DU initiated

If the gNB-CU cannot accept to remove the interface instance with the gNB-DU it shall respond with an F1 REMOVAL FAILURE message with an appropriate cause value.

Unsuccessful F1 Removal, gNB-CU initiated

If the gNB-DU cannot accept to remove the interface instance with the gNB-CU it shall respond with an F1 REMOVAL FAILURE message with an appropriate cause value.

#### 8.2.8.4	Abnormal Conditions

Not applicable.

## A.2 XnAP

### 8.4.6	Xn Removal

#### 8.4.6.1	General

The purpose of the Xn Removal procedure is to remove the interface instance between two NG-RAN nodes in a controlled manner. If successful, this procedure erases any existing application level configuration data in the two nodes.

NOTE:	In case the signalling transport is shared among several Xn-C interface instances, and the TNL association is still used by one or more Xn-C interface instances, the initiating NG-RAN node should not initiate the removal of the TNL association.

The procedure uses non UE-associated signaling.

#### 8.4.6.2	Successful Operation

Figure 8.4.6.2-1: Xn Removal, successful operation

An NG-RAN node1 initiates the procedure by sending the XN REMOVAL REQUEST message to a candidate NG-RAN node2. Upon reception of the XN REMOVAL REQUEST message the candidate NG-RAN node2 shall reply with the XN REMOVAL RESPONSE message. After receiving the XN REMOVAL RESPONSE message, the initiating NG-RAN node1 shall initiate removal of the TNL association towards NG-RAN node2 and may remove all resources associated with that interface instance. The candidate NG-RAN node2 may then remove all resources associated with that interface instance.

If the Xn Removal Threshold IE is included in the XN REMOVAL REQUEST message, the candidate NG-RAN node2 shall, if supported, accept to remove the interface instance with NG-RAN node1 if the Xn Benefit Value of the interface instance determined at the candidate NG-RAN node2 is lower than the value of the Xn Removal Threshold IE.

If case of network sharing with multiple cell ID broadcast with shared Xn-C signalling transport, as specified in TS 38.300 [9], the XN REMOVAL REQUEST message and the XN REMOVAL RESPONSE message shall include the Interface Instance Indication IE to identify the corresponding interface instance.

#### 8.4.6.3	Unsuccessful Operation

Figure 8.4.6.3-1: Xn Removal, unsuccessful operation

If the candidate NG-RAN node2 cannot accept to remove the interface instance with NG-RAN node1 it shall respond with an XN REMOVAL FAILURE message with an appropriate cause value.

If case of network sharing with multiple cell ID broadcast with shared Xn-C signalling transport, as specified in TS 38.300 [9], the XN REMOVAL REQUEST message and the XN REMOVAL FAILURE message shall include the Interface Instance Indication IE to identify the corresponding interface instance.

#### 8.4.6.4	Abnormal Conditions

Void.

## A.3 X2AP

### 8.3.14	EN-DC X2 Removal

#### 8.3.14.1	General

The purpose of the EN-DC X2 Removal procedure is to remove the interface instance between eNB and en-gNB in a controlled manner. If successful, this procedure erases any existing application level configuration data in the two nodes.

NOTE:	In case the signalling transport is shared among several X2-C interface instances, and the TNL association is still used by one or more X2-C interface instances, the initiating node should not initiate the removal of the TNL association.

The procedure uses non UE-associated signaling.

#### 8.3.14.2	Successful Operation

Figure 8.3.14.2-1: eNB Initiated EN-DC X2 Removal, successful operation

Figure 8.3.14.2-2: en-gNB Initiated EN-DC X2 Removal, successful operation

If case of network sharing with multiple cell ID broadcast with shared X2-C signalling transport, as specified in TS 36.300 [15], the EN-DC X2 REMOVAL REQUEST message and the EN-DC X2 REMOVAL RESPONSE message shall include the Interface Instance Indication IE to identify the corresponding interface instance.

eNB initiated EN-DC X2 Removal:

An eNB initiates the procedure by sending the EN-DC X2 REMOVAL REQUEST message to a candidate en-gNB. Upon reception of the EN-DC X2 REMOVAL REQUEST message the candidate en-gNB shall reply with the EN-DC X2 REMOVAL RESPONSE message. After receiving the EN-DC X2 REMOVAL RESPONSE message, the initiating eNB shall initiate removal of the TNL association towards en-gNB and may remove all resources associated with that interface instance. The candidate eNB may then remove all resources associated with that interface instance.

If the X2 Removal Threshold IE is included in the EN-DC X2 REMOVAL REQUEST message, the candidate en-gNB shall, if supported, accept to remove the interface instance with eNB if the X2 Benefit Value of the interface instance determined at the candidate en-gNB is lower than the value of the X2 Removal Threshold IE.

en-gNB initiated EN-DC X2 Removal:

An en-gNB initiates the procedure by sending the EN-DC X2 REMOVAL REQUEST message to a candidate eNB. Upon reception of the EN-DC X2 REMOVAL REQUEST message the candidate eNB shall reply with the EN-DC X2 REMOVAL RESPONSE message. After receiving the EN-DC X2 REMOVAL RESPONSE message, the initiating en-gNB shall initiate removal of the TNL association towards eNB and may remove all resources associated with that interface instance. The candidate eNB may then remove all resources associated with that interface instance.

If the X2 Removal Threshold IE is included in the EN-DC X2 REMOVAL REQUEST message, the candidate eNB shall, if supported, accept to remove the interface instance with en-gNB if the X2 Benefit Value of the interface instance determined at the candidate eNB is lower than the value of the X2 Removal Threshold IE.

#### 8.3.14.3	Unsuccessful Operation

Figure 8.3.14.3-1: eNB Initiated EN-DC X2 Removal, unsuccessful operation

Figure 8.3.14.3-2: en-gNB Initiated EN-DC X2 Removal, unsuccessful operation

If the candidate receiving node cannot accept to remove the interface instance with initiating node it shall respond with an EN-DC X2 REMOVAL FAILURE message with an appropriate cause value.

If case of network sharing with multiple cell ID broadcast with shared X2-C signalling transport, as specified in TS 36.300 [15], the EN-DC X2 REMOVAL REQUEST message and the EN-DC X2 REMOVAL FAILURE message shall include the Interface Instance Indication IE to identify the corresponding interface instance.

#### 8.3.14.4	Abnormal Conditions

Void.

# Text boxes

9.2.1.16	   F1 REMOVAL REQUEST

This message is sent by either the gNB-DU or the gNB-CU to intiate the removal of the interface instance and the related resources.

Direction: gNB-DU ( gNB-CU, gNB-CU ( gNB-DU.

| IE/Group Name | Presence | Range | IE type and reference | Semantics description | Criticality | Assigned Criticality |
| --- | --- | --- | --- | --- | --- | --- |
| Message Type | M |  | 9.3.1.1 |  | YES | reject |
| Transaction ID | M |  | 9.3.1.23 |  | YES | reject |