3GPP TSG-RAN WG3 #114-e								   										   R3-21xxxx

01-11 Nov 2021

Online

| CR-Form-v12.1 |
| --- |
| CHANGE REQUEST |
|  | 38.473 | CR | 0805 | rev | 1 | Current version: | 15.15.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network | x | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Correction on F1 Removal for RAN Sharing in Rel-15 |
| --- | --- |
| Source to WG: | Radisys, Reliance JIO, ZTE, Lenovo, Motorola Mobility, Ericsson |
| Source to TSG: | R3 |
| Work item code: | NR_newRAT-Core |  | Date: | 2021-10-10 |
| Category: | F |  | Release: | Rel-15 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) … Rel-15 (Release 15) Rel-16 (Release 16) Rel-17 (Release 17) Rel-18 (Release 18) |
| Reason for change: | The intent of F1 Removal procedure is to remove a F1 Interface Instance for both Shared and Non-Shared TNLA case. Hence the misleading term “signaling connection” in the F1 Removal procedural text shall be replaced with “Interface Instance” to address both Shared and Non-Shared TNLA case. |
| Summary of change: | Replace the “signaling connection” by “interface instance” in text description of the F1 Removal procedure. Impact analysis: Impact assessment towards the previous version of the specification (same release): This CR has impact from functional point of view. The impact can be considered isolated because it only modifies the text descriptions for F1 Removal procedure for RAN sharing. There is no ASN.1 impact. |
| Consequences if not approved: | The usage of F1 Removal procedure for RAN Sharing will not be clear. |
| Clauses affected: | 8.2.8.2; 8.2.8.3 |
|  | Y | N |  |  |
| Other specs |  | x | Other core specifications | TS/TR ... CR ... |
| affected: |  | x | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | x | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: | Rev1: Revision of R3-214762, add Ericsson as the co-signer |

Start of change

#### 8.2.8.2	Successful Operation

Figure 8.2.8-1: F1 Removal, gNB-DU initiated, successful operation

Figure 8.2.8.2-2: F1 Removal, gNB-CU initiated, successful operation

Successful F1 Removal, gNB-DU initiated

The gNB-DU initiates the procedure by sending the F1 REMOVAL REQUEST message to the gNB-CU. Upon reception of the F1 REMOVAL REQUEST message the gNB-CU shall reply with the F1 REMOVAL RESPONSE message. After receiving the F1 REMOVAL RESPONSE message, the gNB-DU may initiate removal of the TNL association towards the gNB-CU, if applicable, and may remove all resources associated with that interface instance. The gNB-CU may then remove all resources associated with that interface instance.

Successful F1 Removal, gNB-CU initiated

The gNB-CU initiates the procedure by sending the F1 REMOVAL REQUEST message to the gNB-DU. Upon reception of the F1 REMOVAL REQUEST message the gNB-DU shall reply with the F1 REMOVAL RESPONSE message. After receiving the F1 REMOVAL RESPONSE message, the gNB-CU may initiate removal of the TNL association towards the gNB-DU, if applicable, and may remove all resources associated with that interface instance. The gNB-DU may then remove all resources associated with that interface instance.

#### 8.2.8.3	Unsuccessful Operation

Figure 8.2.8.3-1: F1 Removal, gNB-DU initiated, unsuccessful operation

Figure 8.2.8.3-2: F1 Removal, gNB-CU initiated, unsuccessful operation

Unsuccessful F1 Removal, gNB-DU initiated

If the gNB-CU cannot accept to remove the interface instance with the gNB-DU it shall respond with an F1 REMOVAL FAILURE message with an appropriate cause value.

Unsuccessful F1 Removal, gNB-CU initiated

If the gNB-DU cannot accept to remove the interface instance with the gNB-CU it shall respond with an F1 REMOVAL FAILURE message with an appropriate cause value.

End of change