3GPP TSG-RAN WG3 #114-e	R3-215948

Online, 01 – 11 Nov, 2021

Agenda Item:	31.2.6

Source:	Ericsson (moderator)

Title:	Summary of Offline Discussion on PWS Test Flag

Document for:	Approval

# Introduction

CB: # 114_PWSTest

- Whether the requirements in CT1 is clear enough to trigger the solution discussion in NG-RAN?

- Capture agreements if any

- If no consensus, no further discussion in RAN3 without any LS from other groups

(Ericsson - moderator)

Summary of offline disc R3-215948

# For the Chairman’s Notes

//to be added

# Discussion

In RAN3-114e recent agreements made in CT1 were discussed.

The following conclusions were analysed from the discussion paper in [1]:

[quote] …. CT1 made recent agreements to introduce a new “Test Flag” as part of the WRITE-REPLACE-WARNING-REQUEST and WRITE-REPLACE-WARNING-REQUEST-NG-RAN messages that the CBC/CBCF may send to the AMF. The purpose is to enable “to indicate to the NG-RAN node that the request is to be processed and responded to normally, but shall not result in broadcast over the air and shall not allocate any resources (i.e. the request cannot be cancelled)”.

In order to align RAN3 specifications with CT1 specifications additions need to be made over the NGAP and the F1AP. [unquote]

For convenience, an excerpt from TS23041, capturing the agreed introduction of the Test Flag is reported below:

----------------------------Excerpt from TS23.041----------------------------

### 9.2.16	WRITE-REPLACE-WARNING-REQUEST Request/Indication

| PARAMETER | REFERENCE | PRESENCE |
| --- | --- | --- |
| Message Type | 9.3.28 | M |
| Message Identifier | 9.3.1 | M |
| Serial-Number | 9.3.3 | M |
| Repetition-Period E-UTRAN | 9.3.36 | M |
| No-of-Broadcasts-Requested | 9.3.9 | M |
| List of TAIs | 9.3.29 | O |
| Warning Area List | 9.3.30 | O |
| Extended Repetition-Period | 9.3.37 | O |
| Warning-Type | 9.3.24 | O |
| Warning-Security-Information | 9.3.25 | O |
| Data Coding Scheme | 9.3.18 | O (NOTE 1) |
| Warning Message Content E-UTRAN | 9.3.35 | O |
| OMC ID | 9.3.31 | O |
| Concurrent Warning Message Indicator | 9.3.32 | O |
| Send Write-Replace-Warning-Indication | 9.3.39 | O |
| Global eNB ID | 9.3.46 | O |
| List of NG-RAN TAIs | 9.3.54 | O |
| Warning Area List NG-RAN | 9.3.55 | O |
| Warning Message Content NG-RAN | 9.3.51 | O |
| Global RAN Node ID | 9.3.53 | O |
| RAT Selector NG-RAN | 9.3.56 | O |
| Warning Area Coordinates | 9.3.63 | O |
| Test Flag | 9.3.64 | O (NOTE 2) |
| NOTE1: The Data Coding Scheme IE is not required for ETWS primary notification but it is mandatory for ETWS secondary notification and CMAS warning messages when Warning Message Content E-UTRAN IE is present. NOTE 2: This IE may only be included if the CBC sends the request to a PWS-IWF. |

### 9.2.26	WRITE-REPLACE-WARNING-REQUEST-NG-RAN Request/Indication

| PARAMETER | REFERENCE | PRESENCE |
| --- | --- | --- |
| Message Type | 9.3.28 | M |
| Message Identifier | 9.3.1 | M |
| Serial-Number | 9.3.3 | M |
| Repetition-Period NG-RAN | 9.3.52 | M |
| No-of-Broadcasts-Requested | 9.3.9 | M |
| RAT Selector NG-RAN | 9.3.56 | M |
| List of NG-RAN TAIs | 9.3.54 | O |
| Warning Area List NG-RAN | 9.3.55 | O |
| Warning-Type | 9.3.24 | O |
| Warning-Security-Information | 9.3.25 | O |
| Data Coding Scheme | 9.3.18 | O (NOTE) |
| Warning Message Content NG-RAN | 9.3.51 | O |
| OMC ID | 9.3.31 | O |
| Concurrent Warning Message Indicator | 9.3.32 | O |
| Send Write-Replace-Warning-Indication | 9.3.39 | O |
| Global RAN Node ID | 9.3.53 | O |
| Warning Area Coordinates | 9.3.63 | O |
| Test Flag | 9.3.64 | O |
| NOTE: The Data Coding Scheme IE is not required for ETWS primary notification but it is mandatory for ETWS secondary notification and CMAS warning messages when Warning Message Content NG-RAN IE is present. |

----------------------------End of Excerpt from TS23.041----------------------------

In TS23.041 the Test Flag is defined as follows:

----------------------------Excerpt from TS23.041----------------------------

### 9.3.64	Test Flag

The Test Flag IE may be included to indicate to the NG-RAN node that the request is to be processed and responded to normally, but shall not result in broadcast over the air and shall not allocate any resources (i.e. the request cannot be cancelled).

----------------------------End of Excerpt from TS23.041----------------------------

During the online discussion it was mentioned that:

-	The purpose of the Test Flag is to run a sanity check on the infrastructure that is supposed to transport a PWS message up until the message reaches the over-the-air transmission point, but without broadcasting the message over the air. 
the infrastructure on which the delivery of PWS relies on is defined by different 3GPP WGs. It consists of a signalling route from e.g. CBC to AMF, a signalling route from AMF to RAN and a signalling route within a potentially split RAN. This is why the Test Flag solution was derived from CT1 (at stage 2) as CT1 maintains the overall system view on PWS.

- the advantage of the Test Flag is that such test procedures on the infrastructure do not consume over the air resources nor they imply the UE needs to “wake up” and check the relevant SIBs.

- (Some) operators need the Test Flag capability to check PWS availability (i.e. then need to sanity check the infrastructure supporting PWS message delivery) because their government has imposed requirements on PWS availability, especially if the government pays for the service.

- Without the Test Flag functionality, issues affecting PWS transmission may be discovered only at the time when a PWS message needs to be signalled. The latter causes to miss broadcasting of the affected PWS message, which is, in some countries, not acceptable.

-	The discussion on the usefulness/reason of the added feature should be addressed in CT1, since CT1 agreed the stage 2 CR and subsequently CT approved it and published it in TS 23.041 v17.2.0. RAN3 is asked to implement the stage 3 CRs or to recommend to CT1 clarifications that would make the specifications less ambiguous (if at all needed).

-	The wording of the text in TS23.041 could be improved.

Question 1: Is the stage 2 description in TS 23.041 clear enough? If not, what improvements could be suggested to make it clearer?

| Company | Answer | Comment |
| --- | --- | --- |
| Ericsson | The text is clear | TS23.041 is very clear in specifying the receiver´s behaviour of the Test Flag. It says that the test flag is used “to indicate to the NG-RAN node that the request is to be processed and responded to normally, but shall not result in broadcast over the air and shall not allocate any resources”, hence there seems to be no clear missing parts to this description. Perhaps the text may be improved with a description of what could be deduced at system level if the PWS Write Replace Warning message including the Test Flag fails/succeeds to be delivered. A rewording example could be as follows: The Test Flag IE may be included to indicate to the NG-RAN node that the request is to be processed and responded to normally, but shall not result in broadcast over the air and shall not allocate any resources (i.e. the request cannot be cancelled). If the procedure associated with the Test Flag results into a failure, the management system may use this information to trouble shoot the issue causing the failure and allow for successful future delivery of PWS messages. |

Question 2: Should an LS be sent to CT1 to recommend clarifications to their specification in TS23.041?

| Company | Answer | Comment |
| --- | --- | --- |
| Ericsson | Not necessarily | We do not think there is an immediate need for an LS. However, if RAN3 agrees that the text in TS23.041 needs to be improved an LS can be triggered. |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-215222 Corrections of procedures for PWS tests (Ericsson, one2many, KPN)	Discussion

R3-215921 Addition of Test Flag for PWS  [TEI17_TestFlag] (Ericsson, one2many, KPN)	CR0816, TS 38.473 v16.6.0, Rel-16, Cat. B

R3-215922 Addition of Test Flag [TEI17_TestFlag] (Ericsson, one2many, KPN)	CR0676, TS 38.413 v16.7.0, Rel-16, Cat. B