3GPP TSG-RAN WG3 #114-e	R3-215879

Online, 1-11 November 2021

Agenda Item:	19.3

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on CB: # 1904_Pos_LatencyImprovement

Document for:	Approval

# Introduction

CB: # 1904_Pos_LatencyImprovement - Any other enhancements for latency improvements? (HW - moderator) Summary of offline disc R3-215879

It is propose to the response time IE where [1] and  [2] have different view and check other proposal

Please provide your feedback by 4th Friday afternoon 14h00 UTC, pending to responses, the moderator will propose a resolution by online session of 8th Monday.

# For the Chairman’s Notes [TBC]

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion [if needed]

## Time T delivery

In [2] it is propose that, Time T does not need to be delivered to RAN or UE. It can be sent during LCS procedures. This is up to SA2.

Q3-1-1: The companies are invited to express view on proposal, and clarify RAN3 impact if any.

| Company | Comment |
| --- | --- |
| Huawei | We are fine with the proposal |
| Qualcomm | What does the proposal mean (see the highlight)? That the proponents propose to send T using LPP or NRPPa? We can discuss further. A measurement time T can be used to allow measurements close to the time T. The whole purpose is to have all measurements performed near to T. |
| Ericsson | Fine with the proposal. LCS signalling is outside of RAN3 scope. |

## Response time encoding

They are several proposal on encoding the Response time IE.

In [1], it is propose to set the value of the Time IE to be integer from 1 to 128 and the Time Unit IE can have multiple choice including ten-seconds, seconds and ten-milli-seconds

In [2] it is propose to include in the Response time some simple positioning latency and accuracy metrics to gNB. The periodicity existing in NRPPa can be re-used.

Q3-2-1: The companies are invited to express view on proposal, whether on encoding is preferred or merged of the 2 proposals, etc...

| Company | Comment |
| --- | --- |
| Huawei | We have preference for LPP like encoding. The gNB may not be able to well interpret what does the “no delay” or “delay tolerant” (coded in [2]) mean, i.e., how long the gNB could take for measurements before responding to the LMF. Similarly, the gNB may not well interpret the accuracy coding in [2]. The other way may be to include the value of the accuracy. In this case, however, The accuracy metrics seems to restrict the gNB, i.e., the gNB should be able to try the best and would not fail if the accuracy is not satisfied. |
| Qualcomm | The proposals in [2] do not seem to help with the purpose, which is to ensure that measurements are performed within a certain time window. The LMF will have no idea when to expect the response. We can start with [1] even if exact values can be fine-tuned [FFS etc] |
| Ericsson | We can follow majority to leave the exact values FFS in [1]. But in our view, NRPPa should have a finer reporting than LPP to meet the QoS guarantee. (Btw, good to have a time unit IE, so that there won’t be a late correction clarifying what the time unit is 😉) |

## Correction in procedural text clause 8.5.1.2

In [1] it is propose to use “shall, if supported” in the procedural text in clause 8.5.1.2.

Q3-3-1: The companies are invited to express view on proposal, should it be agreed?

| Company | Comment |
| --- | --- |
| Huawei | Yes |
| Qualcomm | Yes |
| Ericsson | We don’t think that a “shall, if supported” can really reflect the gNB ability to meet the response time requested by LMF. As per our paper [2] analysis, it depends on factors outside 3GPP, like the transport network capacity/latency, collocation of RAN/CN, etc., that procedural text cannot describe. |

## Measurement Amount

In [1] it is propose to include a Measurement Amount IE along with the Measurement Periodicity IE in the NRPPa Measurement Request message for the case of periodic reporting is required.

Q3-4-1: The companies are invited to express view on proposal, should it be agreed?

| Company | Comment |
| --- | --- |
| Huawei | Yes |
| Qualcomm | Sorry, but this seems out of scope of this WI / AI ?? |
| Ericsson | Yes, this addresses our comment from last time. |

# Conclusion, Recommendations [TBC]

If needed

# References

R3-215393, (TP for POS BL CR for TS 38.455, TS 38.473): Latency improvement in positioning (Huawei)

R3-215441, Discussion on latency improvements for Rel-17 positioning (Ericsson)