3GPP RAN3 #114-e	R3-215822

1st November – 11th November 2021

Online

Agenda Item:	8.3.4

Source:	Ericsson

Title:	SoD_CB: # 19_MDTReportAmount

Document for:	Discussion, Decision

# Introduction

CB: # 19_MDTReportAmount

- SA5 confirms that reportAmount is beneficial to configure for MDT measurements M4, M5, M6 and M7 in R3-214722.

- Apply to NR only or both LTE and NR?

- Check details and provide stage2/3 CRs/TPs, split the work, if needed

(E/// - moderator)

Summary of offline disc R3-215822

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

In [3] RAN3 sent an LS to RAN2 and SA5 to ask whether it is beneficial to introduce the Report Amount as part of the M4, M5, M6, M7 measurement configurations.

RAN3 received reply LSs on the inclusion of the Measured Amount for the MDT measurements M4, M5, M6, M7, see [1]-[2].

In [2] RAN2 confirmed that reportAmount is necessary to configure the UE with D1 measurement (part of M6 measurement) reports from the UE. RAN2 left discussions on M4, M5, M7 to SA5.

In [1] SA5 confirms that reportAmount is beneficial to configure for MDT measurements M4, M5, M6 and M7.

A number of contributions were submitted to RAN3-114e to identify solutions for the introduction of a Report Amount for the MDT measurements M4, M5, M6, M7. Some companies submitted CRs for NR and some others for both E-UTRAN and NG-RAN.

## Agreement on the introduction of the Report Amount IE for the M4, M5, M6, M7 measurements configurations

All the contributions submitted at RAN3-114e propose to agree to the introduction of the Report Amount IE for the M4, M5, M6, M7 measurements configurations.

However, some companies proposed to support the inclusion of the new IE for both E-UTRAN and NG-RAN, while some other companies proposed support only for the NG-RAN.

The original LS sent by RAN3 in [3] asked to RAN2 and SA5 about the benefits of introducing the Report Amount for both E-UTRAN and NG-RAN, namely the LS did not specify that the enhancement was only for one system.

The replies received form RAN2 and SA5 are not targeting a specific system either.

Companies are invited to provide their view on the following:

Is the introduction of the Report Amount IE as part of the M4, M5, M6, M7 measurement configurations beneficial for both E-UTRAN and NG-RAN?

| Company | Comment |
| --- | --- |
| Ericsson | Yes, as confirmed by the reply LSs from RAN2 and SA5, the enhancement is beneficial independently of the system. Namely, the issues of not having the Report Amount for M4, M5, M6, M7 are present in both E-UTRAN and NG-RAN. |
| Huawei | Disagree. In the original LS from RAN3, it clearly said that: Release: Rel-17 Work Item: NR_ENDC_SON_MDT_enh-Core It implies that the replies from RAN2 and SA5 are made in the scope of rel-17. Therefore, we would like to keep the changes within NG-RAN as part of the rel-17 WI. |
| ZTE | Disagree. The MDT for LTE has been commercial for more than ten years and become late cycle of the produce, we don’t see much benefit to introduce Report amount in LTE. |

Can RAN3 agree to the introduction of the Report Amount IE as part of the M4, M5, M6, M7 measurement configurations for both E-UTRAN and NG-RAN?

| Company | Comment |
| --- | --- |
| Ericsson | Yes. The new IE is optional and backwards compatible, hence even the E-UTRAN system can support it with no impact on legacy. The new IE is beneficial as already confirmed in the LSs from RAN2 and SA5 |
| Huawei | We support only to introduce it in NG-RAN as part of the SONMDT rel-17 WI. |
| ZTE | We only support to introduce in NG-RAN for Rel-17. |

## Inclusion of the “Infinity” value

In [4] it is proposed that the newly added Report Amount IE should not support value “Infinity”. Such value could be derived by absence of the IE.

Companies are invited to provide their views on whether to include value “Infinity” or whether not to include it and to interpret absence of the Report Amount IE as “report to Infinity”

| Company | Comment |
| --- | --- |
| Ericsson | We support not to include “Infinity” and to support absence of the Report Amount IE as “Report to Infinity”. As it was confirmed in the LS from RAN3 in [3], in absence of the Report Amount IE measurements will be collected to “Infinity”. It is therefore good to continue with this assumption and to interpret absence of the Report Amount IE as report to infinity. Hence the value “Infinity” is not needed. |
| Huawei | We propose to keep alignment as M1. If we don’t include the infinity value. It may cause misunderstanding, for example, some may think that there is no any report amount at all from CN/OAM, and may decide a value arbitrary which seems unexpected. |
| ZTE | We support to keep infinite as it is. To support absent of “infinite” is actually a new function for NG-RAN, an old NG-RAN have to update to support it. We don’t think it is necessary to introduce this enhancement. |

## Value Range for the Report Amount in M4, M5, M6, M7

In [5] it is explained that measurements M5, M6, M7 are for RRM purposes and for that they should have an extended value range with respect to M1 and M4.

For this [5] proposes to give to the M4 Report Amount IE the value range ENUMERATED (1, 2, 4, 8, 16, 32, 64, infinity), while to give to the M5/M6/M7 Report Amount IE the value range ENUMERATED (1, 2, 4, 8, 16, 32, 64, 128, 256,512,1024,2048, infinity)

Companies are invited to provide their views on whether the Report Amount IE should have different value ranges for the M5/M6/M7 measurements and for the M4 measurement.

| Company | Comment |
| --- | --- |
| Ericsson | We do not see the need for such differentiation. Keeping a single range of Report Amount values simplifies the implementation. |
| Huawei | Agree with E///’s comments above. Don’t see any strong need to differentiate the value among MDT measurements. |
| ZTE | We see the different value range is needed. The original report amount is considered based on UE but not for Network entity, it is not necessary to align the report amount between NG-RAN node and UE. In addition, M5/M6/M7 are enforced in the network and NG-RAN node does not worry about power saving. And more report amount is possible and beneficial. |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-214722, Reply LS on Report Amount for M4, M5, M6, M7 measurements (SA5)

R3-214335, Reply LS on Report Amount for M4, M5, M6, M7 measurements (RAN2)

R3-212961, LS on Report Amount for M4, M5, M6, M7 measurements (RAN3)

R3-214502, Discussion on the introduction of the Report Amount in MDT Measurements (Ericsson)

R3-215732, Report Amount for M4, M5, M6, M7 measurements (ZTE)