3GPP TSG-RAN WG3 #114-e			draft Tdoc R3-215992

Online, 1-11 November 2021

Title:	[DRAFT] Reply LS on Guidelines on Port Allocation for New 3GPP Interfaces

Response to:	LS (R3-214671) on Guidelines on Port Allocation for New 3GPP Interfaces from CT4

Release:	Rel-17

Source:	Ericsson [to become RAN3]

To:	CT4

Cc:	RAN2, SA4, CT3, SA5, SA2, SA, CT, RAN

Contact Person:

#### Name:	Gino Masini

E-mail Address:	gino.masini@ericsson.com

Send any reply LS to:	3GPP Liaisons Coordinator, 3GPPLiaison@etsi.org

1. Overall Description:

RAN3 thanks CT4 for the latest information and status report on the port number allocation solutions.

Solutions #1-4, 8 all have varying impacts on implementations and/or deployments, and have dependencies on the operator's infrastructure, including transport infrastructure. In general, they are not considered feasible.

Solutions #3, 5 which affect the transport network layer, including SCTP, are also unfeasible. RAN3 prefers not to impact transport layer implementations, given that SCTP is today the basis for all RAN3-defined interfaces.

We acknowledge the possible drawback of Solution #6, as described in Sec. 4.4.3 of TR 29.941. RAN3  understands that implementations are responsible for resolving any collisions. We would ask CT4 to keep us informed of any updates on this.

RAN3 confirms that static port number allocation by 3GPP (Solution #6 in TR 29.941) and port allocation via OAM (Solution #7 in TR 29.941) shall be the favored way forward. There is a strong preference in RAN3 to avoid requests to IANA, adopting the above 2 solutions for the foreseeable future.

2. Actions:

To CT4 group.

ACTION: 	RAN3 asks CT4 group to take the above into account, to keep us informed of any updates, and to make the necessary provisions to make Solutions #6 and #7 in TR 29.941 possible. We encourage CT4 to complete the definition of the acceptance criteria, resolving the corresponding FFS and Editor’s Note in the assignment procedure (TR 29.941 Annex D, Sec. D.2). We would also ask CT4 the following:

- Confirm that, once agreed by CT4 and documented in Table D.3-1 of TR 29.941, port allocation shall be normative.

Note: In RAN3 it was suggested that a web page maintained by MCC would be more appropriate for this.

- Considering the port assignment procedure for Sol. #6 (TR 29.941 Annex D, Sec. D.2), clarify whether the WG requesting a new port is expected to address IANA first, before addressing CT4. If so, considering past experiences with IANA, it might be beneficial to document this procedure in an informative way, as a reference. [NB: this is pending resolution in final discussion]

3. Date of Next TSG-RAN3 Meetings:

TSG-RAN3 Meeting #114bis-e	17-26 January 2022				Online

TSG-RAN3 Meeting #115-e	21 February-3 March 2022			Online