3GPP TSG-RAN WG3 #114-e			draft Tdoc R3-21xxxx

Online, 1-11 November 2021

Title:	[DRAFT] Reply LS on Guidelines on Port Allocation for New 3GPP Interfaces

Response to:	LS (R3-214671) on Guidelines on Port Allocation for New 3GPP Interfaces from CT4

Release:	Rel-17

Source:	Ericsson [to become RAN3]

To:	CT4

Cc:	RAN2, SA4, CT3, SA5, SA2, SA, CT, RAN

Contact Person:

#### Name:	Gino Masini

E-mail Address:	gino.masini@ericsson.com

1. Overall Description:

RAN3 thanks CT4 for the latest information and status report on the port number allocation solutions.

Solutions #1-4, 8 all have varying impacts on implementations and/or deployments, and have dependencies on the operator's infrastructure, including transport infrastructure. In general, they are not considered feasible.

Solutions #3, 5 which affect the transport network layer, including SCTP, are also unfeasible. RAN3 prefers not to impact transport layer implementations, given that SCTP is today the basis for all RAN3-defined interfaces.

We acknowledge the possible drawback of Solution #6, as described in Sec. 4.4.3 of TR 29.941. It is understood that implementations are responsible for resolving any collisions.

RAN3 confirms that static port number allocation by 3GPP (Solution #6 in TR 29.941) and port allocation via OAM (Solution #7 in TR 29.941) shall be the favored way forward. There is a strong preference in RAN3 to avoid requests to IANA, adopting the above 2 solutions from now on.

2. Actions:

To CT4 group.

ACTION: 	RAN3 asks CT4 group to take the above into account and to make the necessary provisions to make Solutions #6 and #7 in TR 29.941 possible. We encourage CT4 to complete the definition of the acceptance criteria, resolving the corresponding FFS and Editor’s Note in the assignment procedure (TR 29.941 Annex D, Sec. D.2). We would also ask CT4 the following:

- Confirm that, once agreed by CT4 and documented in Table D.3-1 of TR 29.941, port allocation shall be normative.

- Considering the port assignment procedure for Sol. #6 (TR 29.941 Annex D, Sec. D.2), confirm whether the WG requesting a new port is expected to address IANA first, before addressing CT4. If so, considering recent experiences with IANA, it might be beneficial to specify this in the procedure. [NB: this is pending resolution of Q6 in the 2nd round]

3. Date of Next TSG-RAN3 Meetings:

TSG-RAN3 Meeting #114bis-e	17-26 January 2022				Online

TSG-RAN3 Meeting #115-e	21 February-3 March 2022			Online