3GPP TSG-RAN WG3 #114-e			draft Tdoc R3-216015

Online, 1-11 November 2021

Title:	[DRAFT] Reply LS on UE Location Aspects in NTN

Response to:	LS (R3-214706) on UE location aspects in NTN from SA2

Release:	Rel-17

Work Item:	NR_NTN_solutions

Source:	Ericsson [to become RAN3]

To:	SA2, RAN2

Cc:	CT1

Contact Person:

#### Name:	Gino Masini

E-mail Address:	gino.masini@ericsson.com

1. Overall Description:

RAN3 thanks SA2 for the LS on UE location aspects in NTN.

RAN3 has discussed the options for reporting of TAC in the ULI described by SA2 and can provide the following observations.

Options A1, A2 and C add complexity to the gNB; they are based on UE location information which can be obtained by the gNB from the UE and have no protocol impact.

Option D seems to be the simplest one from RAN point of view, but it may not enable the AMF to discriminate the UE location precisely enough. This is the only option which would signal more than one TAC to the core network, which is not considered desirable by some companies.

Option B would provide additional information to the gNB which might be beneficial to drive e.g. NNSF. Given that this option has UE impact, it seems to require RAN2 discussion.

Combinations (e.g. Opts. C and D, or potentially also option B, if feasible) have also been discussed and appear to have some merit, but no consensus has been reached at this time regarding a RAN3 preferred solution.

RAN3 has also discussed the possibility to signal additional information to the AMF concerning uncertainty/reliability of the reported NR CGI for the UE, and there is no consensus at this time on any such proposal. We would ask SA2 to clarify whether such information is required in the AMF.

2. Actions:

To SA2 and RAN2 groups.

ACTION: 	RAN3 asks SA2 and RAN2 to take the above into account and provide additional feedback, if any.

We would also ask SA2 to clarify whether uncertainty/reliability information for the reported NR CGI for the UE, is required in the AMF.

3. Date of Next TSG-RAN3 Meetings:

TSG-RAN3 Meeting #114bis-e	17-26 January 2022				Online

TSG-RAN3 Meeting #115-e	21 February-3 March 2022			Online