3GPP TSG-RAN WG3 #114-e			draft Tdoc R3-216015

Online, 1-11 November 2021

Title:	[DRAFT] Reply LS on UE Location Aspects in NTN

Response to:	LS (R3-214706) on UE location aspects in NTN from SA2

Release:	Rel-17

Work Item:	NR_NTN_solutions

Source:	Ericsson [to become RAN3]

To:	SA2, RAN2

Cc:	CT1

Contact Person:

#### Name:	Gino Masini

E-mail Address:	gino.masini@ericsson.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

1. Overall Description:

RAN3 thanks SA2 for the LS on UE location aspects in NTN.

RAN3 has discussed the options for reporting of TAC in the ULI described by SA2, but no consensus has been reached at this time regarding a RAN3 preferred solution. RAN3 can provide the following observations.

- Options A1, A2 and C require the gNB to determine the TAC based on UE location information which can be obtained by the gNB from the UE and may reuse current User Location information IE.

- Option D requires the gNB to send all TACs via a new IE to the AMF, but it may not enable the AMF to discriminate the UE location precisely enough.

- Option B would provide additional information to the gNB which might be beneficial to drive e.g. NNSF. Given that this option has UE impact, RAN3 cannot comment on its feasibility, which requires RAN2 discussion.

- Combinations (e.g. Opts. C and D, or potentially also option B, if feasible) have also been discussed and appear to have some merit.

RAN3 has also discussed the possibility to signal additional information to the AMF concerning uncertainty/reliability of the reported NR CGI for the UE. RAN3 cannot determine whether this information is required in the AMF, and would like to ask SA2 to comment on this aspect.

2. Actions:

To SA2 and RAN2 groups.

ACTION: 	RAN3 kindly asks SA2 to take the above into account and provide additional feedback and/or preference regarding the listed options, if any.

RAN3 kindly asks RAN2 to take the above into account and provide feedback on the feasibility of Opt. B, if needed.

RAN3 would also like to ask SA2 to clarify whether uncertainty/reliability information for the reported NR CGI for the UE, is required in the AMF.

3. Date of Next TSG-RAN3 Meetings:

TSG-RAN3 Meeting #114bis-e	17-26 January 2022				Online

TSG-RAN3 Meeting #115-e	21 February-3 March 2022			Online