3GPP TSG-RAN WG3 #114-e							 R3-215882

1-11 November 2021

Online

Agenda Item:	20.2.3

Source:	ZTE (moderator)

Title:	Summary_of_offline_disc_CB # 2003_NTN_Cell_Rel

Document for:	Approval

# Introduction

This contribution is to kick off the following discussion.

CB: # 2003_NTN_Cell_Rel - What is reference use case? Is it based on Xn presence or is it based on OAM? - If based on OAM the topic is out of RAN3 scope - If based on Xn, is there anything needed on top of current Xn functionality? - Capture agreements if any (ZTE - moderator) Summary of offline disc R3-215882

The deadline is Thursday, November 4th, 23:00 UTC.

# For the Chairman’s Notes

[To be added]

# Discussion

## Issue 1: Clarification on the status of Xn in Rel-17

According to [1], the status of Xn should be clarified in RAN3, e.g. do not support Xn in this release, or discuss the RAN2 decision impact, e.g. on CHO mobility, or do not discuss at at Xn etc...

Question: What is your opinion on the status of Xn in Rel-17?

| Company | Comment |
| --- | --- |
| ZTE | According to the agreements in the previous meetings, Xn may exist between 2 gNBs handling NTN, Serving/neighbor NTN cell information, if any, may be exchanged between gNBs via Xn, the Xn has been supported in Rel-17 without any enhancement. |
| Ericsson | No particular showstopper seems to be present here to use Xn in Rel-17 for NTN. In conclusion, we don’t think we should capture any restrictions on using Xn; current agreements are OK. |
| CATT | We could assume the Xn is supported without any enhancement. In case of earth fixed cell deployment, the serving cell and neighbor cell relations are stable, legacy Xn procedures could be reused without any enhancement to exchange the cell information. For Handover case, we could assume the legacy handover procedures could be reused. |

## Issue 1bis: Potential RAN3 impact on Xn based on the RAN2’s progress

According to [1], RAN2 has spent time on the optimized Xn handover operation, i.e. time based CHO.

Question: Whether RAN3 should also discuss the impact of CHO on Xn?

| Company | Comment |
| --- | --- |
| ZTE | No, there is no LS or information from RAN2 to indicate the discussion of CHO issue over Xn in RAN3. |
| Ericsson | CHO as agreed by RAN2 relies on Xn being set up between source and target, and current NTN agreements in RAN3 do not preclude this. It is true that due to the peculiar nature of NTN transparent architecture, setting up Xn between two NTN gNBs does not automatically make them “neighbors” in a TN sense, however once Xn is set up (and it could be set up even “statically”, by OAM), CHO is possible. No problem here. |
| CATT | No, pending to RAN2. CHO is under discussion of RAN2, and there’s no RAN3 impact is identified. RAN3 could work on that if any RAN3 impact is identified by RAN2. |

## Issue 2: Any enhancement over Xn on cell relation in Rel-17?

In [2], as the potential issue, i.e. periodic configuration update on Xn could be solved by the OAM and Rel-17 is the first release for NTN, there is no need to introduce the enhancement on cell relation over Xn in this release.

Question: Whether the enhancement on cell relation over Xn is needed in Rel-17?

| Company | Comment |
| --- | --- |
| ZTE | No, as there is no explicit use case on cell relation with impact over Xn so far, it is no need to introduce any enhancement over Xn on cell relation in this release. |
| Ericsson | No. It was already clarified that LEO orbits are predictable and periodic, hence there is no need for signaling enhancements. Once the network knows the periodicity(ies) involved, that is sufficient information to make the relevant mechanisms work, if an implementation so desires. So, not even a periodic “configuration update” via OAM is needed. |
| CATT | No, the cell relations are predictable, OAM based solution should be sufficient. |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-215101	no support of Xn interface	             Huawei

R3-215740	Further Discussion on Cell Relation for NTN  	ZTE