3GPP TSG-RAN WG3 #114-e	R3-215824

1 – 11 Nov 2021

Agenda Item:	31.2.2

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on _DirectDataFwd_E1aspects

Document for:	Approval

# Introduction

CB: # 21_DirectDataFwd_E1aspects

- For Non-shared case: Sol3: Nok, CATT, China Telecom Sol1: Huawei, Samsung, China Telecom, E///, LGU+

- Allocation of TNL addresses for intra-system direct forwarding: NGAP and E1AP impact

- Capture agreements and provide CRs if agreeable

(HW - moderator)

Summary of offline disc R3-215824

(HW - moderator)

Summary of offline disc R3-215838

# For the Chairman’s Notes

Propose to agree the following:

Proposal 1: TBD.

Proposal 1: TBD.

# Discussion – First round

## Direct data forwarding indication for intra-5GS handover

Last RAN3#113-e meeting agreed to support direct data forwarding indication for intra-5GS system handover, as follows.

- Support the direct forwarding indication with the intra-NR system case, upon SA2 agreements if any impact on SA2 identified

### NG impact

As observed from the contributions, there are two options to indicate the direct forwarding path availability indicator.

- Option 1: Source RAN node informs directly the target NG-RAN node by including the direct forwarding path available in Source to Target container, as proposed in R3-215363

- Option 2: SMF informs the target NG-RAN node in the Handover request message, as proposed in R3-215670

All contributions think both options could work. In R3-214772, it is proposed that from TS 23.502 because when source RAN node indicates direct forwarding path available, there is no reason for SMF to do indirect forwarding instead

The proponent of option 1 thinks this is simple, and has much less impact on SA2 compared with option 2.

The proponent of option 2 thinks that there have backward compatibility issue for option 1 due to the difference release of node.

- However, there can be a backward compatibility issue with option 1 where the SMF is release 15 and RAN node is release 16. In that case the SMF would apply indirect forwarding, even though source RAN node would indicate direct path available to target RAN node.

- Option 1 would result in target RAN node allocating an IP address from the direct forwarding pool instead of the indirect forwarding pool in the above case.

For reference, the moderator observes that from section 4.9.1.3.2 of TS 23.502, currently the SMF will not provide the Direct Forwarding Path Availability to the NG-RAN node at step 9. This means that for option 2, SA2 specification update is needed.

Moderator observation: Currently for intra-5GS system NG based handover, the SMF will not provide the Direct Forwarding Path Availability to the target NG-RAN node in the Handover Request message.

In addition, R3-215615 provides draft LS to SA2 on the indication of direct data forwarding availability.

Question: Which option is your preferred option for direct data forwarding indication for intra-5GS handover, and reason (e.g., the SA2 impact level, the different node releases issue, others etc)?

Question: Is there any need to notify SA2 about our agreement on the direct data forwarding availability indicator? The moderator understands this may/may not be related to the previous question, and good to collect views together.

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Prefer option 1. This option clearly has no impact on SA2 specification while option 2 does. Not fully understand the concern of the backward compatibility issue mentioned in 4772. The scenario “the SMF is release 15 and RAN node is release 16” is a little strange. Maybe the opponent can provide more details. Even if this scenario exists, as indicated above, From TS 23.502 when source NG-RAN node indicates direct forwarding path available to the R15 SMF, there is no reason for SMF to do indirect forwarding instead. Meanwhile the source NG-RAN can indicate it in the source to target container, then the target node can assign the direct data addresses from the direct address space. So we don’t see any issue for option 1. No strong view about LS even if option 1 is finally agreed. |
| Nokia | Option 2. The impact is less; only need an update of the semantic description. Also enables the SMF to keep control between direct and indirect forwarding. |

### E1 impact:

Over E1 interface, both R3-214773 and R3-215364 propose to add another codepoint “intra-system direct path available” for intra-system handover with direct data forwarding. The moderator proposes the following proposal.

Moderator proposal: Over E1 interface, add another codepoint “intra-system direct path available” for intra-system handover with direct data forwarding.

Please provide any view / comments on this topic and the proposal in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Agree |
| Nokia | Agree. |

## Inter-system HO from 4G to 5G in CP-UP separation scenario

The moderator minutes of the previous meeting were provide in R3-214150. Before the discussion, the scenario being discussed is re-iterated below:

- indirect data forwarding from EPS to 5GS in case one DRB in target gNB contains QoS flows mapped to different E-RABs in the source eNB

Then for CP-UP separation scenario, for the following two solutions, still quite different views are observed (the same as previous meeting):

- Four companies are in favor of solution 1.

- Three companies are in favor of solution 3.

Non-shared case: Two solutions are left on the table to support direct data forwarding from EPS to 5GS in scenario 4. Comparison and down selection is performed at next meeting. Solution 1: CU-CP requests one data forwarding address from the CU-UP using the existing signalling. CU-CP feedback the tunnel address to the two E-RABs in Handover Request Ack message to 5GC. With this, the data from the two E-RABs in the source node will be sent to one DRB buffer in the target (ref R3-211957/R3-212545/R3-212356) Solution 3: Add Data Forwarding from E-UTRAN Request List to the DRB To Setup List in PDU Session Resource To Setup List within Bearer Context Setup Request message and Data Forwarding from E-UTRAN Response List to the DRB Setup List in PDU Session Resource Setup List within Bearer Context Setup Request message (ref R3-211642/R3-211642/R3-211958).

The discussion below tries to first address the issues mentioned in the contributions.

### Solution 1 analysis

R3-214770 raises the following end marker issue, thinks that the out of sequence delivery may happen under this scenario.

- In the present case, the Y shape (solution 1) would create useless problems. For example, with solution 1 the target CU UP is not aware that if one, two or 3 E-RABs source endpoints are sender. When it receives the first end marker packets for E-RAB1 it will not expect subsequent packets that might arrive from E-RAB2 and will instead immediately start the delivery of fresh NG-U target packets as per TS 38.300 resulting in out of sequence delivery for the forwarded packets of E-RAB2.

While in R3-215480, it thinks that this is not an issue for 4G to 5G HO.

- This is nonetheless a non-issue, as inter-RAT HO is not lossless. PDCP is reset, and target node can start sending fresh data from CN after receiving the first end-marker.

Also in R3-215536, it indicates that the same issue is also applicable for solution 3, i.e. the characteristic of Scenario 4.

- In this scenario 4, the target NG-RAN node needs to put the data packets received over two E-RAB tunnels to the buffer of one DRB. The target NG-RAN node may receive data packets from the two tunnels simultaneously. In this case, how to decide the sequence to putting the data received from the two tunnels to one DRB buffer is not clear. Different vendors may have different implementation as the examples given in the figure. This may leads that the sequence of the data put to the buffer of the DRB is different from which is received from the CN.

- Out of order delivery for direct data forwarding is the characteristic of Scenario 4

The moderator tends to have the following question:

Question: Is Solution 1 acceptable/preferred to you based on the above analysis?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Yes. And we agree with the analysis particular of 5480 considering the non-lossless for 4G to 5G handover. |
| Nokia | No. The issue of end marker has not been solved. This creates out of sequency delivery unless you drop all packets received over second, third, etc.. forwarding tunnels after the end markers received over the first forwarding tunnel. For that aspect the analysis in tdoc R3-215536 is wrong i.e. solution 3 has NO in-sequence delivery, in contrast to what R3-215536 claims. Therefore, we cannot accept solution 1 based on a wrong technical analysis. Another aspect is if forwarded packets of other tunnels are dropped after receiving the end markers over the first tunnel, then there is no in-sequence delivery issue but then solution 1 works less efficient than solution 3. Said differently, solution 1 is more lossy than solution 3. Whether this is acceptable is another debate. But additionally, it would need to be checked how an implementation on field react to receiving forwarded packets after receiving the end marker packets. There is no guarantee that an implementation would not badly react and generate Error Indication messages towards the peer node at every handovers (see CT4 specifications). In summary, solution 3 adds one IE over the interface (is this a big cost?) but has no in-sequence delivery, is less risky and is more efficient. |

### Solution 3 analysis

R3-214770 think the solution 3 is clear approach as indicated below, and align with TS 23.502 section 4.11.1.2.2:

- CU UP is requested to allocate two tunnel endpoints and therefore the CU UP is aware that there are two forwarding tunnels that will generate separate end marker packets.

While R3-215480 and R3-215362 thinks this solution is not needed given that TS 29.281 section 4.3.0 has the following descriptions.

- The GTP-U protocol supports the possibility for one GTP-U tunnel endpoint to receive packets from multiple remote GTP-U endpoints”

And R3-215536 thinks that solution 3 have the same out of sequence delivery issue, and is too heavy for the specific case.

- Considering only the scenario 4 (multiple E-RABs to a DRB mapping) needs to be considered specifically, solution 3 seems a little heavy to address this scenario.

Question: Is Solution 3 acceptable/preferred to you based on the above analysis?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | No. A little heavy solution for a specific scenario 4 (proposed in R3-215536) |
| Nokia | Yes. Indeed solution 3 adds one IE over the interface (is this a big cost?) but has no in-sequence delivery, is less risky and is more efficient compared to solution 1: For solution 1, the issue of end marker has not been solved. This creates out of sequency delivery unless you drop the packets after the end markers. For that aspect the analysis in tdoc R3-215536 is wrong i.e. solution 3 has NO in-sequence delivery, in contrast to what R3-215536 claims. Therefore, we cannot accept solution 1 based on a wrong technical analysis. Another aspect of solution 1 is if packets are dropped after first end markers, then there is no in-sequence delivery issue but then solution 1 works less efficient than solution 3. Said differently, solution 1 is more lossy than solution 3. Whether this is acceptable is another debate. But additionally, it would need to be checked how an implementation on field react to receiving forwarded packets after receiving the end marker packets. There is no guarantee that an implementation would not badly react and generate Error Indication messages towards the peer node at every handovers. |

### Solution 1 vs. solution 3

Given that this has been discussed in several meetings, the moderator would propose the same question as in the SOD R13-214150 of the last RAN3 meeting.

Question: If your preferred solution is not agreeable by RAN3 (i.e. no consensus), what is your second best choice, including the “do nothing” solution.

Please provide any view / comments on this topic and the proposal in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Do nothing. |
| Nokia | At a bare minimum, we should check the end markers issue. If end markers issue is proven not an issue (which is not the case today) then we could refocus the debate of pain (add one IE over the interface) vs gain (be less lossy) which is a different question. |

### Potential way forward for this meeting

Given the same positions from companies, the moderator tends to collect your suggestions as input to be discussed at the 2nd round discussion, if any.

| Company | Comment |
| --- | --- |
| Nokia | At a bare minimum, we should check the end markers issue. If end markers issue is proven not an issue (which is not the case today) then we could refocus the debate of pain (add one IE over the interface) vs gain (be less lossy) which is a different question. |

### Potential CRs (can be left to 2nd round if needed)

R3-215362 proposes to add a note in TS 38.413 given that this new scenario is not explicitly mentioned as above, it seems that there is need to specify that one GTP-U tunnel endpoint corresponding to multiple remote GTP-U endpoints for the EPC to 5GC direct data forwarding case in RAN specification.

R3-214771 proposes to add Data Forwarding from E-UTRAN Request List IE in PDU Session Resource To Setup List, and add Data Forwarding from E-UTRAN Response List IE in PDU Session Resource Setup List.

Question: Views about the above CRs (e.g. revisions, no need etc)?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Nokia | Second round. Points highlighted above need first clarification before any CR discussion. |

## Further aspects

Please add any further aspects that are in scope and were not included in the above:

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

| R3-214770 | Support of 4g-5g direct data forwarding over E1 with non-shared gNB (Nokia, Nokia Shanghai Bell, China Telecom, CATT) | discussion |
| --- | --- | --- |
| R3-214771 | Support of 4g-5g direct data forwarding over E1 with non-shared gNB (Nokia, Nokia Shanghai Bell, China Telecom, CATT) | CR0642r, TS 38.463 v16.7.0, Rel-16, Cat. F |
| R3-214772 | Allocation of TNL addresses for intra-system direct forwarding (Nokia, Nokia Shanghai Bell, Orange, China Telecom, CATT) | discussion |
| R3-214773 | Allocation of TNL addresses for intra-system direct forwarding (Nokia, Nokia Shanghai Bell, Orange, China Telecom, CATT) | CR0643r, TS 38.463 v16.7.0, Rel-16, Cat. F |
| R3-215362 | Direct data forwarding for 4G to 5G handover (Huawei, Samsung, China Telecom) | CR0691r, TS 38.413 v16.7.0, Rel-16, Cat. F |
| R3-215363 | Direct data forwarding indication for intra-5GS handover (Huawei, Deutsche Telekom) | CR0692r, TS 38.413 v16.7.0, Rel-16, Cat. F |
| R3-215364 | Direct data forwarding indication for intra-5GS handover (Huawei, Deutsche Telekom) | CR0653r, TS 38.463 v16.7.0, Rel-16, Cat. F |
| R3-215480 | E1 aspects of inter-system direct data forwarding (Ericsson) | discussion |
| R3-215536 | Direct data forwarding for inter-system HO from 4G to 5G (Samsung, LGU+, Huawei) | discussion |
| R3-215615 | LS on indication of direct data forwarding availability (CATT,Nokia, Nokia Shanghai Bell,China Telecom) | LS out To: SA2,CT4 CC: |
| R3-215670 | Allocation of TNL addresses for intra-system data forwarding (China Telecom, CATT, Nokia, Nokia Shanghai Bell) | CR0713r, TS 38.413 v16.7.0, Rel-16, Cat. F |