3GPP TSG-RAN WG3 #114-e	R3-215825

1 – 11 November 2021

Agenda Item:	9.3.2.2

Source:	Samsung (moderator)

Title:	Summary of Offline Discussion on Mobility Between DC and SA

Document for:	Approval

# Introduction

CB: # 22_DirectDataFwd_DC

- NR SA to EN-DC Handover: Whether to pursue option 3 and the detailed signaling solution to support option 3?

- EN-DC to NR SA Handover: Whether to pursue option 2/3 and the detailed signaling solution to support option 2/3?

- Whether scenario 3, e.g. MN has no direct forwarding, SN has direct forwarding shall be supported?

- Any other topics?

- Capture agreements and provide CRs if agreeable

(Samsung - moderator)

Summary of offline disc R3-215825

# For the Chairman’s Notes

Propose to agree the following:

# Discussion

## Direct data forwarding from MR-DC connected to 5GC to E-UTRAN

In [7][8], problems were identified for supporting direct data forwarding from the source SN to the target eNB during inter-system handover from MR-DC connected to 5GC to E-UTRAN:

1)	The source SN doesn’t know the mapping of a Qos flow to the E-RAB tunnel.

2)	For inter-system handover, the forwarded packet should not include the PDCP SN and QFI. The source SN doesn’t know the handover is inter-system handover.

To solve the two problems, the proposal is to add new IE “Data Forwarding Info from target E-UTRAN node” in XN-U ADDRESS INDICATION message to transmit the E-RAB data forwarding tunnel. The existence of the new IE implicitly indicates an inter-system handover.

Q1: Do you agree the proposal?

| Company | Comment |
| --- | --- |
| Samsung | Yes. Otherwise, direct data forwarding from the source SN to the target eNB cannot be supported. |
| CATT | Support the intention of the proposal. However, as to the solution, in fact, we prefer the solution 1 in the original contribution i.e. MN send the E-RAB id for each flow received from CN to SN and provide data forwarding tunnel per E-RAB. Our view is that the SN case is not completely the same with CP/UP separation scenario. Since SN has both control plane and use plane, it is reasonable to send the E-RAB information from MN to SN which provide reference information. |

Q2: If the answer to Q1 is yes, any comment on the CR in R3-215535 [8]

| Company | Comment |
| --- | --- |

## Direct data forwarding from NR SA to EN-DC HO

The following agreements have been made at last RAN3#113e meetings.

NR SA to EN-DC Handover:

Direct data forwarding is possible between the source NG-RAN node and target SgNB (SN) node.

RAN3 acknowledges that for EN-DC, the SgNB could have direct data forwarding information with its neighbouring nodes without extra configuration effort.

- One of reasons is that RAN3 specification already supports the SgNB/gNB logical nodes coexistence case via the 5GS-TAC IE in TS 36.423, in which case both could share the direct data forwarding configuration information.

WA: the option 3 below could be pursued between the following options.

- Option 2: target MN – the target MeNB is configured by OAM with the direct forwarding path availability information between the neighboring source nodes and the neighboring target SgNB nodes (i.e. not relevant to itself).

- Option 3: target SN – the target SN is configured by OAM with direct forwarding path availability information between itself and neighboring source nodes

In [1]-[12], it is proposed to turn the WA to the agreement and agree option 3.

Q3: Do you agree to turn the WA to the agreement?

| Company | Comment |
| --- | --- |
| Samsung | Yes. The technical reasons are explained in [1]-[12]. |
| CATT | Yes |

In order to let the Target SN decides direct forwarding path availability between itself and the source NG-RAN, the following specification impact are needed:

-	The target MN provides the source RAN node ID to the target SN;

-	The target SN notifies the direct data forwarding availability indication to the target MN.

Q4: Do you agree the above specification impact is needed?

| Company | Comment |
| --- | --- |
| Samsung | Yes. |
| CATT | Yes |

## Direct data forwarding from EN-DC to NR SA HO

The following agreements have been made at last RAN3#113e meetings.

EN-DC to NR SA Handover:

direct data forwarding is possible between the source SN and the target NG-RAN node.

WA: the option2/3 below could be pursued among the following options

- Option 1: source MN – the source MN is configured by OAM with the direct forwarding path availability information between the source SN and the target node (i.e. not relevant to itself).

- Option 2/3: source SN/target node – the source SN or the target NG-RAN node is configured by OAM with the direct forwarding path between itself and neighboring nodes.

In [1]-[12], it is proposed to take the WA to the agreement and agree that option2/3 below could be pursued for direct data forwarding from EN-DC to NR SA HO.

Q5: Do you agree to turn the WA to the agreement?

| Company | Comment |
| --- | --- |
| Samsung | Yes. The technical reasons are explained in [1]-[12]. |
| CATT | Yes |

For option 2 and option 3, the moderator observed that both target node and source SN could be configured by OAM with the direct forwarding path between itself and neighboring nodes. This information is necessary if the node needs to trigger a handover for its serving UEs (for the source SN, it can serve UEs in case of SgNB/gNB logical nodes coexistence). So option 2 and option 3 are not exclusive.

Observation: Option 2 and Option 3 are not exclusive. Both could be configured by OAM with the direct forwarding path between itself and neighboring nodes.

Q6: Do you agree the observation?

| Company | Comment |
| --- | --- |
| Samsung | Yes. |
| CATT | Yes |

The actual question which needs to be discussed is whether the source SN or the target node decides direct forwarding path availability between the source SN and the target node for handover from EN-DC to SA. There are the following two options:

Option 2a: The source SN decides direct forwarding path availability between the source SN and the target node.

The source MN queries the source SN to get this information. The source MN transmits the information to the SMF. The SMF further transmits the information to the target node.

Option 3a: The target node decides direct forwarding path availability between the source SN and the target node. The target node transmits the information to the source in target node to source node transparent container.

The signaling flow for Option 2a:

Figure 1: The signaling flow for Option 2a:

The signaling flow for Option 3a:

Figure 2: The signaling flow for Option 3a:

Q7: Is option 2a or option 3a your preferred solution for direct data forwarding from EN-DC to SA NR?

| Company | Comment |
| --- | --- |
| Samsung | Option 3a The benefits of Option 3a is that the existing handover signaling flow is not impacted. While for Option 2a, a new procedure is inserted between Handover Required and Handover Command message. This will impact the state machine design in implementation. Currently, the Source MeNB is waiting for Handover Command message after sending out Handover Required message. |
| CATT | Option 2a With option 3a, for EN-DC to SA handover scenario, data forwarding between source SgNB and target gNB has to involve both EPS and 5GS CN node even if direct data forwarding tunnel is available between source SgNB and target gNB. It is not optimal. What’s more, if the SMF finds that indirect data forwarding is not possible and also receive direct data forwarding path not available indication from source MN, data forwarding could not be supported even if there is direct data forwarding tunnel between source SgNB and target gNB. As to the comments from SAMSUNG on option 2a, since SN node is still kept during handover preparation procedure, source MN is already ready to have interaction with source SN node. Message exchange between source MN and source SN would not impact the state design machine between source MN and target node . |

## Intra-system mobility scenarios and common design

The following agreements have been made at last RAN3#113e meetings.

The additional scenarios (i.e. intra-system SN change, and intra-system handover involving MR-DC) are considered, and it is expected to have a common design for all handover scenarios involving MR-DC.

So the agreed solutions should also be applicable for the additional scenarios (i.e. intra-system SN change, and intra-system handover involving MR-DC)

Proposal: Agree that the above proposals for inter-system handover are applicable for intra-system handover involving MR-DC, and intra-system SN change.

Q8: Do you agree the proposal?

| Company | Comment |
| --- | --- |
| Samsung | Agree |
| CATT | Agree |

## Scenario 3 (MN has no direct forwarding, SN has direct forwarding)

The scenario 3 is marked with FFS as follows. This is applicable both for EN-DC to NR SA handover, and NR SA to EN-DC handover.

- Scenario 3 (FFS): MN has no direct forwarding, SN has direct forwarding

### Inter-system handover from NR SA to EN-DC

In inter-system handover from NR SA to EN-DC case, the open point for scenario 3 is whether direct data forwarding should be performed from the source NG-RAN node to the target SN in the following scenario?

- Source NG-RAN node has no direct data forwarding path with the target eNB

- Source NG-RAN node has direct data forwarding path with the target en-gNB

Moderator Analysis: From technical point of view, it is possible to support direct data forwarding from the Source NG-RAN node to the target en-gNB.

E.g. the enhancement based on Option 3 in 3.2:

- The target MN provides direct data forwarding availability indication and the bearer list which terminate at the SN to the MME;  The MME further forwards those information to the AMF/SMF.

- With that, the SMF/UPF and MME/SGW will not assign indirect data forwarding path for the bearers for direct data forwarding.

Q9: Do you think direct data forwarding for scenario3 should be supported for inter-system HO from SA NR to EN-DC?

| Company | Comment |
| --- | --- |
| Samsung | We prefer to firstly focus on the solutions for Scenario 1 and Scenario 2. After those are concluded, scenario 3 can be discussed further. |
| CATT | Current data forwarding path Optimal data forwarding path Scenario 1 MN terminated:Source MN->target node SN terminated:Source SN->Source MN->target node MN terminated: Source MN->target node SN terminated: Source SN->target node Scenario 2 MN terminated:Source MN->target node SN terminated:Source SN->Source MN->target node No optimization could be done Scenario 3 MN terminated: Source MN->S-GW->UPF->Target node SN terminated: Source SN->Source MN-> Serving GW -> UPF ->target node MN terminated: Source MN->Source MN->Target node SN terminated: Source SN->target node In above table, we provide the comparison of the data forwarding path optimization for all 3 scenarios. Obviously, in scenario 1, the optimization is only to avoid the involvement of MN node. However, in scenario 3, the optimization is to avoid the involvement of CN node which has much more benefits. With that, we prefer to support all the 3 scenarios with unified solution if the impact to spec is acceptable. |

### Inter-system handover from EN-DC to SA

In inter-system handover from EN-DC to NR SA case, the open point for scenario 3 is whether direct data forwarding should be performed from the source SN to the target NG-RAN node in the following scenario?

- Source eNB has no direct data forwarding path with the target NG-RAN node

- Source en-gNB has direct data forwarding path with the target NG-RAN node

Moderator Analysis: From technical point of view, it is possible to support direct data forwarding from the Source SN to the target NG-RAN node no matter Option 2a or Option 3a is agreed in 3.3. The solution based on Option 2a was proposed in [9]. The solution based on Option 3a could be as below: The source eNB sends the bearer list terminated at the SN to the MME and to the target. The SMF/AMF indicates direct forwarding path availability of the SN to the source MME. Therefore the MME will not request the SGW to assign indirect data forwarding tunnel for direct data forwarding.

Q10: Do you think direct data forwarding for scenario3 should be supported for inter-system HO from EN-DC to SA?

| Company | Comment |
| --- | --- |
| Samsung | We prefer to firstly focus on the solutions for Scenario 1 and Scenario 2. After those can be concluded, scenario 3 can be discussed further. |
| CATT | Current data forwarding path Optimal data forwarding path Scenario 1 MN terminated:Source MN->target node SN terminated:Source SN->Source MN->target node MN terminated: Source MN->target node SN terminated: Source SN->target node Scenario 2 MN terminated:Source MN->target node SN terminated:Source SN->Source MN->target node No optimization could be done Scenario 3 MN terminated: Source MN->S-GW->UPF->Target node SN terminated: Source SN->Source MN-> Serving GW -> UPF ->target node MN terminated: Source MN->Source MN->Target node SN terminated: Source SN->target node In above table, we provide the comparison of the data forwarding path optimization for all 3 scenarios. Obviously, in scenario 1, the optimization is only to avoid the involvement of MN node. However, in scenario 3, the optimization is to avoid the involvement of CN node which has much more benefits. With that, we prefer to support all the 3 scenarios with unified solution if the impact to spec is acceptable. |

## Further aspects

Please add any further aspects that are in scope and were not included in the above:

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

| [1] R3-214918 | SN direct data forwarding (Qualcomm Incorporated) | discussion |
| --- | --- | --- |
| [2] R3-214919 | SN direct data forwarding (Qualcomm Incorporated) | CR1625r, TS 36.423 v16.7.0, Rel-16, Cat. B |
| [3] R3-214923 | Direct data forwarding between SA and NSA (Qualcomm Incorporated, CATT) | CR1626r, TS 36.423 v16.7.0, Rel-16, Cat. B |
| [4] R3-215365 | Direct data forwarding for mobility between DC and SA (Huawei, Samsung, China Telecom) | CR0553r3, TS 38.423 v16.7.0, Rel-16, Cat. F |
| [5] R3-215532 | Discussion on direct data forwarding for mobility between DC and SA (Samsung, Huawei) | discussion |
| [6] R3-215533 | Direct data forwarding for mobility between DC and SA (Samsung, Huawei) | CR0703r, TS 38.413 v16.7.0, Rel-16, Cat. F |
| [7] R3-215534 | Direct data forwarding from MR-DC connected to 5GC to E-UTRAN (Samsung, Huawei, Verizon Wireless, LGU+) | discussion |
| [8] R3-215535 | Correction of Direct data forwarding from MR-DC connected to 5GC to E-UTRAN (Samsung, Huawei, Verizon Wireless, LGU+) | CR0706r, TS 38.423 v16.7.0, Rel-16, Cat. F |
| [9] R3-215616 | Discussion on data forwarding between DC and SA (CATT,Qualcomm) | discussion |
| [10] R3-215617 | CR on data forwarding between DC and SA (CATT,Qualcomm) | CR0710r, TS 38.423 v16.7.0, Rel-16, Cat. F |
| [11] R3-215781 | Direct data forwarding for mobility between DC and SA (Huawei, Samsung) | CR1645r, TS 36.423 v16.7.0, Rel-16, Cat. F |
| [12] R3-215784 | Direct data forwarding for mobility between DC and SA (Samsung, Huawei) | CR1850r, TS 36.413 v16.7.0, Rel-16, Cat. F |