3GPP TSG-RAN WG3 #114-e	R3-215826

Online, 1 – 11 November 2021

Agenda Item:	9.3.3

Source:	Samsung (moderator)

Title:	Summary of Offline Discussion on Lossless intra-system HO

Document for:	Approval

# Introduction

CB: # 23_Lossless_Intra-systemHO

- Adopt Solution 3b to address the scenario of change in QoS to DRB mapping at target gNB during lossless intra-RAT HO? Adjust semantics of Ignore Mapping Rule Indication IE to be applicable only to lossless intra-system handover data forwarding scenario? Nok, E///

- Adopt Solution 1? Samsung, Huawei, Intel Corporation, China Telecom, LGU+, ZTE

- Capture agreements and provide CRs if agreeable

(Samsung - moderator)

Summary of offline disc R3-215826

# For the Chairman’s Notes

Propose the following:

Agreement:

# Discussion

Agreements at previous meetings:

For supporting lossless handover when a QoS flow is mapped to a different DRB at handover, the old DRB needs to be configured in the target cell for transmitting the forwarded packets

The above mechanism is already supported if the target node is aggregated.

At intra-system HO, in case of per-DRB data forwarding, CU-UP should be aware of old mapping for data forwarding and new mapping for fresh data

Both the old and new mappings are provided to the target CU-UP during the bearer context setup procedure (FFS whether existing IEs are sufficient); go for BC solution

Regarding how to transmit both of the mapping with Bearer context setup procedure, three solutions were discussed at RAN3#113-e meeting without conclusion.

It’s good to see that the three solutions were converged to two in the contributions submitted to this meeting.

Solution 1: Add QoS Flows Information To Be Updated as proposed in R3-211947/48/49[4][5][6]

Solution 3b: Using QoS Flows forwarded on the forwarding tunnel(s) in Data Forwarding Information Request to transmit the Qos flows which will be forwarded (source mapping) over the DRB tunnel. And using QoS Flows Information To Be Setup to transmit the Qos flows which are configured to this DRB at target side. In order to support the following scenario 3 (refer to R3-206006/07 for RAN3#110-e meeting), using “Ignore Mapping Rule Indication” IE to inform CU-UP the DRB is used for data forwarding only [1][2][3].

|  | Source (old) mapping | New mapping by the target CU-CP | What needs to be transmitted from target CU-CP to target CU-UP: – {old mapping}: for handling forwarded packet – [new mapping]: for handling fresh data |
| --- | --- | --- | --- |
| 3 | DRB1: QFI1 DRB2: QFI2 | DRB1: QFI1, QFI2 | DRB1: {QFI1} ( [QFI1, QFI2] DRB2: {QFI2} ( [none] |

Each solution works. The issue has been discussed for several meetings. Convergence is needed in order to solve the confirmed problem.

Q1: Which solution are you ok in order to support lossless intra-system handover in CP-UP separation scenario?

| Company | solution | comments |
| --- | --- | --- |
| Intel Corporation | Solution 1 | Based on the updated Solution 3b, we further took time to go deeper analysis, captured below. We can further discuss, but based on our analysis, we have technical concerns especially on 3rd and 4th points below of the proposed Solution 3b, for which we believe Solution 1 should be adopted. |
| Nokia | Solution 3b | Issues with Solution 1 which we have highlighted multiple meetings. Solution 1 modifies existing meaning and handling of the legacy IEs, and further introduces a new functional requirement to the gNB-CU-UP to be able to handle the same QFI value for multiple DRBs simultaneously. It also brings unclarity as to which DRBs belong to the “old mapping” and which refer to the “new mapping”. This is a new function for the gNB-CU-UP. The following are examples of scenarios where these issues will be encountered with solution 1 - Ex1. (old config: DRB1:QFI1, new config DRB2: QFI1) - Ex.2 (old config: DRB1:QFI1, QFI3; DRB2: QFI2 // new config DRB2: QFI1, QFI2; DRB3: QFI3) With the encoding proposed in Solution 1, the following would be done Ex.1 * QoS Flows Information To Be Setup (DRB1:QFI1) * QoS Flows Information To Be Setup (DRB2: QFI1) The encoding above incurs issues given that two separate DRBs are being signalling as having same QFI, which is not even allowed by RAN2. Basically, the same legacy IEs are used to convey old config and new configs. This solution is expecting that somehow the gNB-CU-UP based on some other information (e.g., data forwarding related IEs) deduces that DRB2 is only meant to be set after data forwarding has completed. This we see as non-backwards compatible as it affects very basic legacy functions. Ex.2 * QoS Flows Information To Be Setup (DRB1: QFI1, QFI3) * QoS Flows Information To Be Setup (DRB2: QFI2) * QoS Flows Information To Be Setup (DRB3: QFI3) * QoS Flows Information To Be Updated (DRB2: QFI1, QFI2) In this example again, multiple QFIs are assigned to multiple bearers simultaneously. Further, DRB2 uses the new IEs to convey the new configuration, while DRB3 conveys the new configuration with the legacy IEs. For these reasons Solution 1 is unacceptable. In regard to remarks from Intel on Solution 3b * Reuse of an existing IE: If this is not preferable, this can easily be tackled via a new IE (as proposed in Ericsson paper) * Backwards compatibility: a CU-CP and CU-UP pair will need to learn ONLY once whether the function is supported or not for one single bearer context setup. This is a minor impact compared to changing meaning of legacy IEs as proposed in Solution 1. Further, the description below regarding BC for Sol1 will not hold valid for the example above given in Ex.2, as there will be a conflict due to the simultaneous QFIs mapped to the same DRBs. |

Analysis of Solution 3b and comparison to Solution 1:

- Abusing “Ignore Mapping Rule Indication” IE in Solution 3b

  - From the last summary [4468], this IE was introduced for UL default DRB where gNB doesn’t want to assign QoS flows yet (over RRC, gNB can assign UL default DRB without any mapping info).

  - Abusing this IE for the purpose of QoS flow remapping does not abide by the original purpose.

- Backward compatibility

  - Solution 3b: CU-UP that does not support this new feature (either by QoS flows included for “to be forwarded” is a strict superset of QoS flows included for “to be setup”, or by not comprehending “Ignore Mapping Rule Indication” with criticality “reject”), CU-UP will reject the BRR SETUP procedure, and thus CU-CP has to retry BRR SETUP to establish the old DRB config first, and then later modify (BRR MOD) for new mapping. Always 2 more extra class-1 procedure.

  - Solution 1: The proposed QoS flows to be updated IE is with criticality “ignore”. If not comprehended by CU-UP, either the old DRB configuration is established, or in the worst case CU-CP needs to trigger BRR MOD proc to modify back to the old DRB configuration. Then, CU-CP can later modify for new mapping. In total, can be 1 more extra class-1 procedure (or in the worst case, 2 more extra class-1 procedure, same as Solution 3b).

- Breaking principle by hijacking the meaning of “QoS flows to be forwarded” as if “QoS flows to be setup” for "old DRB mapping to be updated"

  - Here the situation is about lossless HO where CU-CP first decides the same old DRB configuration for lossless DRB forwarding.

  - Thus “QoS flows to be forwarded” is always equal to “QoS flows to be setup” for old DRB configuration toward CU-UP according to TS 38.300.

  - But this does not mean that we can hijack its meaning and abuse “QoS flows to be forwarded” as if “QoS flows to be setup” for old DRB configuration to be temporary used and its mapping will be updated further.

  - We believe it shall be always that “QoS flows to be setup” is the one used to “establish” a DRB in CU-UP. This is the principle we always should keep in mind.

  - That’s why,

    - Regardless of whether a DRB stays or is gone after remapping, “QoS flows to be setup” shall be one used to establish the DRB with old mapping to handle forwarded packets.

    - Even if new DRB is created due to remapping (so no forwarded packets over this DRB), “QoS flows to be setup” shall be the one used to establish the DRB with new mapping.

- DRB admission by CU-UP

  - Even we assume CU-UP supports this new feature, we should not always assume that CU-UP would admit any DRB requested to be setup by CU-CP.

  - In other words, a solution should work well even in the case that a certain DRB is not admitted by CU-UP.

  - In this case, Solution 3b could be problematic, because forwarding IE is hijacked as “old mapping to be updated”.

  - Here is some comparison based on the cases that has been dealt by papers so far:

| Cases | Solution 1 | Solution 3b |
| --- | --- | --- |
| DRB1 (QF1) è QF1, QF2 DRB2 (QF2) è none | DRB1: forwarding/setup (QF1) + updated IE included (QF1, QF2) DRB2: forwarding/setup (QF2) + no updated IE included If DRB2 is not admitted, - old DRB1(QF1) is first established, - then updated to new mapping (QF1, QF2) as expected. If DRB1 is not admitted (e.g due to no admission of QF1) - old DRB2(QF2) stays. | DRB1: forwarding (QF1) + setup (QF1, QF2) DRB2: forwarding (QF2) + setup (none by new ignore IND) If DRB2 is not admitted, - new DRB1(QF1,QF2) is directly established with forwarding of QF1. If DRB1 is not admitted (e.g. due to no admission of QF1), - QF2 is gone! (even though QF2 is admitted by CU-UP). - because forwarding IE is hijacked as “old mapping to be updated”. |
| DRB1 (QF1, QF3) è none DRB2 (QF2) è QF1, QF2 DRB3 (none) è QF3 | DRB1: forwarding/setup (QF1, QF3) + no updated IE included DRB2: forwarding/setup (QF2) + updated IE included (QF1, QF2) DRB3: no forwarding but setup (QF3) + updated IE included (QF3) If DRB2 is not admitted (e.g. due to no admission of QF2), - old DRB1(QF1,QF3) is first established. - then updated to new mapping DRB1(QF1), DBR3(QF3). | DRB1: forwarding (QF1, QF3) + setup (none by new ignore IND) DRB2: forwarding (QF2) + setup (QF1, QF2) DRB3: forwarding (none) + setup (QF3) If DRB2 is not admitted (e.g. due to no admission of QF2), - QF1 is gone! (even though QF1 is admitted by CU-UP). Only QF3 remains. - because forwarding IE is hijacked as “old mapping to be updated”. |

# Conclusion, Recommendations [if needed]

If needed

# References

| [1] R3-215074 | Discussion on Lossless intra-system HO in disaggregated architecture and QoS flow Mapping over E1 (Nokia, Nokia Shanghai Bell) | discussion |
| --- | --- | --- |
| [2] R3-215076 | Lossless intra-system HO in disaggregated architecture – Sol 3b (Nokia, Nokia Shanghai Bell) | CR0647r, TS 38.463 v16.7.0, Rel-16, Cat. F |
| [3] R3-215481 | Lossless Intra-System HO in CP-UP Separation Scenario (Ericsson) | discussion |
| [4] R3-215529 | Lossless intra-system HO in dis-aggregated gNB scenario (Samsung, Huawei, Intel Corporation, China Telecom, LGU+, ZTE) | discussion |
| [5] R3-215530 | Correction of intra-system HO in CP-UP separation scenario (Samsung, Huawei, Intel Corporation, China Telecom, LGU+, ZTE) | CR0658r, TS 38.463 v15.9.0, Rel-15, Cat. F |
| [6] R3-215531 | Correction of intra-system HO in CP-UP separation scenario (Samsung, Huawei, Intel Corporation, China Telecom, LGU+, ZTE) | CR0659r, TS 38.463 v16.7.0, Rel-16, Cat. A |