3GPP RAN3 #114-e	R3-215827

1st November – 11th November 2021

Online

Agenda Item:	9.3.4

Source:	Ericsson

Title:	SoD_CB: # 24_DynamicACL

Document for:	Discussion, Decision

# Introduction

CB: # 24_DynamicACL

- The source IP address used for data forwarding traffic is signalled from the node sending forwarded data to the target node on a per Qos flow basis? The gNB-CU-UP signals the source IP address to be used for data forwarding to the CU-CP? Huawei, Deutsche Telekom, China Telecom, Ericsson

- For assessment of required granularity of the source IP address information in support of dynamic ACL, RAN3 is kindly requested to include: 1) per PDU session granularity, and 2) per DRB granularity? Focus on direct data forwarding at current stage? Nok

- SA2 has already provided a mechanism to solve the dynamicACL issue for indirect data forwarding? The source IP address used for data forwarding traffic is signalled to the target node on a per UE basis? ZTE

- Provide CRs if agreeable

(E/// - moderator)

Summary of offline disc R3-215827

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

At RAN3.113e RAN3 agreed to the following:

It is proposed to agree that ACL needs to be supported for the following use cases:

- Signalling of source IP address for data forwarding traffic as part of the S1 and NG handover Information for

- Direct data forwarding

- Indirect data forwarding

-    Signalling of source IP address for data forwarding traffic as part of the X2 and Xn handover Information

-    For EN-DC and MR-DC cases, it is proposed to include the source IP address for data forwarding traffic as part of the

- MN-initiated SN Modification request/response

- SN Change Required

- SN addition request

-     In split architecture, at SN side, the source node user plane IP addresses should be also transferred to the ng-eNB-DU, gNB-DU for data forwarding for MN terminated bearers, and to the SN’s gNB-CU-UP for SCG bearers.

Send an LS to SA2 and CT1 to check whether source IP address Information from the CN to target RAN in the case of indirect data forwarding, as part of the S1/NG HO Information, is feasible

Conclude that no further enhancements are needed to address the IP Sec use case for ACL.

One point was left open, which was captured as below:

The granularity of the Source IP Address in support to ACL, to be continued...

RAN3 also agreed to send an LS to SA2, in [1], where the indirect data forwarding use case and possible  solutions was presented.

SA2 replied to RAN3´s LS in [2]. In this LS SA2 asks the following question:

SA2 kindly asks RAN3 to provide their view on whether the source address for a normal Iu-U/N3 tunnel (for example, during Service request procedure from CM_IDLE to CM_CONNECTED) needs to be provided to RAN for ACL support or it can be made aware to RAN by other means.

## Discussion on Granularity of IP Addresses

Three options have been presented at RAN3-114e for the granularity of the Source IP address signalled from source RAN to target RAN.

These three options are described below:

Option 1: per QoS Flow granularity

In [3] a number of vendors and operators propose that the source IP address of direct forwarding traffic, to be forwarded to the target RAN, is signalled with a per QoS Flow granularity. In this way a source IP address may be signalled for each QoS flow whose traffic is forwarded. The reason is to enable the target RAN to identify the source IP address used by traffic associated with a given QoS Class and S-NSSAI. The latter enables cloud based deployments of ACL.

Option 2: per PDU Session/per DRB granularity

In [4] it is proposed to enable a source IP address granularity per PDU Session and per DRB. The motivation is that data forwarding can be done on a per PDU Session and per DRB level, hence a source IP address per PDU Session and per DRB is needed.

Option 3: per UE granularity

In [5] it is proposed that source IP addresses are signalled on a per UE basis. Namely a list of Source IP addresses are signalled per UE, without any specific association to the type of traffic the source IP is used for. The justification for this proposal is in the simplicity of such technique.

In order to enable a faster discussion it is worth mentioning that traffic transmitted as part of a GTP-U tunnel, such as the UP tunnel used for data forwarding, may have different source IP addresses, while the target IP address shall be the same (i.e. the target IP address is the one specified by the target RAN).

This can be deduced from the definitions in TS29.281 reported below:

GTP-U Tunnel: A GTP-U tunnel is identified in each node with a TEID, an IP address and a UDP port number. A GTP-U tunnel is necessary to enable forwarding packets between GTP-U entities.

GTP-U Tunnel Endpoint: A GTP-U tunnel endpoint identifies a user plane context (e.g EPS bearer, PDU session or a RAB) for which a received GTP-U packet is intended. A given GTP-U tunnel endpoint may receive GTP-U packets from more than one source GTP-U peer (See clause 4.3.0).UDP/IP Path: Connection-less unidirectional or bidirectional path defined by two end-points. An IP address and a UDP port number define an end-point. A UDP/IP path carries GTP messages between network nodes related to one or more GTP tunnels.

From the above it can be understood that traffic included in a GTP-U tunnel used for data forwarding shall have the same termination IP address, but it may have different source IP addresses.

Companies are invited to provide their view on preferences for the source IP address granularity options listed above.

| Company | Comment |
| --- | --- |
| Ericsson | We prefer a per QoS Flow granularity. As explained in [3], this allows support for a cloud RAN implementation where instances of the ACL function can be deployed on a per QoS/per Slice level. Such implementations using per QoS/per Slice dedicated ACL instances would not be possible with a per UE source IP address granularity such as Option 3. We think that the standard should not prevent implementations unnecessarily. With respect to Option 2, we would like to point out that different source IP addresses may be used for traffic of different QoS flows included in a data forwarding tunnel established per PDU Session or per DRB. Namely, Option 2 forces the use of the same source IP address for all traffic in the data forwarding tunnel, which again limits implementations unnecessarily. |

## Indirect data forwarding during SN change

In [5] the following is proposed:

It is proposed for RAN3 to further discuss how to solve the dynamic ACL issue for the indirect data forwarding during SN change.

Companies are invited to provide their views on whether the indirect data forwarding during SN change should be considered as a use case that shall be addressed by RAN3

| Company | Comment |
| --- | --- |
| Ericsson | We believe that the indirect data forwarding during SN change use case is a niche use case which may be left out of the use cases addressed by RAN3. |

## Source address for a normal Iu-U/N3 tunnel

In [2] SA2 asks the following question to RAN3:

SA2 kindly asks RAN3 to provide their view on whether the source address for a normal Iu-U/N3 tunnel (for example, during Service request procedure from CM_IDLE to CM_CONNECTED) needs to be provided to RAN for ACL support or it can be made aware to RAN by other means.

Companies are invited to provide their views and answers to the question above.

| Company | Comment |
| --- | --- |
| Ericsson | We are inclined to think that a “normal” S1-U/NG-U tunnel from CN to RAN is likely to be generated by a fixed number of CN UP GWs. For this reason one possibility could be to configure the RAN with the source IP addresses such UP CN nodes may use towards the RAN. Said that, we acknowledge that cloud implementations in the CN may involve the use of different source IP addresses towards the RAN, in which case manual configuration may become a considerable burden for operators. We would therefore reply to SA2 stating that RAN3 considers provisioning to the RAN of the source IP address for traffic transmitted over a normal Iu-U/N3 tunnel as a low priority use case. We would like to highlight that the case of indirect data forwarding is more complex than the one with normal Iu-U/N3 tunnel. This is because the CN UP GW in charge of indirect data forwarding may be either the source CN GW (e.g. source UPF) or the target CN GW (e.g. target UPF) or indeed a different CN GW specifically selected for data forwarding. Hence manual configuration at the RAN of source IP addresses for indirect data forwarding traffic is a more complex and time consuming procedure. |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-214414, LS On ACL support for Indirect Data Forwarding  (RAN3)

R3-215801, Reply LS On ACL support for Indirect Data Forwarding (SA2)

R3-214856, Support of dynamic ACL during handover and dual connectivity (Huawei, Deutsche Telekom, China Telecom, Ericsson)

R3-215317, On the granularity of the source IP address for dynamic ACL (Nokia, Nokia Shanghai Bell)

R3-215619, Discussion on dynamic ACL (ZTE Corporation)