3GPP TSG-RAN WG3 #114	R3-215829

1 - 11 November 2021

Online

Agenda Item:	9.3.6.1

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion – Correction of NG Handover

Document for:	Approval

# Introduction

This is the summary document for the following come back:

CB: # 26_NGHandover

- Check the scenario and issue, whether clarification is needed?

- Provide CRs if agreeable

(Nok - moderator)

Summary of offline disc R3-215829

# For the Chairman’s Notes

Propose the following:

Agree TP … .

# First Round

Background of the issue and Summary of RAN3#113

For NG handover we have the following IE in the Source NG-RAN to Target NG-RAN container IE in section 9.3.1.29:

| >>QoS Flow Information List |  | 1 |  |  | - |  |
| --- | --- | --- | --- | --- | --- | --- |
| >>>QoS Flow Information Item |  | 1..<maxnoofQoSFlows> |  |  | - |  |
| >>>>QoS Flow Identifier | M |  | 9.3.1.51 |  | - |  |
| >>>>DL Forwarding | O |  | 9.3.1.33 |  | - |  |
| >>>>UL Forwarding | O |  | 9.3.1.118 |  | YES | reject |
| >>DRBs to QoS Flows Mapping List | O |  | 9.3.1.34 |  | - |  |

And usage in section 8.4.1.2:

If the DL Forwarding IE is included for a given QoS flow in the PDU Session Resource Information Item IE within the Source NG-RAN node to Target NG-RAN node Transparent Container IE of the HANDOVER REQUIRED message and it is set to "DL forwarding proposed", it indicates that the source NG-RAN node proposes forwarding of downlink data for that QoS flow.

The forwarding proposal is per QoS flow in the above statement. However, the above statement does not say if the proposal is necessarily associated with a PDU session tunnel forwarding.

Observation 1: the text for the DL Forwarding IE doesn’t explicitly say whether this proposal is necessarily associated with a PDU session forwarding tunnel.

Besides, when the flow-DRB mapping is sent another text states:

If the DRBs to QoS Flows Mapping List IE is included in the PDU Session Resource Information Item IE within the Source NG-RAN node to Target NG-RAN node Transparent Container IE of the HANDOVER REQUIRED message, it implicitly indicates that the source NG-RAN node proposes forwarding of downlink data for those DRBs

The sentence highlighted in yellow associate the sending of flow-DRB mapping to a forwarding proposal.

There are therefore two lists to indicate forwarding proposal: the QoS Flow Information List IE and the DRB to QoS Flow mapping List IE.

It is not clear what exactly source node is expected to signal depending on the scenario.

This was left to be continued at last RAN3#113 (see [2]):

To be continued at next RAN3 meeting:

The issue of whether a same QFI can be at the same time in the QoS Flow Information List IE and Associated QoS Flow List IE of the source to target container is still unresolved i.e. the source gNB proposes to target gNB both options: forwarding over the PDU session tunnel and forwarding over the DRB tunnel for a same QFI and let target gNB decide. Some companies think this coding is allowed, some companies think this is not allowed.

RAN3#114

At the last RAN3#113 meeting, it was commented that the principle is “the source proposes, the target decides”. That is well understood, but this doesn’t solve the present question which is related to what can exactly source propose and where. For example, can it propose simultaneously a QoS flow to be forwarded over both PDU session tunnel and DRB tunnel?

We propose here to proceed with a few examples to be more precise in the questions.

Starting point: The source gNB has QoS flows 1,2,3 mapped onto DRB1 and QoS flows 4,5,6 mapped to DRB2. Let us consider the following parameter settings:

Setting 1

Qos flow information list= QFI 4

DRB to flow mapping list = DRB1

Associated QoS flow list (of DRB1)= QFI 1,2,3

Q1: is setting 1 valid according to you? If yes, does it mean that QFI 4 is proposed for PDU session forwarding and QFIs 1,2,3 for DRB forwarding?

| Company | Comment |
| --- | --- |

Setting 2

Qos flow information list= empty.

DRB to flow mapping list = DRB1

Associated QoS flow list (of DRB1)= QFI 1,2,3

Q2: is setting 2 valid according to you? If yes, if the target gNB cannot accept the DRB tunnel forwarding proposed can target gNB still include a DL TEID for PDU session tunnel so that the source could instead forward any of QFIs 1 or 2 or 3 over that PDU session tunnel?

| Company | Comment |
| --- | --- |

Setting 3:

QoS flow information list= QFI 1,2,3

DRB to flow mapping list = DRB1

Associated QoS flow list (of DRB1)= QFI 1,2,3

Q3: is setting 1 valid according to you? If yes which interpretation does it have:

- the QFIs 1,2,3 are proposed by source both for PDU session forwarding and DRB tunnel forwarding and target will decide between the two (interpretation 1)

- the QFIs 1,2,3 are only proposed for DRB tunnel forwarding, but they are present also in the QoS Flow Information List because this list comprises all the QoS flows which are proposed for forwarding by the source in general (interpretation 2).

| Company | Comment |
| --- | --- |

Setting 4

Qos flow information list= QFI 1

DRB to flow mapping list = DRB1

Associated QoS flow list (of DRB1)= QFI 1,2,3

Q4: is setting 4 valid according to you? If yes, which interpretation does it have:

- Target will decide between forwarding QFIs 1,2,3 over the DRB tunnel or forwarding QFI1 only over the PDU session tunnel (interpretation 1)

- Target must first try to set up the DRB forwarding tunnel for QFIs 1,2,3. Only if it doesn’t accept it can fallback by allocating a PDU session TEID (interpretation 2)

- Target should allocate both DRB and PDU session tunnels and source will decide after whether to send QFIs 1,2,3 over the DRB tunnel or whether to send the QFI1 over the PDU session tunnel. (interpretation 3)

| Company | Comment |
| --- | --- |

Setting 5

Qos flow information list= QFI 1,4

DRB to flow mapping list = DRB1

Associated QoS flow list (of DRB1)= QFI 1,2,3

Q5: is setting 5 valid according to you? If yes, which interpretation does it have ?

| Company | Comment |
| --- | --- |

Moderator’s summary:

Majority of companies think …

Proposal 2: TP...

# Second Round

Moderator’s summary:

Majority of companies think …

Proposal 2: TP...

# Conclusion

The following is proposed:

Proposal 1: TP...

# References

R3-214774, Correction of NG handover