3GPP TSG-RAN WG3 #114-e							R3-215830

1 - 11 Nov 2021

Online

Agenda Item:	9.3.6.1

Source:	ZTE - Moderator

Title:	Summary of Offline Discussion on CB: # 27_ReportIntervalMDT

Document for:	Approval

# Introduction

CB: # 27_ReportIntervalMDT

- Correct on the stage 3 specifications (Report Interval IE of M1 configuration) in RAN3 to align with RAN2?

- Provide CRs if agreeable

(ZTE - moderator)

Summary of offline disc R3-215830

Please Note:

Two rounds of discussion.

The first round email discussion is to be ended by Friday (24:00 UTC, 2021-11-05).

The second round email discussion is to be ended before the email deadline at second week (12:00 UTC, 2021-11-09).

# 2 For the Chairman’s Notes

Propose to capture the following:

# 3 Discussion (1st round)

In R3-214982, a misalignment issue between RAN3 (38.413/38.423) and RAN2(38.331) satge3 specifications is further discussed, with more considerations on the alignment throughout specifications and the necessity for backward compatibility. The proposed CRs for 38.413 and 38.423 are provided in [1] and [2].

the misalignment issue:

In RAN3 stage3 specifications (38.413/38.423), the value range of the Report Interval IE of M1 configuration is as below:

(ms120, ms240, ms480, ms640, ms1024, ms2048, ms5120, ms10240, min1, min6, min12, min30, min60)

However, as in the ASN.1 in 38.331, which is marked as the reference for report interval IE in 38.413/38.423, the value range of report interval is not aligned with that in RAN3 specifications.

ENUMERATED {ms120, ms240, ms480, ms640, ms1024, ms2048, ms5120, ms10240, ms20480, ms40960,

min1,min6, min12, min30 }

During last meeting, an old discussion about the stage2 and stage 3 misalignment on M4/M5 was mentioned. Regarding to that issue, an LS[3] has been sent to SA5 to ask about their opinion on the stage2 and stage3 misalignment issue, and we got the reply[4] from SA5 which said that stage3 specifications should be updated to match stage2 specification. After that a further reply[5] was sent to RAN2 to ask RAN2 about the feasibility about the feasibility of stage2 and stage 3 alignment. According to the history of the discussion on stage 2 and stage 3 misalignment issue, Moderator has noticed that there indeed exist misalignment issue throughout specifications. And it would be better that after we get the reply from RAN2, we fix the misalignment issue cross specifications completely.

Now come back to the misalignment issue in this CB, considering the reply from SA5, if the stage 3 specification of RAN2 is to be modified to match SA5, it means the ASN.1 in 38.331 has to be changed. This is not preferred at current time in standardization work.

To prevent the inconvenience of modifying the ASN.1 in RAN2, it is proposed that RAN3 stage 3 specifications should be corrected to align with RAN2, so that the ASN.1 in 38.331 would not be affected. For the potential stage 2 and stage 3 misalignment issue that might be raised because of this correction, SA5 can be notified to change the value range to align with RAN2 and RAN3, so that the misalignment issue for M1 report interval throughout specifications can be solved completely.

Q1: Do you agree that RAN3 should correct the value range of report interval IE in M1 configuration IE in 38.413 and 38.413,  to align with RAN2?

| Company | Yes/No | Comments |
| --- | --- | --- |

In the proposed CRs[1][2], the corrections are a bit different with the original versions submitted at last meeting. To be specific, the correction in the old CRs[6][7] are NBC, while in [1][2], a new IE named Extended Report Interval IE is introduced, as the extension of the Report Interval IE, for the 2 values that need to be added (ms20480, ms40960, ...).

Q2: Do you think the corrections in the proposed CRs are acceptable and can be agreed?

| Company | Yes/No | Comments |
| --- | --- | --- |

# 4 Conclusion, Recommendations

See section 2.

# 5 References

[1] R3-214983 Value range misalignment for Report Interval IE of MDT M1 configuration (NGAP)

[2] R3-214984 Value range misalignment for Report Interval IE of MDT M1 configruation (XnAP)

[3] R3-207222 LS to SA5 on MDT Stage 2 and Stage 3 alignment

[4] S5-206297 Reply LS on MDT Stage 2 and Stage 3 alignment

[5] R3-211140  Reply LS on MDT Stage 2 and Stage 3 alignment  To SA5, RAN2

[6] R3-213802  Misalignment value range for reportInterval IE of MDT(NGAP)

[7] R3-213803  Misalignment value range for reportInterval IE of MDT(XnAP)