3GPP TSG-RAN WG3 #114-e                                                                           R3-21xxxx

1-11 Nov 2021

Online

Title:	[DRAFT]  Reply LS on TCI State Update for L1/L2-Centric Inter-Cell Mobility to RAN3

Response to:	R3-214675/R1-2108527

Release:	Rel-17

Work Item:	NR_feMIMO-Core

Source:	ZTE (to be RAN3)

To:	RAN2,RAN1

Cc:

Contact Person:	Dapeng Li

E-mail Address:	li dot dapeng @ zte dot com dot cn

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

1. Overall Description:

RAN3 thanks RAN1 for LS on on Clarification on TCI State Update for L1/L2-Centric Inter-Cell Mobility. It is noted that potential RAN3 impact has been captured in NR_feMIMO-Core work as reflected in revised WID RP-211586. It is also noted that RAN3 has two meetings left in Rel-17 and has not TU allocated for this feature. Considering only the intra-DU scenario is supported in Rel-17 and the RRC models progress at RAN2 ( Option 1: Cell, Option 2: BWP, Option 3: beam resource (e.g. TCI state, QCL-info), Option 4: new structure (on high level similar to either of the other options) ), RAN3 would like to request feedback on the potential impact on signalling on e.g F1AP from point view from RAN1 and RAN2.

In addition, RAN3 is aware that the term “non-serving cell” is not used in RAN1/2, RAN3 would use the term “a TRP associated with a PCI different from that of the serving cell” instead of “non-serving cell” in inter-cell beam management.

2. Actions:

To RAN1 group.

ACTION: 	RAN3 kindly asks RAN1 to take the above information into consideration and provide the clarification.

To RAN2 group.

ACTION: 	RAN3 kindly asks RAN2 to take the above information into consideration and provide the clarification regarding expected signalling impacts.

3. Date of Next RAN3 Meetings:

3GPP RAN3#115-e		Feb 21-25  2022

3GPP RAN3#115bis-e	April 04-08 2022