3GPP TSG-RAN WG3 #114-e                                                                           R3-21xxxx

1-11 Nov 2021

Online

Title:	[DRAFT]  Reply LS on TCI State Update for L1/L2-Centric Inter-Cell Mobility to RAN3

Response to:	R3-214675/R1-2108527

Release:	Rel-17

Work Item:	NR_feMIMO-Core

Source:	ZTE (to be RAN3)

To:	RAN1, RAN2

Cc:	RAN4

Contact Person:	Dapeng Li

E-mail Address:	li dot dapeng @ zte dot com dot cn

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

1. Overall Description:

RAN3 thanks RAN1 and RAN4 for LS on on Clarification on TCI State Update for L1/L2-Centric Inter-Cell Mobility. RAN3 is aware that the term “non-serving cell” is not used in RAN1/2. However, from the RAN4 LS (R3-214702/R4-2115357), RAN3 understands that a non-serving cell is a neighbour cell with a different PCI from serving cell and that a UE can be scheduled data on both serving and non-serving cells. RAN3 would like to clarify that the understanding derived from the reply LS from RAN4 is correct also for RAN1. Meanwhile, RAN3 would use the term “a TRP associated with a PCI different from that of the serving cell” instead of “non-serving cell” in inter-cell beam management.

On the other hand, it is noted that potential RAN3 impact has been captured in NR_feMIMO-Core work as reflected in revised WID RP-211586. It is also noted that RAN3 has two meetings left in Rel-17 and has no TU allocated for this feature. As agreed in RAN3, only the intra-DU scenario is supported in Rel-17. However,  the RRC models ( Option 1: Cell, Option 2: BWP, Option 3: beam resource (e.g. TCI state, QCL-info), Option 4: new structure (on high level similar to either of the other options) ) is still under discussion in RAN2. Considering the remaining time of Rel-17, RAN3 would like to request feedback on the conclusions with potential impact to RAN3 e.g., F1AP signaling, from viewpoint of RAN2.

2. Actions:

To RAN1 group.

ACTION: 	RAN3 kindly asks RAN1 to take the above information into consideration and provide the clarification on the understanding of RAN4’s reply LS and terminology used in RAN3.

To RAN2 group.

ACTION: 	RAN3 kindly asks RAN2 to take the above information into consideration and provide the feedback regarding expected RAN3 impacts.

3. Date of Next RAN3 Meetings:

3GPP RAN3#114bis-e		Jan.17~26, 2022

3GPP RAN3#115-e	Feb. 21~Mar. 3, 2022