3GPP TSG-RAN WG3 #114-e	R3-215833

Online, 1-11 November 2021

Agenda Item:	9.3.6.1.

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on CB: # 30_PositionCorrections

Document for:	Approval

# Introduction

CB: # 30_PositionCorrections - Check the details (HW - moderator) Summary of offline disc R3-215833

It is propose to check directly if there is any objection or comment on the proposal

The moderator will provide an update 5th Friday afternoon UTC, pending to responses, please if possible provide a first feedback before. Otherwise the official deadline for comment is 9th Tuesday 12 UTC.

# For the Chairman’s Notes [TBC]

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion [if needed]

## LCS to GCS Translation alignment

The correction is to align the LCS to GCS Translation IE, on ASN.1 as sequence, not a list as currently define, and introduce the new IE in procedure text (already in ASN.1). That correction will impact the  rel-17 BL CRs

Q3-1-1. Should the CRs, on LCS to GCS Translation alignment R3-215385 and R3-215386 [1, 2], be agreed?

If not, please clarify why.

If yes, and some minor revisions are needed please provided its in the table, if not minor please provide a draft correction in tracking change in the dedicated folder.

| Company | Comment |
| --- | --- |
| Ericsson | For R3-215386, the IE tabular should be 9.3.1.x. It can be fixed however during the spec implementation by MCC |
| Huawei | Yes Ericsson is correct, we can provide revision also … |
| Nokia | No, this is non-essential (tabular alignment with asn.1). There have been several such CRs discussed online at this meeting for various specs, which have all been considered non-essential – so we should handle such changes consistently. These changes could be added to either the rapporteur CRs or the Rel-17 NR_pos enh BL CRs. Regarding the changes themselves, the “>” can be removed in front of the sub-IEs. |
| Qualcomm | Our comment on reviewing was similar to Nokia’s, this is quasi-editorial, and definitely not essential. During rel-16 several of these were seen in many TPs, some other corrected by the editors, some not. A thorough clean-up of this type of issue would probably keep RAN3 busy for the equivalent of a meeting. But we would be ok for the rapporteurs to try to fix these as part of rel-17 rapporteur work. |

## ASN.1 correction and alignment in tabular

The CR propose to correct the name of some IEs in ASN.1 and correct the list format by make it clear the conditional presence of the list and the length of the list.

Q3-2-1. Should the CRs, on ASN.1 correction and alignement in tabular R3-215387 [3], be agreed?

If not, please clarify why.

If yes, and some minor revisions are needed please provided its in the table, if not minor please provide a draft correction in tracking change in the dedicated folder.

| Company | Comment |
| --- | --- |
| Ericsson | Thank you for the throughout inspection. We remark that some Quantities and Items IEs need to be in bold. We dropped a new revision in the folder with this format change. |
| Huawei | Yes, agreeable We will provide update as proposed by Ericsson, thanks! |
| Nokia | This is also non-essential (tabular alignment with asn.1). We also note that similar issues (e.g. not showing the “Item” level in the tabular) exist in other specs (e.g. S1AP, LPPa) for many years without any concerns. In fact, some of these NRPPa issues were likely copy/pasted from LPPa. Some specs are mostly consistent on how lists are shown in the tabular, and some specs are not… NRPPa is one of the specs (along with LPPa, S1AP) that is not consistent. Some changes could be added to the Rel-17 rapporteur CR, but most of the cleanup comes 15 months too late. |
| Qualcomm | Similar comment to the first one. It was clear in rel-17 that TPs were all over the place in this respect, and specs in general are not all aligned. Again, fine with trying to fix some/all as part of rel-17 rapporteur work. |

## PRS-only TP

RAN2 introduced the the PRS-only TP signaling from LMF to UE, the pending signaling is missing in NRPPa/F1. The CRs have been revised to allow all type of TRP report as specified in TS 38.305

Q3-3-1. Should the CRs, on Correction on PRS-only TP revised in R3-215914 and R3-215915 [6, 7], be agreed?

If not, please clarify why.

If yes, and some minor revisions are needed please provided its in the table, if not minor please provide a draft correction in tracking change in the dedicated folder.

Description…

| Company | Comment |
| --- | --- |
| Ericsson | We support, but we cannot find the tdocs numbers in the FTP website? |
| Huawei | Thanks for spotting this Tdocs are available in R3-215914/ R3-215915 agreeable |
| Nokia | OK |
| Qualcomm | We support and would be happy to co-sign since we mentioned the need to generalize offline. For fun: should this be a separate IE in tabular ? |
| ZTE | Agree |

## SRS configuration

The max value of some list in the SRS configuration are not correct.

Please note that the similar change is proposed in the NRPPa rapporteur correction in R3-215421

Q3-4-1. Should the CRs, on Correction on SRS configuration in  R3-215645 [8], be agreed?

If not, please clarify why.

If yes, and some minor revisions are needed please provided its in the table, if not minor please provide a draft correction in tracking change in the dedicated folder.

| Company | Comment |
| --- | --- |
| Ericsson | This is already part of NRPPa rapporteur correction in [9]. We suggest taking it there. |
| Huawei | Slight preference to see it as correction, we can accept majority or rapporteur view. |
| Nokia | Please include in rapporteur CR. |
| Qualcomm | Does look more like rapporteur CR, but no strong opinion. |
| ZTE | Fine for us to put it into the rapporteur CR. |

# Conclusion, Recommendations [TBC]

If needed

# References

R3-215385, LCS to GCS Translation alignment (Huawei, Ericsson)

R3-215386, LCS to GCS Translation alignment (Huawei, Ericsson)

R3-215387, ASN.1 correction and alignement in tabular (Huawei, Ericsson)

R3-215388, Correction on PRS-only TP (Huawei, CMCC, Ericsson)

R3-215389, Correction on PRS-only TP (Huawei, CMCC, Ericsson)

R3-215914, Correction on PRS-only TP (Huawei, CMCC, Ericsson)

R3-215915, Correction on PRS-only TP (Huawei, CMCC, Ericsson)

R3-215645, Correction to TS38.455 on SRS configuration (ZTE Corporation)

R3-215421, NRPPa Rapporteur Corrections (Ericsson)