3GPP TSG-RAN WG3 Meeting #114-e	R3-215289

# Online, Nov 1st – Nov 11th 2021

Agenda Item:	31.2.1

Source:	Ericsson (moderator)

Title:	Summary of Offline Discussion on Local NG-RAN Node Identifier

Document for:	Approval

# Introduction

CB: # 34_LocalNG-RANnode_Identifier

- Solution 2 is used for the flexible I-RNTI partitioning? The length of local node identifier is self-contained in the I-RNTI? The length value of Local NG-RAN node ID is specified? ZTE

- Introduce an I-RNTI structure for NG-RAN node disambiguation, where the MSB of an I-RNTI indicates a I-RNTI profile. An NG-RAN node is associated to one I-RNTI profile and an I-RNTI profile indicates a specific split of bits for Local gNB ID and Inactive UE Context? A node associated to a certain I-RNTI profile can use multiple Local gNB ID? E///

- Prefer Solution 4b, if Solution 4b cannot be agreed then down-select solution 1 at this meeting? Nok

- Combine option2 and option 4a? HW

(E/// - moderator)

Summary of offline disc R3-215837

Due to changes in some of the solutions, Solution 4 is renamed and split into two schemes, i.e., Solution 4a and 4b as depicted in section 3.

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Solutions proposed in RAN3#114e

The following working assumption has been reached from last meeting:

WA: Down-selection will be based on the listed criteria above. Solution 3 might be considered as a potential enhancement in the next step.

Companies have been encouraged to provide detailed technical analysis on the solutions based on at least the following criteria:

- Minimum configuration effort via OAM

- Flexibility in allocation of maximum number of Inactive UE contexts per NG-RAN node

- Capacity aspect: the number of Inactive UE contexts supported in the network

- Minimized number of signaling exchanges between neighbor nodes via Xn:

  - For initial ID exchange between nodes

  - After an ID change (this may also cover the case that the maximum number of inactive UE contexts has been changed) or addition of another ID for a node

  - For conflict resolutions in case neighboring nodes use the same IDs

- Interoperability between vendors

- Support for RAN sharing

So far, total 5 individual solutions (some of them having been refreshed) have been proposed on how to disambiguate a NG-RAN node from I-RNTI, and some proposals combine aspects of the individual solutions.

One thing to note, the refreshed Solution 4 has discrepancy with the one proposed in last meeting, i.e., the ID length is changed from flexible length to fixed length, at the same time there is other proposal referring to the previous version for combination. Hence we have to rename them as Solution 4a and 4b to avoid all kinds of mixing.

Solution 1: Multiple Local gNB Identifiers per NG-RAN node.

This solution is summarized and presented in [4][5].

- the I-RNTI is encoded as follow:

  - a fixed number of bits, common for all nodes, to encode a UE Context Identifier

  - a fixed number of bits, common for all nodes, to encode a Local gNB ID

- A NG-RAN node can allocate multiple Local gNB IDs.

- The Local gNB Identifiers are selected randomly, and exchanged between NG-RAN nodes.

- Each RAN node communicates its own local identifiers to its neighbour RAN nodes and updates them when change occurs.

Solution 2: One Local gNB Identifier with I-RNTI profile per NG-RAN node.

This solution is summarized and presented in [1][2][3].

- The I-RNTI is encoded as follows

  - A fixed number of bits is used, for all nodes in the network, to identify an I-RNTI profile, 2 bits for full I-RNTI (4 profiles), 1 bit for short I-RNTI (2 profiles)

  - One Local gNB ID is assigned per NG-RAN node

  - For each I-RNTI profile identifier, a fixed number of bits is used to encode a Local gNB ID

  - For each I-RNTI profile identifier, a fixed number of bits is used to encode a UE Context Identifier

- The Local gNB Identifiers are selected randomly, and exchanged between NG-RAN nodes.

- Each RAN node communicates its own local identifier to its neighbor RAN nodes and updates them when change occurs.

Solution 3: Up to 6 Local NG-RAN node identifiers per NG-RAN node.

- Multiple (up to 6) Local gNB IDs can be maintained in one NG-RAN node at the same time.

- An old Local gNB ID is released when all the inactive UEs with the old local node identifier are relocated or released.

- A list of Local gNB IDs is signaled between NG-RAN nodes.

Solution 4a: One Local gNB Identifier with undefined length per NG-RAN node.

This solution is summarized and presented in [8][9].

- The Local gNB Identifier is assigned corresponding to the first leftmost bits of I-RNTI values which it allocates.

- The NG-RAN node selects a Local gNB ID which doesn’t match any MSB of a neighbour NG-RAN node or a neighbour of neighbour NG-RAN Node.

- The Local gNB Identifiers and global gNB Identifiers are exchanged between NG-RAN nodes.

Solution 4b: One Local gNB Identifier with fixed length per NG-RAN node.

This solution is summarized and presented in [6][7].

- One Local gNB Identifier of size 22 bits in case of full I-RNTI and 8 bits in case of short I-RNTI is assigned per NG-RAN ode locally and exchanged over Xn

- The Local gNB Identifiers and global gNB Identifiers are exchanged between NG-RAN nodes.

Solution 5: Simplified I-RNTI profiles, i.e., one Local gNB Identifier with I-RNTI profile per NG-RAN node.

This solution is summarized and presented in [4][5].

- The I-RNTI is encoded as follows

  - One bit is used, for all nodes in the network, to identify an I-RNTI profile. This applies to both full I-RNTI and short I-RNTI.

  - One Local gNB ID of up to 22 bits in case of full I-RNTI and up to 8 bits for short I-RNTI is assigned per NG-RAN node, with the possibility to add more Local gNB IDs (up to 6) if needed for capacity reasons
Comment DT: In [4] 2 profiles with different length are mentioned (high/low capacity), i.e., with 22 or 12 bits for Local gNB ID.

  - For each I-RNTI profile identifier, a fixed number of bits is used to encode a Local gNB ID

  - For each I-RNTI profile identifier, a fixed number of bits is used to encode a UE Context Identifier

- The Local gNB Identifiers are selected randomly, and exchanged between NG-RAN nodes.

- Each RAN node communicates its own local identifiers to its neighbor RAN nodes and updates them when change occurs.

Solution 3 is greyed out based on the WA. Since we do see some analysis is given, it is optional to provide inputs to Sol 3 in the following feedback forms. Just keep in mind Sol 3 supposes not to be the basic mechanism to solve the conflict. Hereafter “each solution” in the following comparison refer to at least Solution 1, 2, 4b, 5, and 2+4a.

## Evaluation based on the criteria

### Criteria 1

Companies are invited to provide their view on each solution based on the following criteria.

- Minimum configuration effort via OAM

* If the field is left blank, it would be assumed that the company agrees no issues by default.

| Company | Evaluation |
| --- | --- |
|  | Sol 1 | Sol 2 | Sol 4b | Sol 5 | Sol 2+4a | Sol 3 |
| Deutsche Telekom | Minimum or no effort! Just number of bits used for long and short I-RNTI for all RAN nodes has to be set by OAM (if not fixed in specs, but this would not allow any flexibility for operators) | Minimum effort! The profile for each RAN node has to be set by OAM | No effort! Fixed number set in specs | Minimum effort! Same as Sol 2 | Minimum or no effort! [8] states that local gNB ID length is set by gNB locally or by OAM based on e.g. the node type and capacity |  |
| E/// | No effort Fixed length does not need OAM configuration. | Low effort OAM configuration may be used to set initial value of I-RNTI profile and update. | No effort Same as Sol1 | Low effort Same as Sol2 | High effort First operators need to coordinate on which way to go between two solutions though both are used for same purpose. Second, in Sol 4a if the Local gNB ID is obtained from Global gNB ID, there is a configuration/coordination effort required to ensure that the “X” MSB of Local gNB ID will not conflict with the “X” MSB of Local gNB ID of a neighboring Node. In addition, since the length of Local gNB ID is unkwoen at a gNB when analysing an I-RNTI received at Resume. This will even need more coordination efforts. |  |

### Criteria 2

Companies are invited to provide their view on each solution based on the following criteria.

- Flexibility in allocation of maximum number of Inactive UE contexts per NG-RAN node

* If the field is left blank, it would be assumed that the company agrees no issues by default.

| Company | Evaluation |
| --- | --- |
|  | Sol 1 | Sol 2 | Sol 4b | Sol 5 | Sol 2+4a | Sol 3 |
| Deutsche Telekom | Limited flexibility! Max number of UE contexts can be increased by adding more IDs per node. No flexibility possible between node types due to fixed length for all nodes. | (Possibly) Best flexibility! Flexibility based on number of profiles to be specified. Tradeoff to be found as increased flexibility results in loss of bits for IDs! Each node can be adapted separately. | No flexibility! Same as Sol 1 but w/o possibility to assign more IDs per node. | Between best and limited flexibility! Similar to Sol 2 with 2 profiles, but possibility to extend max number by adding more IDs per node. | Best flexibility! But seems complex from avoiding ID clashes between neighbors. |  |
| Huawei |  |  |  |  | ID clashes between neighbour nodes are the same for all options. This aspect is not addressed yet in current discussion. |  |
| E/// | Supported Maximum number of inactive UE context varies with the number of Local gNB IDs in use. | Supported | Not supported | Supported | Supported with high complexity |  |

### Criteria 3

Companies are invited to provide their view on each solution based on the following criteria.

- Capacity aspect: the number of Inactive UE contexts supported in the network

* If the field is left blank, it would be assumed that the company agrees no issues by default.

| Company | Evaluation |
| --- | --- |
|  | Sol 1 | Sol 2 | Sol 4b | Sol 5 | Sol 2+4a | Sol 3 |
| Deutsche Telekom | This question is related to criteria 2, i.e., see answers above. Exact numbers, if required, should be given by proponents. |  |
| E/// | depends on the agreed split of bits The max numbers of UE Contexts depends on the number of Local gNB IDs for one node. Example, with split (UE Context / Local gNB ID) of 16/24 bits: 65536 users supported with 1 Local gNB ID, 1M users supported with 16 Local gNB IDs. | Max 67 M users per node Each I-RNTI profile has a corresponding maximum number of Inactive UE Context. | Up to 262k users per node | Max 268M users per node 1 Local gNB ID | Either the max number in Sol 2 or max 268M users per node as in Sol 4a |  |

### Criteria 4

Companies are invited to provide their view on each solution based on the following criteria.

- Minimized number of signaling exchanges between neighbor nodes via Xn:

  - For initial ID exchange between nodes

  - After an ID change (this may also cover the case that the maximum number of inactive UE contexts has been changed) or addition of another ID for a node

  - For conflict resolutions in case neighboring nodes use the same IDs

* If the field is left blank, it would be assumed that the company agrees no issues by default.

| Company | Evaluation |
| --- | --- |
|  | Sol 1 | Sol 2 | Sol 4b | Sol 5 | Sol 2+4a | Sol 3 |
| Deutsche Telekom | Should be set by proponents of solutions, especially w.r.t. conflict resolution. For initial exchange or after ID change the behavior should be very similar except that for Sol 1 and Sol 5 several IDs have to be exchanged per node, if assigned. |  |
| E/// | Medium For initial ID exchange and ID update, one message including one or more IDs is sent to direct neighbouring nodes. For conflict resolution, one message with one new ID will be sent to direct neighbouring nodes. | Low For initial ID exchange and ID update, one message including one ID is sent to direct neighbouring nodes. For conflict resolution, one message with one new ID will be sent to direct neighbouring nodes. | Low Same as Sol2 | Low Same as Sol2 | Possibly high As said, multiple gNBs can use Local gNB ID at different lengths for which the “X” MSB of the respective Local gNB IDs are the same. |  |

### Criteria 5

Companies are invited to provide their view on each solution based on the following criteria.

- Interoperability between vendors

* If the field is left blank, it would be assumed that the company agrees no issues by default.

| Company | Evaluation |
| --- | --- |
|  | Sol 1 | Sol 2 | Sol 4b | Sol 5 | Sol 2+4a | Sol 3 |
| Deutsche Telekom | Supported if ID length set by OAM or spec | Supported | Supported | Supported | Still unclear from given information |  |
| Huawei |  |  |  |  | Interoperability between vendors is supported definitely, because it’s from sol 2 and 4a. |  |
| E/// | Supported | Supported | Supported | Supported | Not supported Unclear when an operator needs to use a common length for Local gNB ID across its network. |  |

### Criteria 6

Companies are invited to provide their view on each solution based on the following criteria.

- Support for RAN sharing

* If the field is left blank, it would be assumed that the company agrees no issues by default.

| Company | Evaluation |
| --- | --- |
|  | Sol 1 | Sol 2 | Sol 4b | Sol 5 | Sol 2+4a | Sol 3 |
| Deutsche Telekom | Supported | Supported | Supported | Supported | Still unclear from given information |  |
| Huawei |  |  |  |  | RAN sharing is supported definitely, because it’s from sol 2 and 4a. |  |
| E/// | Supported | Supported | Supported | Supported | Unclear All the operators within network have to agree on which solution to go and which length to use. |  |

### Others

Any other business

| Company | Comment |
| --- | --- |

## Overall assessment – for 2nd round

TBC based on the above comparison

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-214740 Discussion on I-RNTI partitioning (ZTE, Radisys, Reliance JIO, China Telecom)

R3-214741 Support flexible I-RNTI partitioning (ZTE, Radisys, Reliance JIO, China Telecom)

R3-214742 Support flexible I-RNTI partitioning (ZTE, Radisys, Reliance JIO, China Telecom)

R3-214763 Node Identifier for RRC Inactive (Ericsson)

R3-214764 Addition of Local gNB IDs per NG-RAN node [RRCInactive] (Ericsson)

R3-214820 Down-Selection of Local NG-RAN node Identifier solutions (Nokia, Nokia Shanghai Bell)

R3-214821 Support of Local NG-RAN node Identifier [Local_Node_ID] (Nokia, Nokia Shanghai Bell)

R3-215030 Discussion on Local NG-RAN Node Identifier (Huawei)

R3-215031 Local NG-RAN Node Identifier (Huawei)