3GPP TSG-RAN WG3 #114-e	R3-215909

Electronic Meeting, Nov 1th – 11th, 2021

Agenda Item:	18.4.1

Source:	ZTE (moderator)

Title:	Summary of CB: # AIRAN3_ESSolution

Document for:	Approval

# Introduction

CB: # AIRAN2_ES

- Discuss the solution, input/output, standard impacts

- Merging any agreement parts; provide TP if agreeable

- Capture agreements and open issues

(ZTE - moderator)

Summary of offline disc R3-215909

Two phases of this email discussion:

- Phase 1 Deadline: 12:00AM UTC, 5th Nov.

- Phase 2 Deadline : 6:00AM UTC, 9th Nov, we will try to come up with agreeable TP in the 2nd phase discussion before online session, if needed.

# For the Chairman’s Notes

Propose the following:

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

## Overall structure for AI/ML-based energy saving

[4] put forward the overall structure for AI/ML-based energy saving, which describes that AI-based energy saving follows a unified process regardless of which solutions to make the solution much clear and comprehensible as shown below.

Figure 1. Overall structure of AI-based energy saving

- Data collection is mainly responsible for the data collection, and required data is used to energy saving including current energy information, resource status of ES-cell and neighboring cells, even weather or other required information as input.

- AI-generated information includes load prediction, energy prediction, trajectory prediction, scenario classification or other required information generated by AI/ML model.

- Energy saving decision generation is to generate the energy saving decision based on the input from data collection, and refined input data. AI/ML model can also be used to make energy saving decision.

- Energy saving decision execution is to update the configuration based on the energy saving decisions and execute the decision.

Question 1-1: Companies are invited to provide their views on whether to capture the figure above into the TR, any refinement if yes.

| Company | Yes/No | Comments |
| --- | --- | --- |
| Huawei | No | It seems that this is trying to refine each function block, but we are talking about solutions, so anyway we will have texts about e.g. what the collected data include, what the output of inference could be, etc. And, with this picture, seems we also need to give mapping between this figure and the framework figure? We are making things complicated. |
| Lenovo, Motorola Mobility | Yes | It looks good in general, we can further check when finalizing the TP. |
| Deutsche Telekom | Yes, but … | We are in principle ok to add such figure, but we share a similar view as Huawei. What is missing, is a mapping/explanation how the functional blocks in the figure correspond to the functional framework under definition. Furthermore, some parts are still unclear. E.g. the model inference function is not visible, it seems that data collection creates the AI output. Performance feedback is noted in the figure, but it this the “Feedback” in the functional framework? Why does it go to the block with AI generated information, why not to data collection? More discussion on details is needed. |
| Futurewei | No | We don’t see the needs and benefits for such an overall structure. The structure for network energy saving already exists. AI/ML just provides information from another aspect for decision making. Some functions blocks, such as the “Energy Saving Decision Generation”, are implementation dependent and do not need to be standardized. We believe the current discussions on input, output and feedback are enough. |

## AI/ML Training and Inference deployment

In the last meeting, two options were agreed to captured into the TR:

- Model Training at OAM and Model Inference at NG-RAN

- Model Training and Model Inference at NG-RAN

[1] support Model training is located at OAM and model inference is located at NG-RAN considering there is no requirement for real-time energy saving decision at this time. Moderator think this solution is already captured into the TR.

[9] proposes that NG-RAN node should be able to perform online model training based on the AI/ML model received from OAM. With continuous online training at NG-RAN node, the deployed model can be continuously evolved and improve its accuracy for performance improvement.

Question 2-1: Companies are invited to provide their views on whether to clarify that Model Training is online training or offline training in the TR.

| Company | Comments |
| --- | --- |
| Huawei | Yes, we think we have to do that, technically offline training and online training are of quite different requirements as far as data storage is concerned, while data storage is our of RAN scope. |
| Lenovo, Motorola Mobility | It would be beneficial to clarify what is really online training and offline training. Maybe it can be discussed based on exact solution. Besides, online training and offline training sounds different AI algorithm categories, not sure if we want to touch that in the TR. |
| Deutsche Telekom | In principle, both offline and online training are feasible, but they are used in different parts of model LCM. We would assume that usually (initial) offline training is done in OAM before deploying the model to inference function in RAN. Online training in RAN depends on model and learning method applied. This should be explained for use case under consideration, here ES. |
| Futurewei | We would like to point out that both online training and offline training are training functions (note we don’t have definitions for either of them). Therefore, contribution [9] essentially proposed the third deployment scenario, i.e., model training at both OAM and NG-RAN, model inference at NG-RAN. It is OK if a vendor chooses to do it, but we don’t think there would be standards impacts for this implementation scenario because the current two implementation options have covered the input, output and feedback needs for this scenario. Therefore, we believe whether a RAN node wants to support continuous online training can be left to implementation or something like that. This AI can move forward with the 2 options we have already agreed upon. We would also like to note that this new deployment scenario was proposed to the high-level framework AI (18.2). So, we need to wait until a decision is made in that discussion before we discuss this item in 18.4.1. |

[7] proposes to consider the different deployment solutions of model training and model inference modules in the split architecture base station and two solutions in CU/DU architecture are proposed below:

- Solution #1: Model training and model inference at CU side

- Solution #2: Model training at CU and model inference at DU

Question 2-2: Companies are invited to provide their views on whether the Solution #1, Solution #2 or both, is preferred to be captured into the TR.

| Company | Solution#1, or Solution#2, or both | Comments |
| --- | --- | --- |
| Huawei | Solution#1, but | We think CU should have more knowledge than DU, and DU could provide what is needed by CU. But we suggest to focus on the gNB and OAM case first, i.e. where the model training is at OAM and model inference is at gNB. When this solution is clear, we can discuss the CU/DU split case. |
| Lenovo, Motorola Mobility | Solution#1, and Solution#2 | Depending on the energy saving strategy, if it is beam/cell level energy saving, it could be DU to infer and decide, otherwise it could be up to CU to infer and decide. |
| Deutsche Telekom | Both | Where to place training and inference is strongly dependent on use case and underlying approach to collect which data and to adapt which parameters. We wouldn’t expect to have offline training in RAN nodes, especially not in DU, just online training might be useful. |
| Futurewei | Solution#1 | We would like to note that to enable model inference at DU there will be impact on F1 interface, which will complicate the specifications. |

## Inputs of AI/ML-based Network Energy Saving

Following information as input for AI/ML-based network energy saving are summarized based on contributions:

Input Information from Local node:

- UE mobility/trajectory prediction [3][4][6]

- Energy efficiency gain or energy state [9]

Input Information from UE:

- Location history (e.g., coordinates, serving cell ID), UE historical serving cells and their locations [3]

- UE moving velocity [3]

- UE assistance information with mobility prediction [8]

- UE assistance information with UL/DL traffic prediction [8]

Input from neighboring NG-RAN nodes:

- Past handover performance information [3]

- UE performance after handover [3]

- Energy efficiency gain or energy state [9]

Question 3-1: Companies are invited to provide their views on whether the above input information listed could be used for AI/ML-based Network Energy Saving.

| Company | Comments |
| --- | --- |
| Huawei | Input information from local node: 1: OK. 2: Prefer to use the energy efficiency that reflects the real performance of the RAN node we want to evaluate. Input information from UE: 3/4: No. It could be derived from the “UE history information from UE” IE, which is already there in the local node. 5/6: OK. Input from neighboring NG-RAN node: 7: Nice to have. HO history/HO successful rate could be used as reference for future HO decision, . 8: OK. 9: Prefer to use the energy efficiency that reflects the real performance of the RAN node we want to evaluate. |
| Lenovo, Motorola Mobility | 1: ok 2: ok 2a: ok 3, 4: look like input to predict UE mobility/trajectory, not sure if they can be really regarded as input for energy saving. 5, 6: no, they assume UE capability to perform some kind of prediction, shall be avoided for now. 7,8: not sure if they care useful for energy saving, they look like feedback information. 9: not sure, and looks like feedback information. |
| Futurewei | In general, we agree with the above inputs. But we need to define what the “Energy efficiency gain or energy state” is; we can do it in the WI phase. |

[1] propose to define load prediction function, and UE mobility trajectory prediction if needed by AI-based network energy saving as a kind of tool-box to discuss.

Question 3-2: Companies are invited to provide their views on whether to regard load prediction or UE mobility trajectory prediction as a too-box use case to discuss.

| Company | Yes or No | Comments |
| --- | --- | --- |
| Huawei | Not sure | It was discussed before many times. On one hand, we understand that probably prediction will be used for different use cases; on the other hand, we think the study should focus on the energy saving, load balancing and mobility optimization. What does the toolbox use case mean exactly here, what are the additional spec impacts, in addition to normal collected data and the detailed value of prediction (to be discussed during WI phase I guess) |
| Lenovo, Motorola Mobility | Yes | RAN node may decide to turn off some cell if the predicted load is low and UEs will leave the cell. |
| Futurewei | Yes | A toolbox approach can avoid duplicate specifications/implementations among different use cases. |

## Output of AI/ML-based Network Energy Saving

Following information as input for AI/ML-based network energy saving are summarized based on contributions:

- UE mobility prediction, which can be used to help making handover decisions. [3]

- Recommended Energy saving Strategies including, recommended cell activation/deactivation, symbol shutdown, channel shutdown, carrier shutdown, deep sleep [4][5]

- Predicted energy information, including predicted energy consumption information [4]

- Energy efficiency [6]

- Action level, action type [5]

- Predicted energy state (e.g. Active, High, Low, Inactive) [9]

- Validity time of energy strategy [5] [9]

- Energy saving strategies [9]:

  - Update of SSB periodicity

  - Update of the advertised Bandwidth (use Bandwidth Part Adaptation (BPA) feature

  - Update of DTX for BS

  - Update of the SIB blocks periodicity

  - Use wake-up signaling features/DRX features to increase the number of UEs in sleep mode, depending on traffic patterns

  - Secondary cell activation/deactivation

  - Carrier aggregation turn-on/off

  - Primary/Macro cell activation/deactivation

  - Dual connectivity turn-on/off

Question 4-1: Companies are invited to provide their views on whether the above output information listed could be used for AI/ML-based Network Energy Saving.

| Company | Comments |
| --- | --- |
| Huawei | 1: No. The output should be highly related to the energy saving. The UE mobility prediction should be the input, but not the output. 2: OK. The recommended cell activation/deactivation is OK. Others could also be considered, but not sure if some of them could be exchanged between base stations. 3: No. Prefer to use the energy efficiency that reflects the real performance of the RAN node we want to evaluate. 4: OK. 5: Could consider, but it seems that they are implemented mechanism and not sure if could be transferred via interface. 6: Could consider. But we prefer to use the energy efficiency that reflects the real performance of the RAN node we want to evaluate. 7: No. As discussed in our paper, there is no need to include the validity time together with the output information every time. 8: Not sure if we should agree or disagree each of them, some of them seems straightforward, e.g. activation/deactivation; some of them seems unclear, e.g. update of the advertised Bandwidth, etc, some of them seem to be implemented mechanism and cannot be transferred via interface. Maybe there is no need to go into such details during study item phase, this comment also applies to other use case. |
| Lenovo, Motorola Mobility | 1: we understand mobility prediction will help with energy saving not the other way around. 2,3: ok, need to discuss how to define energy consumption. 4: not sure,, is it a predicted energy efficiency? Otherwise it can be easily measured. 5: need a bit more elaboration 6: intention is ok 7: no, NW can update the energy strategy when it wants. We don’t see the need of a validity time. 8: ok in general |
| Futurewei | Yes. This information could be used as output of the network energy saving function. However, the exact outputs of the network energy saving function and the details need to come from thorough discussion of the group. For example, some of the outputs or decisions, like 2 and some items under 8, would need to be communicated to DUs for CU/DU split scenario if inference is on CU. |

## Performance feedback for the AI/ML-based Network Energy Saving

Following information as feedback information for AI/ML-based network energy saving are summarized based on contributions:

- UE performance after handover [3]

- UE transmission performance measurement [6]

- Resource status of neighboring NG-RAN node [9]

- Energy information efficiency or energy state [9]

Question 5-1: Companies are invited to provide their views on whether the above feedback information listed could be used for AI/ML-based Network Energy Saving.

| Company | Comments |
| --- | --- |
| Huawei | 1/2: OK. They should be the same, e.g., the packet loss rate performed by the target node, or the packet delay performed by the UE. 3: OK. 4: OK, prefer to the energy efficiency. |
| Lenovo, Motorola Mobility | 1. it may only apply to switching off a cell leading to a handover of one UE 2. ok 3. not sure 4. ok |
| Deutsche Telekom | Unclear what is meant by “performance feedback”. In the functional framework we have “Feedback” and “Model Performance Feedback (FFS)”. I would assume “Feedback” is the basis for this question, correct? Ok to all, but with respect to (4) there is a need to clarify the meaning of metrics. What is meant by “Energy information efficiency” compared to “Energy efficiency” or “Energy efficiency gain” mentioned in some other questions before. |
| Futurewei | We agree in general. Note Item 1 and 2 may mean similar things. Also Item 4 should read “Energy information efficiency” instead of “Energy efficiency information” and the definition of “energy efficiency” has to be officially defined and agreed. |

## Procedures

[2] proposes that an NG-RAN node should be able to accept/reject energy saving decision proposals in a neighboring NG-RAN node. And [5] proposes that the predicted energy saving strategy can be exchanged with neighbor cells to provide reference information for optimization decisions.

[5][9] mentioned that predicted resource status reporting can be embedded into existing resource status reporting procedure, and [5] also stated that that can be supported by designing a new procedure referring to the existing resource status reporting procedure. In addition, [9] propose that the target NG-RAN node can stop providing feedback to the source NG-RAN node if the handed-over UE is no longer available at the target NG-RAN node.

Question 6-1: Companies are invited to provide their views on the proposals below:

- Predicted energy saving strategy shall be exchanged between NG-RAN nodes

- Use existing resource status reporting procedure or to define a new one to exchange predicted resource status

| Company | Comments |
| --- | --- |
| Huawei | Not sure. For 1, we think the predicted energy saving strategy is just a predicted info which is not a real decision, what we need is real energy saving decision informed to neighbours; then for 2, we could leave this discussion to normative phase. |
| Lenovo, Motorola Mobility | 1. don’t understand the motivation, first, why one needs to predict energy saving strategy? Secondly, why need to inform the other RAN node? 2. we consider it useful for load balancing use case, not sure why it is needed for energy saving, maybe as feedback information, maybe they are nested. |
| Deutsche Telekom | (1) The meaning of the content of predicted energy saving strategy has be further clarified. For some issues like cell switch on/off it makes certainly sense. For (2) no clear preference. Both alternatives are feasible. Can be decided in WI phase. |
| Futurewei | 1. We don’t think this is necessary. 2. We are restricted from defining a new reporting procedure. We can reuse existing resource status reporting procedure to exchange predicted resource status with neighboring cells. Defining a new procedure is considered out of scope for this R17 SI. |

[3] also mentioned that following information should be considered to be exchanged over Xn interface.

•	Notice of entering sleep mode (optional)

•	Wake-up signal (optional)

Question 6-2: Companies are invited to provide their views on the proposal above?

| Company | Comments |
| --- | --- |
| Huawei | The intention makes sense, but I think the current spec already introduced the mechanisms that one certain cell is deactivated/off, and then the off cell could be requested to activate…I think there is no need to discuss the concrete notice or wake-up, this could be discussed during WI phase to see if existing mechanism could be reused. |
| Lenovo, Motorola Mobility | How is it different from the legacy e.g. cell activation between two RAN node? |
| Deutsche Telekom | We share the same view as Huawei. |
| Futurewei | This information allows a sleeping node to tell neighboring nodes its operating status so better decisions can be made at neighboring nodes. It also allows the sleeping node to be waken up, say by the coverage node, to share the traffic burden in the area. So we support the proposal. |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-215072 Discussion on Standards Impact on energy saving (CATT)

R3-215216 Network Energy Saving (Ericsson)

R3-215473 Network Energy Saving – Solutions and Standard Impacts (Futurewei)

R3-215524 Further discussion on solution to AI-based Energy Saving (ZTE Corporation, Lenovo, Motorola Mobility, China Unicom)

R3-215562 Discussion on Standard Impact for AI/ML based Network Energy Saving (Samsung, Verizon Wireless)

R3-215665 (TP to TR 37.817) Remaining issues for AI based Energy Saving (Huawei)

R3-215707 Solutions of AI based ES for Split Architecture Base Station (China Telecomunication Corp.)

R3-215245 UE assistance information for AI/ML (Qualcomm Incorporated)

R3-215269 AI/ML based network energy saving and load balancing (Intel Corporatio

# Comments

It reads a bit confusing. I suppose it’s asking if AI/ML based network energy saving can generate above output.