3GPP TSG-RAN WG3 #114-e	R3-215909

Electronic Meeting, Nov 1th – 11th, 2021

Agenda Item:	18.4.1

Source:	ZTE (moderator)

Title:	Summary of CB: # AIRAN2_ESSolution

Document for:	Approval

# Introduction

CB: # AIRAN2_ES

- Discuss the solution, input/output, standard impacts

- Merging any agreement parts; provide TP if agreeable

- Capture agreements and open issues

(ZTE - moderator)

Summary of offline disc R3-215909

Two phases of this email discussion:

- Phase 1 Deadline: 12:00AM UTC, 5th Nov.

- Phase 2 Deadline : 6:00AM UTC, 9th Nov, we will try to come up with agreeable TP in the 2nd phase discussion before online session, if needed.

# For the Chairman’s Notes

Propose the following:

Proposal 1:  Capture the overall structure for AI-based energy saving into the TR in the Appendix as implementation reference, and the details needs to be further checked.

Proposal 2: Add the statement for AI-based energy saving in the TR to clarify the potential solutions below:

- AI/ML Model Training is located in the OAM and AI/ML Model Inference is located in the gNB.

- AI/ML Model Training and AI/ML Model Inference are both located in the gNB.

Proposal 3: Add the statement for AI-based energy saving in the TR to clarify the potential solutions in case of CU/DU architecture as below:

- AI/ML Model Training is located in the OAM and AI/ML Model Inference is located in the gNB-CU.

- AI/ML Model Training and Model Inference are both located in the gNB-CU.

Proposal 4: Input information of AI-based network energy saving includes:

Input Information from Local node:

- UE mobility/trajectory prediction

- Energy efficiency

Input Information from UE:

- Location history (e.g., coordinates, serving cell ID), UE historical serving cells and their locations

- UE moving velocity

Input from neighboring NG-RAN nodes:

- Past handover performance information

- Energy efficiency

To be continued:

- UE assistance information with mobility prediction

- UE assistance information with UL/DL traffic prediction

- Energy efficiency gain

- Energy state

- UE performance after handover

Proposal 5: Whether to regard load prediction or UE mobility trajectory prediction as a tool-box use case could be discuss after the solutions for AI-based network energy saving is mature or in the WI normative phase.

Proposal 6: Output information of AI-based network energy saving includes:

- Recommended Energy saving Strategies, including recommended cell activation/deactivation

- Energy efficiency information, including predicted energy consumption information

Proposal 7: Feedback information of AI-based network energy saving includes:

- UE transmission performance after handover

- Resource status of neighboring NG-RAN node

- Energy efficiency information

Proposal 8: Whether to exchange predicted energy saving strategies between NG-RAN nodes should be discussed when the strategies are finally confirmed.

[Ericsson: This proposal is supported by the majority of companies and it could be captured in the TR with a note sayinf that it is FFS which energy saving strategies will be exchanged]

Proposal 9: Leave the discussion how to exchange the predicted resource status between NG-RAN nodes in the WI normative phase.

# Discussion (2nd round)

  - Comments on draft TP

Companies are invited to provide comments on the draft TP for the AI/ML based network energy saving use case.

| Company | Comment |
| --- | --- |
| Nokia | We don’t agree to capture the figure in the Annex of the TR since we don’t see a real value behind doing this. We don’t support the following information from the UE to be provided in the input: Location history (e.g., coordinates, serving cell ID), UE historical serving cells and their locations UE moving velocity Visited cell information is provided in UE History Information from UE and is available at the local node. Regarding exact coordinates it is not clear if they are really needed for the purpose of energy saving but furthermore, UE may not be willing to provide those. We propose to modify the output of AI/ML based energy saving as: AI/ML-based network energy saving model can generate following information as output: Energy saving strategy, such as recommended cell activation/deactivation Handover strategy, including recommended candidate cells for taking over the traffic Predicted energy efficiency information Regarding the feedback, how is now load measurement and resource status different in the TP? |
| Ericsson | We agree with Nokia on the Annex. As commented already we think this discussion belongs to the framework and not to the use case description. We propose to remove it. We also do not accept the Location History input from the UE. We made some changes to the TP, where we mainly proposed to capture the exchange of proposed Energy Saving strategies, with an FFS on the strategy to select. |

# Discussion (1st round)

## Overall structure for AI/ML-based energy saving

[4] put forward the overall structure for AI/ML-based energy saving, which describes that AI-based energy saving follows a unified process regardless of which solutions to make the solution much clear and comprehensible as shown below.

Figure 1. Overall structure of AI-based energy saving

- Data collection is mainly responsible for the data collection, and required data is used to energy saving including current energy information, resource status of ES-cell and neighboring cells, even weather or other required information as input.

- AI-generated information includes load prediction, energy prediction, trajectory prediction, scenario classification or other required information generated by AI/ML model.

- Energy saving decision generation is to generate the energy saving decision based on the input from data collection, and refined input data. AI/ML model can also be used to make energy saving decision.

- Energy saving decision execution is to update the configuration based on the energy saving decisions and execute the decision.

Question 1-1: Companies are invited to provide their views on whether to capture the figure above into the TR, any refinement if yes.

| Company | Yes/No | Comments |
| --- | --- | --- |
| Huawei | No | It seems that this is trying to refine each function block, but we are talking about solutions, so anyway we will have texts about e.g. what the collected data include, what the output of inference could be, etc. And, with this picture, seems we also need to give mapping between this figure and the framework figure? We are making things complicated. |
| Lenovo, Motorola Mobility | Yes | It looks good in general, we can further check when finalizing the TP. |
| Deutsche Telekom | Yes, but … | We are in principle ok to add such figure, but we share a similar view as Huawei. What is missing, is a mapping/explanation how the functional blocks in the figure correspond to the functional framework under definition. Furthermore, some parts are still unclear. E.g. the model inference function is not visible, it seems that data collection creates the AI output. Performance feedback is noted in the figure, but it this the “Feedback” in the functional framework? Why does it go to the block with AI generated information, why not to data collection? More discussion on details is needed. |
| Futurewei | No | We don’t see the needs and benefits for such an overall structure. The structure for network energy saving already exists. AI/ML just provides information from another aspect for decision making. Some functions blocks, such as the “Energy Saving Decision Generation”, are implementation dependent and do not need to be standardized. We believe the current discussions on input, output and feedback are enough. |
| Nokia | No | We don’t see a problem with this figure, but we also don’t think it will offer some improvement if captured in the TR. |
| Verizon | No | Agree with Huawei comments above. Seems like we are making it too complicated and trying to specify a certain algorithm in the energy saving decision box. Specifying inputs/outputs and a framework for exchanging data is already being included. This might lead to more confusion. It may be ok to capture as a reference implementation in the Appendix with more clarifications. |
| NEC | Maybe | This looks like duplication of general framework. Not sure what is the benefit of adding such description. |
| Samsung | No | Same view with Huawei. This figure shows the input/output/feedback as well as procedure of training and inference. But we have defined input/output/feedback of the model in the TR. The detailed procedures of training and inference are up to implementation, which is out of RAN3 scope. So it seems there is need to capture this figure. |
| China Telecom | Yes, but | This seems to be based on the general framework for specific design for energy-saving use cases. The structure diagram depicts four functional blocks, but are the AI-generated Information and Energy Saving Decision Generation modules mentioned here can be mapped to model training and model inference modules of the already agreed general framework? And whether they need to be consistent with the description of the general framework here needs further discussion. Secondly, the performance feedback needs more clarification. |
| Intel | No | We don’t think above figure need to be captured in the TR, as it is more implementation specific. To identify standard impact of one use case, we think a well-shaped input/output and feedback is enough. |
| CATT | No | Agree with Huawei. We have defined the framework, so, it is not necessary to capture the figure above for energy saving which may introduce duplicate work. |
| CMCC | Maybe, but | In general, the figure is fine for us, but we partly share the view with Huawei that it is not so necessary. |
| Ericsson | No | As stated by other companies the diagram seems to replicate the functional framework and make it specific for one use case, which is exactly what a functional framework should not do. Namely a functional framework should be use case agnostic (if not we would need one for every case) |
| Qualcomm | Yes, no strong view | Agree it is duplicated with framework figure but it provides more details. |
| ZTE | Yes | As a proponent, since we have discussed two solutions and the potential procedure flow for the AI-based energy saving, we tend to depict a figure to explicitly show a unified process regardless of which solution. And some companies consider this structure figure as a duplicated work, but we want to clarify that AI Framework is to demonstrate the process of AI function operation, and this figure is to show the overall working procedure for the AI-based energy saving. It’s recommended to refine the figure, and capture some information, which has been agreed, into the figure. |

Moderator’s summary:

7 companies state that the figure is agreeable but several of them consider the overall structure as a duplicated work and much details are detailed, while 8 companies don’t agree to capture this figure into the TR, and the structure will make the use case complicated, 1 company state that there is no problem with this figure, 1 company suggest to capture as a reference implementation in the Appendix.

Based on above, the structure is to depict a unified process for AI/ML-based energy saving, and to give an overall sight on the solutions on ES. Moderator tends to conclude to capture the overall structure for AI-based energy saving into the TR in the Appendix as implementation reference, and the details could be further checked.

Proposal 1:  Capture the overall structure for AI-based energy saving into the TR in the Appendix as implementation reference, and the details could be further checked.

## AI/ML Training and Inference deployment

In the last meeting, two options were agreed to captured into the TR:

- Model Training at OAM and Model Inference at NG-RAN

- Model Training and Model Inference at NG-RAN

[1] support Model training is located at OAM and model inference is located at NG-RAN considering there is no requirement for real-time energy saving decision at this time. Moderator think this solution is already captured into the TR.

[9] proposes that NG-RAN node should be able to perform online model training based on the AI/ML model received from OAM. With continuous online training at NG-RAN node, the deployed model can be continuously evolved and improve its accuracy for performance improvement.

Question 2-1: Companies are invited to provide their views on whether to clarify that Model Training is online training or offline training in the TR.

| Company | Comments |
| --- | --- |
| Huawei | Yes, we think we have to do that, technically offline training and online training are of quite different requirements as far as data storage is concerned, while data storage is our of RAN scope. |
| Lenovo, Motorola Mobility | It would be beneficial to clarify what is really online training and offline training. Maybe it can be discussed based on exact solution. Besides, online training and offline training sounds different AI algorithm categories, not sure if we want to touch that in the TR. |
| Deutsche Telekom | In principle, both offline and online training are feasible, but they are used in different parts of model LCM. We would assume that usually (initial) offline training is done in OAM before deploying the model to inference function in RAN. Online training in RAN depends on model and learning method applied. This should be explained for use case under consideration, here ES. |
| Futurewei | We would like to point out that both online training and offline training are training functions (note we don’t have definitions for either of them). Therefore, contribution [9] essentially proposed the third deployment scenario, i.e., model training at both OAM and NG-RAN, model inference at NG-RAN. It is OK if a vendor chooses to do it, but we don’t think there would be standards impacts for this implementation scenario because the current two implementation options have covered the input, output and feedback needs for this scenario. Therefore, we believe whether a RAN node wants to support continuous online training can be left to implementation or something like that. This AI can move forward with the 2 options we have already agreed upon. We would also like to note that this new deployment scenario was proposed to the high-level framework AI (18.2). So, we need to wait until a decision is made in that discussion before we discuss this item in 18.4.1. |
| Nokia | In the terms section we have captured already that Training can be online or offline. We agree with DT that offline training is done (in principle) in OAM and online in the RAN. However, we think that this will be the same for all use cases so it should not be explained per use case. Instead, maybe we could further define what offline and online training mean in the terms section. |
| Verizon | Both offline/online training are possible and they could even work in conjunction with one another i.e., initially the model might be trained and deployed offline, but it could be refined further online based on performance feedback and other factors. |
| NEC | Both are possible depending on solution. |
| Samsung | The online and offline training are distinguished by whether to update the model during inference stage by new-collected data. The choice of online/offline training and detailed training algorithm are out of scope. It is reasonable to put offline training in OAM and online training in RAN. But the training in the TR includes both online and offline ones. And the current two options in TR can cover both online/offline cases. |
| China Telecom | It needs to be clarified. Online training requires further real-time training based on the offline trained model. They are two different processes. |
| Intel | First of all, we think the question is a little bit confusing with what we proposed in [9], as it’s only focus on offline/online training perspective. The proposal itself is to clarify model training and model inference deployment based on existing two solutions: 1) model training in OAM, model inference in RAN 2) model training and model inference in RAN. It is proposed to clarify that it is also possible for RAN to continue model training based on model received from OAM, i.e. 3) model training in OAM and RAN, model inference in RAN. We are ok to specify whether model training is online or offline in different deployments (i.e. three deployments listed above). For online training, it is a synchronized training, where model training is updated in real-time, with real-time data collection and feedback. Offline training is asynchronized model training, where the updated model is not used for model inference in real-time. With that, three deployment models can be further clarified as: 1) offline and online model training in OAM, model inference in RAN 2) offline model training in OAM, online model training in RAN, model inference in RAN 3) offline training, online training, and model inference in RAN To FW’s comment, as we already agreed where to deploy model training and model inference should be discussed per use case based, we don’t think we need to wait for discussion in high level principle. |
| CATT | Yes, agree to clarify online training and offline training. I believe most of the time online training is used for real-time energy saving decision. Currently offline training may be used for energy saving decision on automatically shutting down cell/ channel/carrier/symbol. |
| CMCC | The current TP includes both online and offline training, and whether the NG-RAN node choose the online training or offline training is up to implementation. |
| Ericsson | We do not see the need to differentiate between online and offline training, which are anyhow techniques related to the model implementation and learning process. By acknowledging in 3GPP that there is online and offline training (and nothing else), we are favouring one type of model implementation. We should instead be model agnostic. Training therefore includes all possible tyes of training |
| Qualcomm | Yes. But, the clarification seems to be generic, at least applicable to load balance and mobility optimization too. We can consider whether to put the clarifications in framework part. Online training is based on data collected in real time. Offline training is based on previous collected data. So, theoretically, both kinds of training can happen in OAM and RAN, though offline training in OAM and online training in RAN are more typical. |
| ZTE | We suggest not to clarify whether model training is online training or offline training in the TR. Online/offline training is related to AI/ML algorithms, and three deployments proposed by Intel, in our understanding, has been already included in the potential options agreed in the last meeting. |

Moderator’s summary:

Based on the comments, majority companies has the common understanding that model training could be split into online training and offline training in the different deployments. However, moderator think the current TP has included online training and offline training deployment scenarios. Hence, moderators propose to add the statement for AI-based energy saving to clarify the potential solutions below:

- AI/ML Model Training is located in the OAM and AI/ML Model Inference is located in the gNB.

- AI/ML Model Training and AI/ML Model Inference are both located in the gNB.

Proposal 2: Add the statement for AI-based energy saving in the TR to clarify the potential solutions below:

- AI/ML Model Training is located in the OAM and AI/ML Model Inference is located in the gNB.

- AI/ML Model Training and AI/ML Model Inference are both located in the gNB.

[7] proposes to consider the different deployment solutions of model training and model inference modules in the split architecture base station and two solutions in CU/DU architecture are proposed below:

- Solution #1: Model training and model inference at CU side

- Solution #2: Model training at CU and model inference at DU

Question 2-2: Companies are invited to provide their views on whether the Solution #1, Solution #2 or both, is preferred to be captured into the TR.

| Company | Solution#1, or Solution#2, or both | Comments |
| --- | --- | --- |
| Huawei | Solution#1, but | We think CU should have more knowledge than DU, and DU could provide what is needed by CU. But we suggest to focus on the gNB and OAM case first, i.e. where the model training is at OAM and model inference is at gNB. When this solution is clear, we can discuss the CU/DU split case. |
| Lenovo, Motorola Mobility | Solution#1, and Solution#2 | Depending on the energy saving strategy, if it is beam/cell level energy saving, it could be DU to infer and decide, otherwise it could be up to CU to infer and decide. |
| Deutsche Telekom | Both | Where to place training and inference is strongly dependent on use case and underlying approach to collect which data and to adapt which parameters. We wouldn’t expect to have offline training in RAN nodes, especially not in DU, just online training might be useful. |
| Futurewei | Solution#1 | We would like to note that to enable model inference at DU there will be impact on F1 interface, which will complicate the specifications. |
| Nokia | Focus on solution #1 | We could focus on solution #1 for the time being and consider other solutions once we make some progress. |
| Verizon | Both | In both cases, model training seems to be assumed at CU. This could also be at OAM. Model inference could be at both CU/DU. DU might be best suited for inferences involving optimizations of lower layer stack (e.g. beam optimization) while CU might be best suited for inferences involving higher layer stack (e.g. cell turn off). |
| NEC | Maybe both | Depending on solution and especially on actions taken for ES, both deployment options may be possible. |
| Samsung | Solution 1 first | We may define the details of model input/output first. And then decide whether to allow DU to do inference according to input/output and model functionality. If the input is available at DU and the output is valuable for DU only, we can put inference function at DU. |
| China Telecom | Both | The last meeting had designed the ES use case solution for the non-split architecture base station, considering the deployment of model training to the OAM or base station side, and the model training is located in NG-RAN. The same discussion should be done for the split architecture base station, and both the two scenarios mentioned above should be considered. The two solutions are designed for different scenarios. Solution# 1 is suitable for centralized management scenarios, and solution #2 is more inclined to be used in flexible distributed management scenarios. |
| Intel | Both | Compared with model training, model inference is less complex and can perform in real-time. For CU/DU split architecture of AI-based ES, depending on the energy saving strategy, we think it’s ok to consider model inference at DU. |
| CMCC | Start from solution 1 | Generally, both solutions are supported. Agree with Samsung that maybe we can start from solution 1 and then see whether to use DU to do inference. |
| Ericsson | Prioritise Solution 1 | The gNB-CU is aware of mobility, UE measurements, neighbour cell status. The gNB-CU can therefore have a better understanding of how load will change and migrate and for that on what is the best prediction on energy saving strategies. Note that the cell management function (cell activation, deactivation etc) specified today is triggered by the gNB-CU. Namely an energy based cell activation/deactivation decision is first taken by the gNB-CU. For this reason it makes sense to focus on inference at the gNB-CU |
| Qualcomm | Both | Inference may be running in either CU or DU, depending on delay requirement and data availability. Similar, training can be in either CU or DU. The two solutions are a subset of the possible deployment scenarios but we can start from them. |
| ZTE | Both | Since trajectory prediction and load prediction could be used for AI-based energy saving, model inference could be located in either CU or DU. |

Moderator’s summary:

8 companies agree to capture both solutions for CU/DU architecture, and 6 companies suggest to focus on the solution #1 that Model training and model inference could be at CU side. Hence, moderator conclude to add the statement for AI-based energy saving in the TR to clarify the potential solutions in case of CU/DU architecture as below:

- AI/ML Model Training is located in the OAM and AI/ML Model Inference is located in the gNB-CU.

- AI/ML Model Training and Model Inference are both located in the gNB-CU.

Proposal 3: Add the statement for AI-based energy saving in the TR to clarify the potential solutions in case of CU/DU architecture as below:

- AI/ML Model Training is located in the OAM and AI/ML Model Inference is located in the gNB-CU.

- AI/ML Model Training and Model Inference are both located in the gNB-CU.

## Inputs of AI/ML-based Network Energy Saving

Following information as input for AI/ML-based network energy saving are summarized based on contributions:

Input Information from Local node:

- UE mobility/trajectory prediction [3][4][6]

- Energy efficiency gain or energy state [9]

Input Information from UE:

- Location history (e.g., coordinates, serving cell ID), UE historical serving cells and their locations [3]

- UE moving velocity [3]

- UE assistance information with mobility prediction [8]

- UE assistance information with UL/DL traffic prediction [8]

Input from neighboring NG-RAN nodes:

- Past handover performance information [3]

- UE performance after handover [3]

- Energy efficiency gain or energy state [9]

Question 3-1: Companies are invited to provide their views on whether the above input information listed could be used for AI/ML-based Network Energy Saving.

| Company | Comments |
| --- | --- |
| Huawei | Input information from local node: 1: OK. 2: Prefer to use the energy efficiency that reflects the real performance of the RAN node we want to evaluate. Input information from UE: 3/4: No. It could be derived from the “UE history information from UE” IE, which is already there in the local node. 5/6: OK. Input from neighboring NG-RAN node: 7: Nice to have. HO history/HO successful rate could be used as reference for future HO decision, . 8: OK. 9: Prefer to use the energy efficiency that reflects the real performance of the RAN node we want to evaluate. |
| Lenovo, Motorola Mobility | 1: ok 2: ok 2a: ok 3, 4: look like input to predict UE mobility/trajectory, not sure if they can be really regarded as input for energy saving. 5, 6: no, they assume UE capability to perform some kind of prediction, shall be avoided for now. 7,8: not sure if they care useful for energy saving, they look like feedback information. 9: not sure, and looks like feedback information. |
| Futurewei | In general, we agree with the above inputs. But we need to define what the “Energy efficiency gain or energy state” is; we can do it in the WI phase. |
| Nokia | Input from Local Node 1: OK 2: Not OK. What is this energy saving state? Is it the current state of the gNB? What could be the output corresponding to it? Also, it is unclear why a new measurement energy efficiency gain needs to be introduced as opposed to energy efficiency. Input from UE: 3: Not OK, it is not evident why exact coordinates can be more beneficial as opposed to less granular information (e.g., on cell level), available in existing SON reports. 4: Not OK, it is not evident how UE velocity can improve energy saving. 5,6: Not OK. We don’t think that we should consider predictions from UEs for this Rel. 17 SI. Input from neighbouring NG-RAN nodes 7,8: OK 9: Not OK. An indicator of energy efficiency can be sent between neighbouring nodes. The “gain” can be calculated as a delta between consecutive energy efficiency measurements. |
| Verizon | We are fine with all these different inputs. Additional inputs might also be considered. |
| Samsung | OK for 1,3,4,7,8; Not OK for 2,5,6,9. For 2 and 9: prefer to collect energy efficiency or energy consumption directly. The energy efficiency gain can be calculated based on energy efficiency. The energy state (high or low) is related to the total energy volume. Although same energy state for two devices with different total energy volumes, the remaining energy volumes are diverse. So energy state is not precise to do the energy saving decision. For 5 and 6: Whether and how to involve UE are still under discussion. It is better to consider UE inference until there is conclusion about UE involvement. |
| China Telecom | We agree with all above input information to be used for AI/ML-based network energy-saving use cases |
| Intel | Ok to 2, 7, 8, 9. As shown in section 3.4, the energy state refers to different energy level of one NG-RAN node. For AI/ML-based ES, it is not enough to only consider active/inactive of one NG-RAN node, introducing certain energy levels/states in between is beneficial to define finer energy saving strategy as well as reduce service interruption caused by unnecessary handover. To 1,5, we understand the intention of introducing UE mobility/trajectory prediction is to predict target cell by also considering UE’s trajectory. However, we think this belong to “AI/ML based mobility”, ES AI/ML model can just reuse what has been collected for AI/ML based mobility. Hence, for mobility related information, we suggest to a general description as below: UE mobility/trajectory prediction which is use for AI/ML mobility. To 3, 4, No. It is not clear to us how location history and UE moving velocity can benefit to network energy saving. To 6, it depends on whether UE has such prediction capability. We are fine to keep it in SI phase. Whether it can be supported in normative phase, we need to check with RAN2. |
| CATT | Not OK for 3 since the information already available in local node, no need to further report from UE. Not OK for 5,6.We would like to consider the prediction function located in UE side in further release. In Rel-17,we focus on network based prediction |
| CMCC | Ok for all. But the energy state needs clarification, energy efficiency or energy consumption maybe better. |
| Ericsson | 1. : OK, but we would like to point out that this is a node internal parameter that have no impact on RAN3 specifications work 2.: Ok, but we would like to specify that this parameter may consist of current energy efficiency/state or predictions on energy efficiency/state. The RAN node may produce a list of own Energy Efficiency predictions, based on different possible energy efficiency actions. 3.,4.: OK 5.: Not ok. By knowing the UE speed, the RAN can predict the UE trajectory. Such prediction does not necessarily need AI support. 6.: OK 7., 8.: NOT OK. Why do we need these inputs when what we are trying to solve is how to improve energy efficiency? Such inputs are more suitable for the Mobility and Load Balancing use cases. 9.: We agree with this parameter, but we would like to specify that this parameter may consist of current energy efficiency/state or predictions on energy efficiency/state. The RAN node may produce a list of own Energy Efficiency predictions, based on different possible energy efficiency actions. |
| Qualcomm | Agree all, assuming 3,4 are existing information like UE history information, location info in MDT. For 5 and 6, at least in this release, how UE derives the information is up to UE implementation. |
| ZTE | OK for 1,2,3,4. For 2, we think energy efficiency is enough. For 3,4, these are used for trajectory prediction. For 5,6, UE capability to perform AI/ML function is out of RAN3 scope. OK for 7, and 8,9 seem as the feedback information, not sure if it is needed as input. |

Moderator’s summary:

Input Information from Local node:

- UE mobility/trajectory prediction (11/13 companies support)

- Energy efficiency gain or energy state (10/13 companies support, and majority companies suggest to rephase the wording to energy efficiency)

Input Information from UE:

- Location history (e.g., coordinates, serving cell ID), UE historical serving cells and their locations (8/13 companies support)

- UE moving velocity (8/13 companies support)

- UE assistance information with mobility prediction (6/13 companies support)

- UE assistance information with UL/DL traffic prediction (7/13 companies support)

Input from neighboring NG-RAN nodes:

- Past handover performance information (10/13 companies support)

- UE performance after handover (9/13 companies support)

- Energy efficiency gain or energy state (7/13 companies support)

Proposal 4: Input information of AI-based network energy saving includes:

Input Information from Local node:

- UE mobility/trajectory prediction

- Energy efficiency

Input Information from UE:

- Location history (e.g., coordinates, serving cell ID), UE historical serving cells and their locations

- UE moving velocity

Input from neighboring NG-RAN nodes:

- Past handover performance information

- Energy efficiency

To be continued:

- UE assistance information with mobility prediction

- UE assistance information with UL/DL traffic prediction

- Energy efficiency gain

- Energy state

- UE performance after handover

[1] propose to define load prediction function, and UE mobility trajectory prediction if needed by AI-based network energy saving as a kind of tool-box to discuss.

Question 3-2: Companies are invited to provide their views on whether to regard load prediction or UE mobility trajectory prediction as a too-box use case to discuss.

| Company | Yes or No | Comments |
| --- | --- | --- |
| Huawei | Not sure | It was discussed before many times. On one hand, we understand that probably prediction will be used for different use cases; on the other hand, we think the study should focus on the energy saving, load balancing and mobility optimization. What does the toolbox use case mean exactly here, what are the additional spec impacts, in addition to normal collected data and the detailed value of prediction (to be discussed during WI phase I guess) |
| Lenovo, Motorola Mobility | Yes | RAN node may decide to turn off some cell if the predicted load is low and UEs will leave the cell. |
| Futurewei | Yes | A toolbox approach can avoid duplicate specifications/implementations among different use cases. |
| Nokia | No | Our study is not about load prediction or about UE mobility trajectory prediction. Of course, we may use such predictions in the study (e.g., load prediction can be an input to AI/ML mobility) but we don’t see how defining them as tool-box use cases can provide benefits. |
| Verizon | Yes | Load prediction/UE mobility prediction is certainly useful for energy saving use case. However, they may be applicable to other use cases as well including load balancing/mobility optimization. Also new use cases will likely be considered in the future, so it would be good to consider these as a toolbox potentially applicable to future expanded AI/ML use case list. This helps avoid duplication of specs. |
| NEC | Maybe | It was previously discussed not to introduce tool-box use cases. However, depending on solution load prediction and UE trajectory prediction could be inputs to ES. |
| Samsung | No | Load prediction or UE mobility trajectory prediction are the different AI/ML model functionality instead of use cases. If we intend to differentiate model for prediction and model for decision-making, prefer to define the input/output/feedback according to the model functionality for each use case. |
| China Telecom | Yes, but | It seems fine to consider defining tool-boxes related to different use cases, but there are things that need to be discussed further, such as whether the toolbox is a type of model. |
| Intel | No | Agree with HW that we don’t see additional standard impact. It is more implementation specific. |
| CATT | Yes | Proposed to define load prediction and UE mobility trajectory prediction as a tool-box which can avoid duplicate work. We may not need to discuss input and output of load prediction and UE mobility trajectory prediction in every use cases. |
| CMCC | Yes | The information of load prediction or UE mobility trajectory prediction is beneficial for the decision of energy saving. |
| Ericsson | No | Like others, we do not understand how a “toolbox” should be specified in any different way than a piece of information needed. We work on a use case basis and we identify the information needed to support the use case. If this information is reused in many use cases, let it be. We signal for example neighbour cell information for many reasons, ANR, PCI management, RACH optimization etc. and yet, we did not define a “Neighbour Information Toolbox” |
| Qualcomm | Yes | Yes, they are generally applicable to all kinds of other use cases. |
| ZTE | Yes | Agree. From our perspective, trajectory prediction and load prediction could be used for the use cases which are agreed in the TR now. So, we suggest to regard prediction as a tool-box use case. |

Moderator’s summary:

8 companies agree to regard load prediction or UE mobility trajectory prediction as a tool-box use case to discuss in order to avoid duplicated work, while 5 companies disagree because there is no additional specification impacts. Moderator here tries to make a conclusion that whether to regard load prediction or UE mobility trajectory prediction as a tool-box use case could be discuss after the solutions for AI-based network energy saving is mature or in the WI normative phase.

Proposal 5: Whether to regard load prediction or UE mobility trajectory prediction as a tool-box use case could be discuss after the solutions for AI-based network energy saving is mature or in the WI normative phase.

## Output of AI/ML-based Network Energy Saving

Following information as input for AI/ML-based network energy saving are summarized based on contributions:

- UE mobility prediction, which can be used to help making handover decisions. [3]

- Recommended Energy saving Strategies including, recommended cell activation/deactivation, symbol shutdown, channel shutdown, carrier shutdown, deep sleep [4][5]

- Predicted energy information, including predicted energy consumption information [4]

- Energy efficiency [6]

- Action level, action type [5]

- Predicted energy state (e.g. Active, High, Low, Inactive) [9]

- Validity time of energy strategy [5] [9]

- Energy saving strategies [9]:

  - Update of SSB periodicity

  - Update of the advertised Bandwidth (use Bandwidth Part Adaptation (BPA) feature

  - Update of DTX for BS

  - Update of the SIB blocks periodicity

  - Use wake-up signaling features/DRX features to increase the number of UEs in sleep mode, depending on traffic patterns

  - Secondary cell activation/deactivation

  - Carrier aggregation turn-on/off

  - Primary/Macro cell activation/deactivation

  - Dual connectivity turn-on/off

Question 4-1: Companies are invited to provide their views on whether the above output information listed could be used for AI/ML-based Network Energy Saving.

| Company | Comments |
| --- | --- |
| Huawei | 1: No. The output should be highly related to the energy saving. The UE mobility prediction should be the input, but not the output. 2: OK. The recommended cell activation/deactivation is OK. Others could also be considered, but not sure if some of them could be exchanged between base stations. 3: No. Prefer to use the energy efficiency that reflects the real performance of the RAN node we want to evaluate. 4: OK. 5: Could consider, but it seems that they are implemented mechanism and not sure if could be transferred via interface. 6: Could consider. But we prefer to use the energy efficiency that reflects the real performance of the RAN node we want to evaluate. 7: No. As discussed in our paper, there is no need to include the validity time together with the output information every time. 8: Not sure if we should agree or disagree each of them, some of them seems straightforward, e.g. activation/deactivation; some of them seems unclear, e.g. update of the advertised Bandwidth, etc, some of them seem to be implemented mechanism and cannot be transferred via interface. Maybe there is no need to go into such details during study item phase, this comment also applies to other use case. |
| Lenovo, Motorola Mobility | 1: we understand mobility prediction will help with energy saving not the other way around. 2,3: ok, need to discuss how to define energy consumption. 4: not sure,, is it a predicted energy efficiency? Otherwise it can be easily measured. 5: need a bit more elaboration 6: intention is ok 7: no, NW can update the energy strategy when it wants. We don’t see the need of a validity time. 8: ok in general |
| Futurewei | Yes. This information could be used as output of the network energy saving function. However, the exact outputs of the network energy saving function and the details need to come from thorough discussion of the group. For example, some of the outputs or decisions, like 2 and some items under 8, would need to be communicated to Dus for CU/DU split scenario if inference is on CU. |
| Nokia | 1) UE Mobility Prediction: Not OK 2) Recommended Energy Saving Strategies: OK for cell activation/deactivation but not OK on the finer granularity ones (symbol shutdown, channel shutdown, carrier shutdown, deep sleep). These seem to be more implementation specific. 3) Predicted Energy Information: Not OK, energy consumption doesn’t give sufficient information on the network performance. 4) Energy Efficiency: OK 5) Action level (channel, subframe, carrier), action type (switch on/off): Not OK, same reasons as 2. 6), 8) Predicted energy state and Energy Saving Strategy per state: Could be interesting to consider different predicted energy saving states at a gNB but some more thinking is needed on the exact strategies. 7) Validity time: Not ok, this can be indicated implicitly through a new energy saving decision. |
| Verizon | We are fine with the list of outputs. Additional ones might be considered in future. There seems some overlap (e.g. between 2 and 8). A consolidated list might be better. |
| Samsung | OK for 1,2,3,4,5,6,7 Not OK for 6 and 8 For 6: prefer to output energy efficiency or energy consumption. The energy state (high or low) is related to the total energy volume. Although same energy state for two devices with different total energy volumes, the remaining energy volumes are diverse. So it seems that energy state is not precise. For 8: it seems some of them are implementation related. |
| China Telecom | We agree with the list of outputs to be used for AI/ML-based network energy-saving use cases |
| Intel | Yes to 2, 3, 4, 5, 6, 7, 8. From the information listed above, we think 2/5/8 can all be categorized into energy saving strategy. We suggest merging the list from 2/5/8 as energy saving strategy. |
| CATT | Not OK for 1. 1 may be the output of Mobility Optimization. Energy Saving can use it as an input. Not OK for 5.We think 5 could be part of 2,thereby no need to list it independently For 8,agree with others that some are implemented related. |
| CMCC | OK for 2,3,4,5,7 For 1, the UE mobility prediction seems not a direct output of energy saving. For 6, it could be replaced by 4 For 8, some of them are overlapped with other items. |
| Ericsson | 1. Ok, but this is a node internal parameter that is not exposed over the interfaces 2. This information should be limited to cell level indications. A RAN node should not require a different RAN node to e.g. reduce the amount of resources used, or remove one carrier. Those are RAN internal decisions. 3. Ok. 4. Ok Note: We would like to point out that 2,3 and 4 could be provided together, e.g. an output could be a predicted energy consumption efficiency level for a given cell configuration action (e.g. turn off/on certain cells) 5. Not OK. As commented above, a RAN node should recommend to neighbour nodes actions per cell. Anything more than a cell level action that cannot be deduced by source RAN because it is very implementation specific. 6. Ok, but this is covered already by 3 and 4. 7. ok 8. NOT OK. As above, the actions in 8. Require an in depth knowledge of the neighbour RAN implementation, which is not available |
| Qualcomm | OK for 2,4,5,6,7. 1 could be tool box use case and not ES specific. 8 need further study. 3 is more or less duplicated with 4. |
| ZTE | 1: We agree that UE mobility prediction could be regard as input information for ES rather output information. 2: OK 3: Could be included in energy efficiency (bullet 4) 4: OK 5/6: Energy efficiency is enough. 7: No 8: Could be included in 2. Details could be further studied. |

Moderator’s summary:

- UE mobility prediction, which can be used to help making handover decisions. (5/13 companies support)

- Recommended Energy saving Strategies including, recommended cell activation/deactivation, symbol shutdown, channel shutdown, carrier shutdown, deep sleep (12/13 companies support, and majority companies support recommended cell activation/deactivation)

- Predicted energy information, including predicted energy consumption information (9/13 companies support, and moderator think it is overlapped with bullet4)

- Energy efficiency (11/13 companies support)

- Action level, action type (6/13 companies support)

- Predicted energy state (e.g., Active, High, Low, Inactive) (7/13 companies support)

- Validity time of energy strategy (8/13 companies support)

- Energy saving strategies (Majority companies consider it is overlapped with other items)

Proposal 6: Output information of AI-based network energy saving includes:

- Recommended Energy saving Strategies including, recommended cell activation/deactivation

- Energy efficiency information, including predicted energy consumption information

## Performance feedback for the AI/ML-based Network Energy Saving

Following information as feedback information for AI/ML-based network energy saving are summarized based on contributions:

- UE performance after handover [3]

- UE transmission performance measurement [6]

- Resource status of neighboring NG-RAN node [9]

- Energy information efficiency or energy state [9]

Question 5-1: Companies are invited to provide their views on whether the above feedback information listed could be used for AI/ML-based Network Energy Saving.

| Company | Comments |
| --- | --- |
| Huawei | 1/2: OK. They should be the same, e.g., the packet loss rate performed by the target node, or the packet delay performed by the UE. 3: OK. 4: OK, prefer to the energy efficiency. |
| Lenovo, Motorola Mobility | 1. it may only apply to switching off a cell leading to a handover of one UE 2. ok 3. not sure 4. ok |
| Deutsche Telekom | Unclear what is meant by “performance feedback”. In the functional framework we have “Feedback” and “Model Performance Feedback (FFS)”. I would assume “Feedback” is the basis for this question, correct? Ok to all, but with respect to (4) there is a need to clarify the meaning of metrics. What is meant by “Energy information efficiency” compared to “Energy efficiency” or “Energy efficiency gain” mentioned in some other questions before. |
| Futurewei | We agree in general. Note Item 1 and 2 may mean similar things. Also Item 4 should read “Energy information efficiency” instead of “Energy efficiency information” and the definition of “energy efficiency” has to be officially defined and agreed. |
| Nokia | 1,2: What is the difference between 1 and 2? 3: OK 4. Not OK. It is unclear why energy state should be part of the feedback. On the energy efficiency gain, it is not clear why we need a gain as opposed to energy efficiency. |
| Verizon | We are fine with all of these. As DT pointed above, some clarification of definition of the metrics would be useful. Additional ones might be added too. |
| Samsung | OK for 1, 2, 3 For 4, prefer energy efficiency or energy consumption. The energy state (high or low) is related to the total energy volume. Although same energy state for two devices with different total energy volumes, the remaining energy volumes are diverse. So energy state is not precise to do the energy saving decision. |
| China Telecom | We agree with above listed feedback information, but they seem to be used as feedback from Actor to Data Collection. In addition, we should also consider the feedback between model training and model inference, e.g., the prediction accuracy and confidence feedback. |
| Intel | Ok to all. For 4, we are ok with either “energy efficiency” or “energy efficiency gain” (a relative value, e.g. going up, going down, stay flat). For energy state, as explained in questions before, energy state refers to the energy level of one NG-RAN node, Active, High, Low, Inactive, etc. |
| CATT | All except 2. We think all the above feedback information could be used for AI/ML-based Network Energy Saving, but 1 may include 2, so, 2 may be not needed. |
| CMCC | OK for all, and energy efficiency is preferred for 4. |
| Ericsson | We agree with 4, but not with 1., 2., 3. The reason not to agree to 1..,2.,3, is that those feedback seem relevant to the load balancing and mobility scenarios but not to the energy saving scenario. We could anyhow be ok with them |
| Qualcomm | Agree 3 and 4. 1 and 2 are generic, not only for ES. |
| ZTE | OK for 3 and 4. 1/2 seems not related to energy saving. |

Moderator’s summary:

- UE performance after handover (9/14 companies support)

- UE transmission performance measurement (10/14 companies support, and moderator tends to merge bullet 2 into bullet 1)

- Resource status of neighboring NG-RAN node (12/14 companies support)

- Energy information efficiency or energy state (13/14 companies support, and majority companies suggest to rephase the wording to energy efficiency)

Proposal 7: Feedback information of AI-based network energy saving includes:

- UE transmission performance after handvoer

- Resource status of neighboring NG-RAN node

- Energy efficiency information

## Procedures

[2] proposes that an NG-RAN node should be able to accept/reject energy saving decision proposals in a neighboring NG-RAN node. And [5] proposes that the predicted energy saving strategy can be exchanged with neighbor cells to provide reference information for optimization decisions.

[5][9] mentioned that predicted resource status reporting can be embedded into existing resource status reporting procedure, and [5] also stated that that can be supported by designing a new procedure referring to the existing resource status reporting procedure. In addition, [9] propose that the target NG-RAN node can stop providing feedback to the source NG-RAN node if the handed-over UE is no longer available at the target NG-RAN node.

Question 6-1: Companies are invited to provide their views on the proposals below:

- Predicted energy saving strategy shall be exchanged between NG-RAN nodes

- Use existing resource status reporting procedure or to define a new one to exchange predicted resource status

| Company | Comments |
| --- | --- |
| Huawei | Not sure. For 1, we think the predicted energy saving strategy is just a predicted info which is not a real decision, what we need is real energy saving decision informed to neighbours; then for 2, we could leave this discussion to normative phase. |
| Lenovo, Motorola Mobility | 1. don’t understand the motivation, first, why one needs to predict energy saving strategy? Secondly, why need to inform the other RAN node? 2. we consider it useful for load balancing use case, not sure why it is needed for energy saving, maybe as feedback information, maybe they are nested. |
| Deutsche Telekom | (1) The meaning of the content of predicted energy saving strategy has be further clarified. For some issues like cell switch on/off it makes certainly sense. For (2) no clear preference. Both alternatives are feasible. Can be decided in WI phase. |
| Futurewei | 1. We don’t think this is necessary. 2. We are restricted from defining a new reporting procedure. We can reuse existing resource status reporting procedure to exchange predicted resource status with neighboring cells. Defining a new procedure is considered out of scope for this R17 SI. |
| Nokia | 1. OK in general though we do not agree on the action level (subframe, channel, carrier, device). Other than this, it is ok in our view if a gNB informs a neighbour of its intentions to switch off or switch on its cells. 2. OK to define a new procedure that is used to exchange predictions. |
| Verizon | (1) Yes, exchange of energy saving strategy helps neighbor nodes in their optimization decisions. (2) Both are feasible, can be captured as possible solutions in TR and then decide in WI phase if needed. |
| Samsung | (1) Yes, the predicated energy saving strategy can be exchanged with neighbor cells to provide reference information for optimization decisions (e.g. handover, load balancing, energy saving, etc.). For example, a node predicts it will be switched off in one minute. The node can exchange such predicted energy saving strategy with its neighbors to inform the action plan in advance, so the neighbor cells can take it as reference information to make proper decision (such as UE handover, load transferring, switch on/off and so on) to avoid the unnecessary handover, handover ping-pong, switch-off/on ping-pong, local overload etc. (2) Both ways are fine. Same view as Verizon, prefer to capture them as two options and then to decide in WI phase. |
| China Telecom | 1. Yes, it is possible to allow the exchange of information related to predictive energy-saving strategies between base stations; 2. Both methods of exchanging predicted resource status can be accepted. |
| Intel | 1) Not sure. It depends on what energy saving strategy is included in the information exchanged to neighbour node. It is not clear to us how all information of energy saving strategy is needed or useful to neighbour NG-RAN. 2) prefer use framework of existing resource status reporting procedure as baseline. Either add new element to existing signaling or introduce new one for predicted resource status can be left to normative work. |
| CATT | Exchange Predicted energy saving strategy may be useful, but it may lead to pre-occupied more resource than expected. Further consideration is needed. |
| CMCC | 1. Yes 2. both are ok |
| Ericsson | 1. Yes. With this we mean that an energy saving strategy, such as offloading a certain amount of resources to a neighbour RAN node, should be signalled to a neighbour RAN node. This is because the overall objective is to increase energy efficiency “globally” and not in one node only. If the target RAN node indicates that there is en energy efficiency deterioration as a consequence of the offloading, then that strategy is not good and another needs to be chosen. Hence, we propose that source and target confirm that an energy saving strategy has positive effects on both nodes before implementing it This is an aspect that can be left for normative phase. |
| Qualcomm | Yes for both |
| ZTE | We agree to exchange predicted energy efficiency between NG-RAN nodes. It is a overall optimization for AI-based network energy saving. Both ways are feasible. Prefer to use the existing procedure. |

Moderator’s summary:

For bullet 1), 9/14 companies support to exchange predicted energy saving strategies between NG-RAN nodes, while the rest are not sure whether the strategies is needed to exchange, and what is included in the energy saving strategies to neighboring nodes should be first clarified. Moderators tries to make a conclusion that whether to exchange predicted energy saving strategies between NG-RAN nodes should be discussed when the strategies are finally confirmed.

Proposal 8: Whether to exchange predicted energy saving strategies between NG-RAN nodes should be discussed when the strategies are finally confirmed.

For bullet 2), majority companies suggest to leave the discussion how to exchange the predicted resource status between NG-RAN nodes in the normative phase.

Proposal 9: Leave the discussion how to exchange the predicted resource status between NG-RAN nodes in the normative phase.

[3] also mentioned that following information should be considered to be exchanged over Xn interface.

•	Notice of entering sleep mode (optional)

•	Wake-up signal (optional)

Question 6-2: Companies are invited to provide their views on the proposal above?

| Company | Comments |
| --- | --- |
| Huawei | The intention makes sense, but I think the current spec already introduced the mechanisms that one certain cell is deactivated/off, and then the off cell could be requested to activate…I think there is no need to discuss the concrete notice or wake-up, this could be discussed during WI phase to see if existing mechanism could be reused. |
| Lenovo, Motorola Mobility | How is it different from the legacy e.g. cell activation between two RAN node? |
| Deutsche Telekom | We share the same view as Huawei. |
| Futurewei | This information allows a sleeping node to tell neighboring nodes its operating status so better decisions can be made at neighboring nodes. It also allows the sleeping node to be waken up, say by the coverage node, to share the traffic burden in the area. So we support the proposal. |
| Nokia | In our view, the above mechanisms are already supported in current specification. |
| Verizon | We share same view as Nokia above. |
| Samsung | Same view as Nokia and Verizon. The two mechanisms are already supported. |
| China Telecom | We share the same view as Huawei. |
| Intel | Agree with HW and Nokia, it is already supported in current spec. |
| CATT | Agree with Nokia |
| CMCC | Agree that it is already supported in current spec. |
| Ericsson | Maybe this detailed information can be left to normative phase but it seems very similar to legacy. |
| Qualcomm | For sleep mode, if it is cell activation/deactivation, it has been supported. If it is anything beyond cell activation/deactivation, e.g. finer granularity of on/cell or some interim state between cell on/off, we need to wait RAN1/RAN2 discussion. For wake-up signaling, I assume it is to wake-up network instead of UE. So, it needs RAN1/RAN2 study first. |
| ZTE | Agree with HW |

Moderator’s summary:

Based on the comments from companies above, majority companies mention that the mechanisms have been already supported in the current specification. Hence, moderator think there is no consensus on this proposal.

Proposal 10: No consensus …

# Conclusion, Recommendations [if needed]

If needed

# References

R3-215072 Discussion on Standards Impact on energy saving (CATT)

R3-215216 Network Energy Saving (Ericsson)

R3-215473 Network Energy Saving – Solutions and Standard Impacts (Futurewei)

R3-215524 Further discussion on solution to AI-based Energy Saving (ZTE Corporation, Lenovo, Motorola Mobility, China Unicom)

R3-215562 Discussion on Standard Impact for AI/ML based Network Energy Saving (Samsung, Verizon Wireless)

R3-215665 (TP to TR 37.817) Remaining issues for AI based Energy Saving (Huawei)

R3-215707 Solutions of AI based ES for Split Architecture Base Station (China Telecomunication Corp.)

R3-215245 UE assistance information for AI/ML (Qualcomm Incorporated)

R3-215269 AI/ML based network energy saving and load balancing (Intel Corporatio

# Comments

It reads a bit confusing. I suppose it’s asking if AI/ML based network energy saving can generate above output.