3GPP TSG-RAN WG3 #114-e	R3-21xxxx

Online, 1st - 11th November 2021

Agenda Item:	22.2.4

Source:	Ericsson (moderator)

Title:	CB: # MBS2_BearerMgmt - Summary of email discussion

Document for:	Approval

# Introduction

This is the summary of offline discussions for AI 22.2.4, for which Mdme Chair summarized the papers as follows:

CB: # MBS2_BearerMgmt

- Further discussion on the open issues

- Flow control mechanism for Multicast/Broadcast

- E1AP/F1AP signalling for Multicast/Broadcast session management

- Stage2/stage3 TPs if agreeable and check details, split work, if needed

- Capture agreements and open issues

(E/// - moderator)

Summary of offline disc R3-215888

# For the Chairman’s Notes

Propose the following:

to be added, stage 2/3 proposals to be identified after the 1st round

please add to each block of questions additional questions if you feel important topics have been missed by the moderator

# Discussion

## Shared F1-U bearer control

3.1.1	Turn the WA: For split MRB with common PDCP, shared F1-U tunnel is used into an agreement

| Company | Comment |
| --- | --- |
| Ericsson | agree |
| Nokia | Agree. |
| Qualcomm | Agree. For UE specific retransmission initiated by CU, a separate per UE F1-U tunnel may be needed. |
| Huawei | Agree |

3.1.2	Agree that the gNB-DU decides how many F1-U shared bearers are established per MRB context, taking into account potential needs for location dependent content delivery.

| Company | Comment |
| --- | --- |
| Ericsson | agree |
| Nokia | Disagree. CU seems better placed to see the location dependent need. |
| Qualcomm | Disagree. Bearer establishment should be decided by CU. |
| Huawei | Disagree. Same view with Nokia. |

3.1.3	If finally agreed by RAN2 for mobility, agree that gNB-DU shall be enabled deciding whether retransmitted data is provided for a specific UE only (scheduled with C-RNTI) or for all UEs (scheduled with G-RNTI).

| Company | Comment |
| --- | --- |
| Ericsson | agree, and we do not want to see per-UE F1-U bearers being setup for retransmission |
| Nokia | Pending RAN2. |
| Qualcomm | For PDCP Status Report based retransmission, CU should send the retransmission packet to DU using UE specific F1-U tunnel. Typically, the retransmission is UE specific (C-RNTI). If many UEs didn’t receive the packet, G-RNTI based retransmission may be more efficient. In this case, CU sends the missed packet to DU using shared F1-U tunnel and DU decides to deliver by G-RNTI or C-RNTI. If in the future, RLC feedback is supported for MRB, DU can decide retransmission using PTP or PTM. For HARQ retransmission via C-RNTI or G-RNTI, it is up to RAN1. |
| Huawei | Disagree. For per UE retransmission and for gap-filling transmission after handover, the gNB-DU does not have the information to decide to send the data via PTP. In these cases, the gNB-CU can send these packets to the gNB-DU via UE specific tunnel(s), then DU will know it should send them to the UE via PTP. |

3.1.4	Support of PTP only configuration. There are two approaches:

1) although possible as per RRC configuration, F1(/E1) does not foresee explicit support of PTP only configuration

2) F1/E1 does provide explicit support of PTP only configuration.

| Company | Comment |
| --- | --- |
| Ericsson | please go for 1), reducing options, keeping the system simple and avoiding DU-CU communication if for once, “PTP-only” needs to re-configured to “PTP/PTM”. |
| Nokia | 2) I assume the question refers to the support of non-split MRB PTP bearer. Given RAN2 recent decision to not enable deactivation of the PTM leg of a split MRB bearer, there are cases where it is useful to change the bearer type for a UE from split MRB into non-split MRB PTP bearer. See tdoc R3-214791 for details. |
| Qualcomm | Based on Nokia feedback on RAN2 decision, it seems that 2) is the only option. |
| Huawei | 2) We should align with RAN2 decision. For an MRB configured with PTP leg only, whether shared F1 tunnel or UE dedicated F1 tunnel to be used should be discussed by RAN3, as mentioned in contributions [6][11]. |

## MBS Session Resource Context Control

3.2.1	E1AP: Introduce a setup of E1 procedures to control NR MBS resources in gNB-CU-UP including NG-U and F1-U terminations common for BC and MC. FFS whether this works on MRB context or MBS Session level.

| Company | Comment |
| --- | --- |
| Ericsson | agree, we would prefer E1 procedures to work on MBS session level |
| Nokia | Disagree. The tunnel termination could be piggy-backed together with the first UE context setup. |
| Huawei | Disagree. Better to align with the way used for NG for MC and BC. |

3.2.2	F1AP: Turn the WA: For Multicast, reuse the existing UE-associated F1AP procedures to provide per UE the joined MBS Session IDs into an agreement

| Company | Comment |
| --- | --- |
| Ericsson | agree |
| Nokia | Agree. |
| Huawei | Agree. |

3.2.2	F1AP: For MC, shall MBS Session information be provided

1) via UE associated F1-C signaling or

2) via “shared” “MBS session associated” signaling

and hence control of shared resources be achieved

1) by UE-associated signaling or

2) by “MBS session associated” signaling?

| Company | Comment |
| --- | --- |
| Ericsson | In order to keep UE associated resource handling separate from shared MBS session resource handling, we propose to go for 1), i.e. introduce “MBS session associated” signaling procedures, which can be nicely used for MC and BC. This is a straightforward, allows to nicely separate MBS resource control from individual resource control and is the only reasonable stage-3 design choice. |
| Nokia | We prefer the UE-associated way which can piggyback the MBS session information, therefore 1). This can save the addition of non-UE associated procedure by piggybacking the MBS context and the shared tunnel addresses. Overall simpler. |
| Huawei | Prefer 1) |

3.2.3	F1AP: RAN2 shall design RRC in a way that MBS Session related RRC Configuration for the Lower Layers residing in the gNB-DU in a way that the identical content of the DU to CU RRC Information container can be added to the all the UEs that have joined the multicast session

| Company | Comment |
| --- | --- |
| Ericsson | agree |
| Nokia | I would refrain from talking in the name of RAN2. |
| Qualcomm | Agree |
| Huawei | Same view with Nokia, it is up to RAN2. |

## F1-U Flow Control for NR MBS

3.3.1: It is proposed to turn the WA
WA: For Broadcast and Multicast, optional use of DL flow control in the shared F1-U tunnel. 
into an agreement

Please provide your view below

| Company | Comment |
| --- | --- |
| Ericsson | agree |
| Nokia | Agree. |
| Qualcomm | Agree |

3.3.2: It is proposed that for BC no additional specification work is needed for F1-U flow control

please provide your view below

| Company | Comment |
| --- | --- |
| Ericsson | agree |
| Nokia | Some clarification to TS 38.425 is useful. |
| Qualcomm | Agree. No actual frame change, just some clarification. |
| Huawei | Same view with Nokia. Need some clarification. |

We seem to have two options on the table to progress with specification of F1-U flow control for multicast NR MBS, if applied, in case multiple RLC entities are involved:

1) minimum approach: no additional specification work, with the option to specify explicitly that behaviour of gNB-DU is implementation matter.

2) extensive approach: specify additional details of gNB-DU as e.g. in [2], [14], [15]

| Company | Comment |
| --- | --- |
| Ericsson | we suggest 1) |
| Nokia | We prefer 2) because some specification is needed in TS 38.425. |
| Qualcomm | Prefer 2 |
| Huawei | Agree with Option 2). Some clarifications in TS 38.425 is needed, as R3-215143. Reuse existing PDU Type 0 and Type 1 to support flow control for multicast and broadcast. For MRB with PTM leg, the ‘Highest transmitted/delivery NR PDCP Sequence Number’ could be reused to indicate the Highest transmitted/delivery NR PDCP Sequence Number of the slowest UE within the cell or the DU. in case there is no PTP-AM leg, reuse the ‘Highest transmitted NR PDCP Sequence Number’, in case there is PTP-AM leg, reuse ‘Highest delivery NR PDCP Sequence Number’. |

# References

R3-215043	Further Consideration on MBS Bearer Management over F1E1 (CATT), discussion

R3-215044	Further Consideration on Flow Control Mechanism over F1-U (CATT), discussion

R3-215046	TP for 38.463 on MBS Bearer Management at E1 interface (CATT), other

R3-215141	(TPs to TS 38.401 38.470, 38.460 BL CRs) Bearer management for Broadcast (Huawei, CBN, Nokia, Nokia Shanghai Bell, China Unicom, China Telecom, CMCC), other, 38.401

R3-215142	(TPs to TS 38.401, 470, 460 BL CRs) Bearer Management for Multicast (Huawei, CBN, China Unicom, China Telecom, CMCC), other, 38.401

R3-215143	(TP to TS 38.425 BL CR) Flow Control for MBS (Huawei, CBN, China Unicom, China Telecom), other, 38.425

R3-215205	On Bearer Management over E1/F1 (Ericsson), other

R3-215206	[TP for BL CR 38.473, 38.463] On Bearer Management over E1/F1 (Ericsson), other, 38.473

R3-215272	(TP to TS 38.460 BL CR) Support of Multicast Distribution Setup and Release (Lenovo, Motorola Mobility, Huawei, Qualcomm Incorporated), other

R3-215273	(TP to TS 38.463 BL CR) Support of Multicast Distribution Setup and Release (Lenovo, Motorola Mobility, Huawei, Qualcomm Incorporated), other

R3-215274	Remaining Issues on F1 Interface for MBS (Lenovo, Motorola Mobility, discussion

R3-215372	(TP to TS 38.425 BL CR) FLow Control over F1 for NR MBS (ZTE), other

R3-215373	(TP to TS 38.473 BL CR) Bearer Management over F1 for NR MBS (ZTE), other

R3-215516	Flow control for MBS multicast session (Samsung), other

R3-215673	Discussion on MBS Bearer Management (CMCC), discussion

R3-215138	Consideration on Multicast Session Management (Huawei, CBN, Lenovo, Motorola Mobility, Qualcomm Incorporated, China Unicom, China Telecom), other (partly, proposal 9)