3GPP TSG-RAN WG3 #114-e							R3-215863

1 November – 11 November 2021

Online

Agenda Item:	14.2

Source:	ZTE (moderator)

Title:	Summary of Offline Discussion on MRDC2 - SCG (de)activation

Document for:	Approval

# Introduction

CB: # MRDC2_SCGActivation_Deactivation

- Check details of the proposed TPs which shall reflect the agreements

- Support partial rejection for SCG (de)activation during SN addition in XnAP/X2AP? New cause value(s) for the SCG (de)activation rejection?

- CU/CU-CP makes the final decision of SCG (de)activation based on the assisting information obtained from CU-UP and DU, FFS the content of the assisting information? CU-CP sets the specific criteria to CU-UP and DU for SCG (de)activation?

- F1 and E1 impact?

- Check RAN2 progress on the SCG activation method for the uplink data coming

- Capture agreements as stage2/stage3 CRs and check details, split work, if needed

- List open issues for next meeting in the summary

(ZTE - moderator)

Summary of offline disc R3-215863

It is proposed to divide the discussion into two phases:

-	Phase 1: Identify the issues to be discussed in RAN3

Deadline: Please provide your views by 4:00am UTC Wednesday November 3rd

-	Phase 2: Further discussion to capture agreements and open issues

Deadline: TBD pending on the outcome of Phase 1

# For the Chairman’s Notes

[TBD]

# Phase 1 discussion

Please note that some terms in the discussion part refer to the following meanings:

Partial rejection: SCG (de)activation request is rejected when accepting the whole procedure.

Full rejection: The whole procedure is rejected due to the rejection of SCG (de)activation request.

SCG (de)activation during MN initiated SN modification: MN requests SCG (de)activation during MN initiated SN modification

SCG (de)activation during SN addition: MN requests SCG (de)activation during SN addition

## Partial/full rejection of SCG (de)activation

In the last meeting, we have agreed to support partial rejection for SCG deactivation during MN initiated. But the other cases are still FFS, e.g. SN addition and MN requests SCG activation during MN initiated SN modification.

According to the contributions, almost all the companies propose to support partial rejection for SCG deactivation during SN addition. The following reasons are presented.

- In case of inter-MN handover without SN change, if there is SN-terminated SCG bearer and the target MN is not aware of, then the full rejection from SN would fail the handover procedure [1].

- The motivation for SCG deactivation is energy saving when additional throughput is not needed, not load in the SCG [3].

- During SN addition procedure, the first selected SN should be the best SN for the UE. Full rejection may lead to unnecessary SN change and signalling overhead [9][11].

Question 1: Do companies agree that partial rejection shall be supported for SCG deactivation during SN addition?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | SN is the controller of SCG, and thus the flexibility shall be allowed |

In moderator’s view, as long as RAN3 agrees to support partial rejection for SCG deactivation during SN addition, a new indicator with two codepoints, e.g. SCG Activation Response IE, needs to be added in SN addition request acknowledge message to indicate the SCG is activated or deactivated.

Question 2: Do companies agree to add a new indicator with two codepoints, e.g. SCG Activation Response IE, in SN Addition Request Acknowledge message to indicate the SCG is activated or deactivated?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | A new indicator is needed if partial rejection is allowed for SCG deactivation during SN addition. |

However, for the cases of SCG activation during SN addition procedure or MN initiated SN modification procedure, it is hard to reach a consensus according the contributions. The reasons for each camp are listed as follows.

MN initiated SN modification

Partial rejection:

- If MN requests SCG activation to let SN support a new QoS flow, SN may reject the request and configure a SN terminated MCG bearer for the new QoS flow due to lack of SCG resources or power saving [9].

Full rejection:

- SN may reject the request of SCG state change while accepting the SN modification request only in case of bearer type change or ongoing traffic on the SN-terminated SCG DRB. SN should simply fail the whole procedure in other cases [1].

- As required in the WID, SN shall activate the SCG when it is needed due to data increases [3].

SN addition

Partial rejection:

- The first selected SN should be the best SN for the UE. Full rejection may lead to unnecessary SN change and signalling overhead [9][11].

- It is more efficient to support partial rejection. The SN modification procedure can be used to (de)activate the SCG when it is needed. Or MN can trigger SN release or SN change [13][15].

Full rejection:

- MN initiates the SCG activation for the purpose of offloading, thus it is not the obligatory for MN to choose and select certain SN and wait for its resources for activated SCG [1].

- As required in the WID, SN shall activate the SCG when it is needed due to data increases [3].

- The argument that later MN can initiate SN release if partial rejection is supported, this will absolutely waste the signalling as the MN has no intention to keep the SN [7].

Furthermore, a compromise solution is proposed in [3] which proposes to use three codepoints for the indicator, e.g. “activate”, “deactivate”, and “activate or reject”. The third codepoint “activate or reject” is used to indicate that SCG is indeed desperately needed and it shall be activated.

Form moderator’s point of view, we have already discussed this issue in several meetings, and for the sake of progress, it is suggested to follow the majority view.

Question 3: Companies are kindly asked which option below is preferred for the rejection of SCG activation during SN addition.

- Partial rejection with two codepoints

- Partial rejection with three codepoints

- Full rejection

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | 1) | There is scenario that requires supporting partial rejection for SCG activation during SN addition. It could be better to allow this flexibility since it seems harmless. A smart SN can decide whether to use partial rejection or legacy rejection. |

Question 4: Companies are kindly asked which option below is preferred for the rejection of SCG activation during MN initiated SN modification.

- Partial rejection with two codepoints

- Partial rejection with three codepoints

- Full rejection

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | 1) | There is scenario that requires supporting partial rejection for SCG activation during SN addition. It could be better to allow this flexibility since it seems harmless. A smart SN can decide whether to use partial rejection or legacy rejection. |

## New cause value

In the last meeting, we have made a WA on defining a general cause value to indicate the request is rejected due to the rejection of SCG (de)activation. It is FFS whether specific reasons shall be defined. According to the contributions, half companies propose to use general cause value, and half companies propose to use specific cause values. From moderator’s point of view, it is indeed beneficial to use specific cause values to provide additional information. However, it is not quite necessary considering the complexity. So companies that support the use of specific cause values are encouraged to provide the cause values that shall be introduced to further assess the complexity.

Question 5: Companies are kindly asked which option below is preferred for the new cause value. If option 2) is preferred, please provide the cause values that shall be introduced.

- General cause value

- Specific cause values

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | 1) | SCG (de)activation is a simple function and it’s not necessary to include the specific rejection reason. This may cause unnecessary signalling and slow down the whole procedure. |

## E1/F1 interface related issues

In previous meetings, we have agreed that F1 signalling enhancement shall follow the principle of X2/XnAP signalling enhancement. However, in the last meeting, some companies suggested to reconsider whether DU can initiate SCG (de)activation via UE Context Modification Required, which has already been captured in the latest F1AP BLCR (R3-214644).

From moderator's point of view, SCG resource is stored in SN-DU, thus SN-DU is completely aware of SCG resource status. For example, if SN-DU acknowledges no user data expected or wishes to save power, it can require SN-CU to deactivate SCG, then the SN-CU finally decides to accept or reject the request from SN-DU. In order for SN-CU to make a good decision, it shall interwork with MN before acception or rejection. If the gNB-DU is allowed to initiate SCG (de)activation via UE Context Modification Required message, it is simple for us to just remove the Editor's note and keep the corresponding contents in the BLCR.

Question 6: Do companies agree that gNB-DU can request SCG (de)activation via UE Context Modification Required message, and gNB-CU fianlly decides to accept or reject the request?

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | Yes | This WID aims to save energy via SCG (de)activation. Therefore, from the perspective of energy saving, it could be better to allow DU to request SCG (de)activation. |

Next issue is whether E1 interface enhancement is needed. It seems to be common understanding that CU-UP shall be aware of the SCG (de)activation state, and the controversial issue is which solution shall be chosen to achieve that. According to the contributions, two options are proposed, including 1) using E1 signalling to inform CU-UP and 2) using flow control mechanism. The flow control mechanism can be achieved by setting the desired buffer size to be 0 or using a cause value “radio link outage” in the Downlink Data Delivery Status procedure [12][16]. The reasons for each camp are listed as follows.

E1 signalling:

- NR PDCP entity just considering the radio link is unavailable when it receives an indication of radio link outage, and it is needed to clarify that it also indicates SCG deactivation [12].

- In terms of time delay, the E1 signalling is CU-CP->CU-UP and CU-CP->SN-DU at the same time while the flow control mechanism is CU-CP->SN-DU->CU-UP, so the E1 signalling has lower latency [12][16].

- In case that the CU-CP wants to deactivate SCG when CU-UP has ongoing data transmission with the SN-DU, or has data to be transmitted to the SN-DU, CU-UP can reject the SCG deactivation directly via E1 signalling, but it has to trigger SCG activation to the CU-CP using flow control mechanism [12].

- Setting the buffer size to be 0 in the flow control can stop CU-UP transferring DL data to DU, however CU-UP will not distinguish whether it is caused by SCG deactivation or by lack of resources in the DU. Which might have backward compatibility issue as well [16].

- Downlink Data Delivery Status procedure is triggered by DU based on implementation, it is not mandated in the legacy when the procedure shall be triggered [16].

- The desired buffer size is per radio bearer. To stop all SCG DL data transfer, DU has to trigger Downlink Data Delivery Status for all SCG radio bearers [16].

- Some mandatory fields in the Downlink Data Delivery Status PDU, i.e., flags in the header, may not be useful at all in case of SCG activation/deactivation [16].

- The Downlink Data Delivery Status is transmitted via F1-U which is less reliable compared to via E1 signalling [16].

Flow control mechanism:

- Flow control is faster than E1 signalling, so when DL data appears for SCG then the UP can start sending is sooner if it waits for flow control information only. Waiting for CP indication once SCG is activated may introduce unnecessary delay [3].

- It has fewer specification impacts comparing to E1 signalling [12].

To support the E1 signalling solution, [9][12][16] believe that a new indicator shall be added in the Bearer Context Setup Request and Bearer Context Modification Request message to let CU-UP be aware of SCG (de)activation. [12][16] also think that partial rejection may be needed in case CU-CP triggers SCG deactivation while CU-UPs have ongoing data transmission towards the SN-DU for SCG/split bearer. [12] believe that a new indicator shall also be added in the Bearer Context Setup Response and Bearer Context Modification Response message. As for the flow control mechanism, [12] believe that only some clarifications need to be added.

Question 7: Companies are kindly asked whether CU-UP shall be aware of the SCG (de)activation state. If yes, which option below is preferred?

- E1 signalling

- flow control mechanism

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | 1) | Using E1 signalling is more straightforward. FFS on the detailed enhancements. |

Another remaining issue is how CU/CU-CP obtains the assisting information from DU or CU-UP to make the final decision of SCG (de)activation. The legacy E1 and F1 inactivity notification mechanisms are widely discussed. Some companies believe using legacy mechanisms are sufficient to provide the assisting information, while some companies believe they need to be enhanced. From moderator’s point of view, we have agreed that RAN3 does not enhance Activity Notification to support SCG (de)activation for the MN/SN initiated SCG (de)activation. Thus, it could be better to align E1AP and F1AP with XnAP, e.g. do not enhance E1 and F1 inactivity notification mechanisms to support SCG (de)activation.

Question 8: Do companies agree that E1 and F1 inactivity notification mechanisms shall not be enhanced to keep align with XnAP?

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | Yes | No need to enhance the inactivity notification mechanisms for E1AP and F1AP. The legacy mechanisms are sufficient to help CU-CP make a good decision. |

Some companies propose to discuss the HO signalling. From moderator’s point of view, we have already discussed this issue in previous meetings, and made a conclusion in the RAN3 #112 e-meeting that we shall wait for RAN2 progress before further discussing this issue [20]. Therefore, to avoid repeated discussions in RAN3, moderator suggest to postpone the discussion of HO signalling until RAN2 makes further progress .

The other issues proposed in the contributions, such as IE naming, may be discussed in the second round.

# Phase 2 discussion

# Conclusion, Recommendations [if needed]

If needed

# References

R3-214765	(TP for SCG BL CR to TS 37.340) Handling of network rejection for SCG (de)activation (Ericsson)	other

R3-214766	(TP for SCG BL CR to TS 38.423) Handling of network rejection for SCG (de)activation (Ericsson)	other

R3-214807	(TP to SCG BL CR to 38.423, LTE_NR_DC_enh2-Core) Completion of the solution for the SCG activation state change (Nokia, Nokia Shanghai Bell)	other

R3-214808	(TP to SCG BL CR to 36.423, LTE_NR_DC_enh2-Core) Completion of the solution for the SCG activation state change (Nokia, Nokia Shanghai Bell)	other

R3-214877	(TP to BL CR of TS38.401) Discussion on the SCG (de)activation (Samsung)	other

R3-214878	(TP to BL CR of TS38.473) Discussion on the SCG (de)activation (Samsung)	other

R3-214941	(TP for SCG BL CR to TS36.423) Acceptance / Rejection of SCG Activation / Deactivation (NEC)	other

R3-214942	Assisting information for SCG Activation / deactivation on E1 (NEC)	discussion

R3-215006	TP for SCG BL CR to TS38.423 36.423 38.463 (ZTE)	other

R3-215007	TP for SCG BL CR to TS 38.473 (ZTE)	other

R3-215107	(TP to 38.401 SCG BL CR) SCG activation and deactivation (Huawei)	other

R3-215108	(TPs to 38.463 38.425 SCG BL CR) SCG activation and deactivation (Huawei)	other

R3-215111	Discussion on efficient Activation/Deactivation for SCG (CATT)	discussion

R3-215112	(TP for SCG BLCR for TS 38423)efficient Activation/Deactivation for SCG (CATT)	other

R3-215325	Left issues on SCG activation and deactivation (Lenovo, Motorola Mobility)	discussion

R3-215326	Discussion on SCG activation and deactivation impact on E1 interface (Lenovo, Motorola Mobility, ZTE, NEC, Samsung)	discussion

R3-215327	Support of SCG Activation and Deactivation (Lenovo, Motorola Mobility)	CR0623r1, TS 38.463 v16.7.0, Rel-17, Cat. BR3-213940	Discussion on efficient Activation/Deactivation for SCG (CATT)	discussion

R3-213941	(TP for [LTE_NR_DC_enh2-Core] SCG BLCR for TS 38423) efficient Activation/Deactivation for SCG (CATT)	CR0660r, TS 38.423 v16.6.0, Rel-17, Cat. B

R3-212993	SCG BL CR to TS 38.473(Samsung) CR0777r0, TS 38.473 v16.5.0, Rel-17, Cat. B

R3-212784	Summary of offline discussion on SCG activation and deactivation