3GPP TSG-RAN WG3 #114-e                                                                                  R3-215886

01 – 11 Nov 2021

Agenda Item:	21.3

Source:	ZTE (moderator)

Title:	Summary of Offline Discussion on New QoS Related Parameters

Document for:	Approval

# Introduction

CB: # NRIIOT2_NewQoS

- The maximum value of survival time? The available survival time within the TSC Assistance Information IE is introduced over Xn and F1 interfaces?

- The maximum value of periodicity should be extended to 60000000 us or not needed?

- TPs if agreeable

(ZTE - moderator)

Summary of offline disc R3-215886

Please provide your views by 8:00 UTC Wednesday November 3nd so that they may be taken into account during the online session.

# For the Chairman’s Notes

[TBD]

# Discussion (Phase 1)

At RAN3#113e, the following agreements and open issues for the new QoS parameters (survival time) was captured in the Chair’s Minutes:

The working assumptions is agreed, i.e. supporting the Survival Time for both downlink and uplink.

The granularity of the survival time is 1 us (i.e. the same as the Periodicity IE).

The maximum value of the survival time should be at least 3 times the maximum value of the Periodicity IE.

No RAN3 actions are needed for the TSN service in acknowledge mode, unless further action is required by other groups.

Keep the current Survival time encoding unchanged in the BLCRs.

To be continued...

In the following, we take each related question in a separate section.

## The maximum value of the periodicity

The following papers propose whether it is necessary to extend the maximum value of the periodicity.

- In R3-215133, only the top three rows in TS 22.104 will be considered. In addition, in TS 38.331, the periodicity of the ConfiguredGrantConfig used to configure uplink transmission without dynamic grant is set as maximum of 640 ms. Hence there is no need to extend the periodicity.

- In R3-215123, these two use cases with transfer intervals up to 60s in 22.104 are very important cases when the Periodic deterministic communication is provided by 5G system. So the maximum value of the periodicity should be chosen based on the required use case from 22.104 instead of the CG/SPS periodicity maximum value.

Moderator’s Summary and Proposal:

Based on the email discussion from the last meeting, majority companies agree that there is no need to increase the maximum value of the periodicity and only one company propose to increase the maximum value of the periodicity.  So, the moderator intends to have the following proposal.

Proposal: No need to increase the maximum value of the periodicity.

Question 1: Do you agree the above Moderator proposal?

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes | Although we initially wanted to increase the maximum value of the periodicity, we could accept no enhancements in order to reach a quick agreement. |
| Huawei | Yes |  |

Proposed conclusion: Capture the following in the Chair’s Notes:

## The maximum value of survival time

The following values are proposed as seen from the contributions to this meeting.

- R3-215123 proposes to be 180s.

- R3-214737 proposes to be 1.92s (i.e. 3 times the maximum value of the Periodicity IE).

- R3-214830, R3-215083 and R3-215133 propose to be 6.4s (i.e. 10 times of the maximum value of the Periodicity IE).

Moderator’s Summary and Proposal:

3 companies support 10 times of Periodicity, one company supports 3 times of Periodicity, and another company proposes 180s.

Question 2: For the maximum value of the survival time, which of the following options do companies prefer?

- Option 1: 180s

- Option 2: 1.92s

- Option 3: 6.4s

| Company | Option preferred | Comments |
| --- | --- | --- |
| ZTE | Option2 | If the maximum value of the periodicity is increased to 60s, we also agree to Option1. In addition, we think that 3 times of the periodicity can meet the requirements and there is no need to expand to 10 times. |
| Huawei | Option 3 | Option 2 is also acceptable to us. No big issue since these large values will not be used considering the TSN strict requirements. |

Proposed conclusion: Capture the following in the Chair’s Notes:

## The survival time during handover

The following papers propose that the Survival Time assistance information is transmitted during the handover.

- In R3-214737, based on the definition of Survival Time, the Survival Time measurement needs to take into account the time of handover interruption or wireless link failure recovery.  During the handover, two cases about the measurement of Survival Time need to be considered:

- Case 1: In the handover process, the Survival Time has exceeded the allowed range because the packet has not been sent for a long time.

- Case 2: In the handover process, the Survival Time does not exceed the allowed range. That means, at least the target gNB has one opportunity to receive/send packets before the Survival Time exceeds the allowed range.

- In R3-214830, it proposes to introduce Available Survival Time within the TSC Assistance Information IE transferred over Xn and F1. The main motivation there is that it is essential for the target gNB to know the AST, so it can determine the level of reliability that is needed when transmitting the first packet following handover.

- In R3-215083, it proposes that the Available Survival Time only for downlink is delivered over Xn and F1 interfaces during the handover. In case of uplink packet transmission, it would not be clear how the source node could estimate the remaining survival time and whether the Available Survival Time for uplink transmission could provide the benefit.

- In R3-215133, the Source NG-RAN can transfer the separate survival time state for the uplink and downlink to the target NG-RAN as an assistance information to help the target NG-RAN determine the scheduling scheme both for uplink and downlink. Below lists several possible ways to transfer the Survival Time assistance information :

- Option 1: The available the survival time as proposed in R3-213448.

- Option 2: The survival timer running duration or the timing when the survival timer is triggered running.

- Option 3: A simple survival time state indicator (activated or not)

Moderator’s Summary and Proposal:

Based on the email discussion from the last meeting, majority companies think the Available Survival Time is beneficial during the handover. In this meeting’s contributions, the main concerns are: whether the Survival Time assistance information involves uplink and downlink, whether the Survival Time assistance information involves Xn and F1, and the content of Survival Time assistance information, whether the Survival Time measurement needs to take into account the time of handover interruption or wireless link failure recovery. The following questions are used to collect companies’ opinions and clarify the concerns.

Question 3a: For uplink Survival Time assistance information, which of the following options do companies prefer to deliver during handover?

- Option 1: Available survival time (the remaining survival time of the total ST)

- Option 2: The survival timer running duration

- Option 3: A survival time state indicator (activated or not)

- Option 4: none

- Option 5: others

| Company | Option preferred | Comments |
| --- | --- | --- |
| ZTE | Option 4 | Since the uplink ST information is kept in UE, no uplink Survival Time assistance information need to be delivered between RAN interfaces. |
| Huawei | Either Option 2 or option 3 | For UL, the NG-RAN can also be aware of the UE entering into ST state since it is the NG-RAN that generates/sends the retransmission grant containing e.g. the NDI indication. Also especially for period traffic, RAN could be aware if the UL data is missing in this period. Option 1 is also acceptable to us. |

Question 3b: If the answer to question 3a is not “option 4”，which interface(s) do companies prefer to deliver the uplink Survival Time assistance information?

- a): XnAP

- b): F1AP

- c):Xn-U

- d) F1-U

- e) others

| Company | Interface(s) to deliver the uplink Survival Time assistance information | Comments |
| --- | --- | --- |
| Huawei | a), and NGAP F1AP is FFS | The F1AP impact is pending on the solution. For example, if option 3 is agreed, then the CU can be aware of the ST state due to the periodical service. |

Question 4a: For downlink Survival Time assistance information, which of the following options do companies prefer to deliver during handover?

- Option 1: Available survival time (the remaining survival time of the total ST)

- Option 2: The survival timer running duration

- Option 3: A survival time state indicator (activated or not)

- Option 4: none

- Option 5: others

| Company | Option preferred | Comments |
| --- | --- | --- |
| ZTE | Option 3 | We think the Downlink ST assistance information can be used for target eNB to determine whether to enter DL ST state quickly when transmitting the first packet following handover. However, the ST timer is per PDU in the user plane, it is difficult to deliver PDU level Timer to the target gNB during HO. Therefore, we think that the simplest way is to send a ST state indicator (activated or not) to the target gNB through the control plane. |
| Huawei | Either Option 2 or option 3 | Option 1 is also acceptable to us. |

Question 4b: if the answer to question 4a is not “option 4”，which interface(s) do companies prefer to deliver the downlink Survival Time assistance information?

- a): XnAP

- b): F1AP

- c):Xn-U

- d) F1-U

- e) others

| Company | Interface(s) to deliver the downlink Survival Time assistance information | Comments |
| --- | --- | --- |
| ZTE | a) | It is beneficial to deliver the DL ST state indicator over Xn interface as our comments for Q4a. And for the gNB-CU/gNB-DU split case, since the DL ST timer is maintained in MAC, only the gNB-DU knows and uses the DL ST state(e.g. whether the DL ST timer is activated or not). for the DL ST state indicator delivery, the source gNB-DU should deliver the DL ST state indicator to the source gNB-CU and the target gNB-CU should further deliver the DL ST state indicator to the target gNB-DU. |
| Huawei | a), and NGAP F1AP is FFS. | The F1AP impact can be further discussed if there is any agreement on NGAP/XnAP. |

Question 5a: Whether the Survival Time measurement needs to take into account the time of handover interruption or wireless link failure recovery?

| Company | Yes or No | Comments |
| --- | --- | --- |
| ZTE | No | Since the DL ST timer is counted per PDU, and will run either in the source gNB or in the target gNB, which will not be impacted by the handover interruption or wireless link failure recovery (e.g. Uu interruption). So, it is not necessary to consider the time of handover interruption or wireless link failure recovery for the Survival Time measurement. |
| Huawei |  | Not clear the question to us. Is the question related to the decision of source NG-RAN to send the ST state during the handover? Then yes, the source NG-RAN can send the ST state or variants in case it thinks this is beneficial, e.g. for DAPS handover, or the ST value is large. And we understand this is up to the discretion of the source node, and no specification impact is foreseen. |

Question 5b:  If the answer to question 5a is “Yes”，what will be the specification impacts except delivering the Survival Time assistance information(if any)?

| Company | Comments |
| --- | --- |

Proposed conclusion: Capture the following in the Chair’s Notes:

# Conclusion, Recommendations [if needed]

If needed

# References

| R3-214737 | (TP for Introduction of Enhanced IIoT support over NG/Xn/F1/E1) Analysis of New QoS Related parameters (ZTE) | other |
| --- | --- | --- |
| R3-214830 | (TP for NR_IIOT_URLLC_enh BL CR for TS 38.423) Survival Time and handover (Nokia, Nokia Shanghai Bell) | other |
| R3-215083 | Discussion on the remaining issues for the Survival Time (Samsung) | discussion |
| R3-215123 | Discussion on new QoS related parameters (CATT) | discussion |
| R3-215124 | (TP for BLCR for TS 38413) new QoS related parameters (CATT) | other |
| R3-215133 | (TP for eIIOT BLCR for TS 38.473) Survival time remaining issues (Huawei) | other |