3GPP TSG-RAN WG3#114			R3-215950

E-Meeting, 1 – 11 November 2021

Title:	LS on Clarification of SCG outside RA for slicing

Response to:

Release:	Rel-17

Work Item:	NR_Slice

Source:	RAN3

To:	RAN2

Cc:

Contact Person:

#### Name:	Philippe Godin

Tel. Number:	+33 1 6040 0304

E-mail Address:	philippe.godin@nokia.com

Attachments:

1. Overall Description:

RAN3 is discussing a solution to address temporary resource shortage for a slice 1 in a gNB cell called Multi Carrier Resource Sharing solution. This solution assumes that the gNB hosts another cell with different frequency and overlapping coverage where the same slice 1 is available. It consists of setting up DC using SCG resources on the “other cell” for offloading the PDU sessions of slice 1 of some or all UEs.

RAN3 is not sure it gNB can select such “other cell” outside of the RA (registration area) of the concerned UE.

There are two views:

- View 1: the “other cell” can be outside the RA as long as the slice 1 for the PDU session is supported by the “other cell”.

- View 2: the current “Allowed NSSAI” which the gNB has received in context setup from 5GC is an allowance only in the current RA of the UE. Therefore, the gNB cannot be sure that it is allowed for this UE to consume resources of slice 1 in that “other cell” which is outside the RA. It should therefore not do it.

2. Actions:

To SA2 group:

ACTION: 	RAN3 kindly ask SA2 to give guidance between view 1 and view 2.

3. Date of Next TSG-RAN WG3 Meetings:

TSG-RAN WG3#114bis-e                       17 – 26 January 2021			E-meeting