3GPP TSG-RAN WG3 #114-e	R3-215875

Online, 1 – 11 Nov, 2021

Agenda Item:	17.3

Source:	ZTE(moderator)

Title:	Summary of Offline Discussion on CB: # RANSlicing3_UESliceMB

Document for:	Approval

# Introduction

This contribution is to kick off the following discussion.

CB: # RANSlicing3_UESliceMBR For UE slice MBR: - The S-MBR is signaled to the RAN for network slices with PDU Sessions that have an active user plane at the UE? E/// - Include the UE-slice-MBR in the Allowed NSSAI IE? Huawei, CATT - In split architecture, which entity is used to enforce UL and DL slice MBR? How to handle UE-Slice-MBR enforcement in DC scenario? Samsung. For Target NSSAI: - To setup the dual connectivity based on the Target NSSAI and the corresponding RFSP index from the CN? Huawei - Introduce the Redirection Assistance Information IE containing the Target NSSAI IE and the corresponding Index to RAT/Frequency Selection Priority IE in the INITIAL CONTEXT SETUP REQUEST message and DOWNLINK NAS TRANSPORT message? LG - Introduce Target NSSAI IE in NGAP? ZTE For SSC mode 3 issue: - Check issue in SSC mode 3 operation when network slice admission control is performed? Samsung - Capture agreements and open issues - Provide CRs if agreeable, split work (ZTE - moderator) Summary of offline disc R3-215875

Please Note: plan to do two rounds of discussion in this meeting.

The first round email discussion plan to be end 2 hour before on-line session  1st week.(Wednesday 11:00 UTC, 2021-11-3)

The second round email discussion based on decision from on-line session.

# For the Chairman’s Notes

# First Round Discussion

### Impact on RAN slicing of UE slice MBR

### NGAP impact

Companies in [1][2][5] thinks UE Slice MBR IE should be carried in Allowed NSSAI IE, namely as part of the following messages:

- Initial UE Context Setup Request

- Handover Request

- PATH SWITCH REQUEST ACKNOWLEDGE

- DOWNLINK NAS TRANSPORT

- CONNECTION ESTABLISHMENT INDICATION

- INITIAL UE MESSAGE

- REROUTE NAS REQUEST

- UE INFORMATION TRANSFER

- UE CONTEXT MODIFICATION REQUEST[5]

Companies in [4][7][8] thinks signal the  UE Slice MBR in a way similar to the UE AMBR.namely as part of the following messages:

- Initial UE Context Setup Request

- Handover Request

- Path Switch Request Ack

- Downlink NAS Transport

- PDU Session Resource Setup Request

- UE Context Modification Request

It can be observed from the above options that the common part would be the first four messages in NGAP.

Proposal 1: To carry UE slice MBR information in the following messages of NGAP:

- Initial UE Context Setup Request

- Handover Request

- Path Switch Request Ack

- Downlink NAS Transport

Q1: Please provide your view on Proposal.

| Company | Do you agree the proposal. | Comment |
| --- | --- | --- |
| ZTE | Yes |  |

The different part of the impact due to different understanding of the SA2 specification.

Option 1[1][2][5] thinks UE Slice MBR IE should be carried in Allowed NSSAI IE, based on the description in SA2 as following:

5.15.13 Support of data rate limitation per Network Slice for a UE A UE subscription information may include an optional Slice Maximum Bit Rate for the UE (Subscribed UE-Slice-MBR) for an S-NSSAI, which applies for 3GPP access type only. The Subscribed UE-Slice-MBR includes a UL and a DL value. If a Subscribed UE-Slice-MBR is associated to an S-NSSAI in the subscription information, it is provided by the AMF to the RAN when the AMF provides the Allowed NSSAI for the UE to the RAN as UE-Slice-MBR QoS parameter. The UE-Slice-MBR QoS parameter is defined in clause 5.7.2.6. If the Subscribed UE-Slice-MBR for a UE changes, the AMF updates UE-Slice-MBR in the RAN accordingly.

While Option 2 [4][7][8] thinks to carry UE Slice MBR IE in a way like UE AMBR.

23.501: 5.7.1.10 UE-Slice-MBR enforcement and rate limitation If a supporting RAN receives for a UE a UE-Slice-MBR (see clause 5.7.2.6) for an S-NSSAI from the AMF, the RAN shall apply this UE-Slice-MBR for all PDU Sessions of that UE corresponding to the S-NSSAI which have an active user plane if feasible. In particular, the RAN shall enforce this UE-Slice-MBR as follows: As described in TS 23.502, “AMF to (R)AN: N2 Request (N2 SM information received from SMF, security context, Mobility Restriction List, UE-AMBR, List of UE-Slice-MBR(s) (optional and for 3GPP access type only),” a list of UE-Slice-MBR(s) should be transmitted from AMF to RAN, and this IE is an optional IE.

Q2: Please provide your view on options.

| Company | Option 1/2/other | Comment |
| --- | --- | --- |
| ZTE | Option 2 | 1: “ AMF to the RAN when the AMF provides the Allowed NSSAI for the UE to the RAN as UE-Slice-MBR QoS parameter” does not mean the IE should be carried in Allowed NSSAI IE. Take “INITIAL UE MESSAGE” as an example, in this message Allowed NSSAI is contained but UE-Slice-MBR should not contain in this IE. 2: Allowed NSSAI IE does not contained in XnAP while in order to enforce rate limitation, while for UE-AMBR or UE slice MBR, MN and SN should to negotiate the information. So in general the parameter is similar as UE-ABMR and signalling in option 2 should take as baseline in RAN. |

### UE-Slice-MBR for MR-DC scenario

Companies in  [8]thinks the impact of UE-Slice-MBR should consider MR-DC scenario,in this case MN and SN node should co-ordinate to meet the requirement together. For UE AMBR, it is MN takes the role of decision to allocate quota between MN and SN. Similar as UE AMBRE, it is reasonable to follow the same principle for UE-Slice-MBR. :

Proposal : The MN decides the split of DL UE AMBR bit rate limits among the MN and the SN. The NG-RAN node that hosts the PDCP entity enforces the respective DL UE Slice MBR bit rate limits. The NG-RAN node that hosts the MAC entity enforces the respective UL UE Slice MBR bit rate limits.

Company [7] propose: RAN3 agrees to introduce a List of SN UE- Slice-MBR (s) in S-NODE ADDITION REQUEST message and S-NODE MODIFICATION REQUEST in TS 38.423, to support the UE-Slice-MBR enforcement in dual connectivity scenario.

At this stage ,The Moderator would to take stage 2 as first priority and would like to consider following proposal at first. Detail messages can be consider later.

Proposal 2: The MN decides the split of DL UE AMBR bit rate limits among the MN and the SN. The NG-RAN node that hosts the PDCP entity enforces the respective DL UE Slice MBR bit rate limits. The NG-RAN node that hosts the MAC entity enforces the respective UL UE Slice MBR bit rate limits.

Q3: Please provide your view on proposal.

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes |  |

### UE-Slice-MBR for RAN split scenario

One company in [8] thinks the impact of UE-Slice-MBR should consider RAN split scenario, in this case CU-CP,CU-UP and DU node should co-ordinate to meet the requirement together. For UE AMBR, it is CU-CP takes the role of decision to allocate quota between nodes. Similar as UE AMBRE, it is reasonable to follow the same principle for UE-Slice-MBR. :

Proposal : The CU-CP decides the split of DL UE AMBR bit rate limits among the CU-UP and DU. The NG-RAN node that hosts the PDCP entity enforces the respective DL UE Slice MBR bit rate limits. The NG-RAN node that hosts the MAC entity enforces the respective UL UE Slice MBR bit rate limits.

One company in [7]  propose: Proposal 3, RAN3 agrees to introduce a List of UL UE-Slice-MBR(s) in UE CONTEXT SETUP REQUEST message and UE CONTEXT MODIFICATION REQUEST message in TS 38.473, to support the UL UE-Slice-MBR rate control in gNB-DU,

Proposal 4, RAN3 agrees to introduce a List of UE-DL-Slice-MBR (s) in BEARER CONTEXT SETUP REQUEST message and BEARER CONTEXT MODIFICATION REQUEST message in TS 38.463, to support the DL UE-Slice-MBR enforcement in RAN.

One company in [11] propose:

- For E1 interface:

- BEARER CONTEXT SETUP REQUEST

- BEARER CONTEXT MODIFICATION REQUEST

- For F1 interface:

- UE CONTEXT SETUP REQUEST

- UE CONTEXT MODIFICATION REQUEST

At this stage ,The Moderator would to take stage 2 as first priority and would like to consider following proposal at first. Detail messages can be consider later.

Proposal 3: The CU-CP decides the split of DL UE AMBR bit rate limits among the CU-UP and DU. The NG-RAN node that hosts the PDCP entity enforces the respective DL UE Slice MBR bit rate limits. The NG-RAN node that hosts the MAC entity enforces the respective UL UE Slice MBR bit rate limits.

Q4: Please provide your view on proposal.

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes |  |

### Target NSSAI

One company in [9] propose-to introduce Target NSSAI IE in the following messages for NGAP including:

INITIAL CONTEXT SETUP REQUEST

HANDOVER REQUEST

PATH SWITCH REQUEST ACKNOWLEDGE

DOWNLINK NAS TRANSPORT

Connection Establishment Indication

AMF CP RELOCATION INDICATION

UE INFORMATION TRANSFE

REROUTE NAS REQUEST

One company in [10] propose Introduce the Redirection Assistance Information IE containing the Target NSSAI IE and the corresponding Index to RAT/Frequency Selection Priority IE in the INITIAL CONTEXT SETUP REQUEST message and DOWNLINK NAS TRANSPORT messsage.

One company in [11] propose :

The Target NSSAI and the corresponding RFSP index are delivered over the following NGAP messages:

INITIAL CONTEXT SETUP REQUEST

DOWNLINK NAS TRANSPORT

RAN3 is kindly asked to discuss to setup the dual connectivity based on the Target NSSAI and the corresponding RFSP index from the CN.

The common part of the proposals are :

Proposal 4: To introduce Target NSSAI IE in the following messages for NGAP:

INITIAL CONTEXT SETUP REQUEST

DOWNLINK NAS TRANSPORT

Q5: Please provide your view on this proposal.

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes |  |

### Issue in SSC mode 3

One company [7]  thinks if network slice admission control is performed in NG-RAN, there will be an issue in SSC mode 3 that service continuity cannot be kept.

Proposal 5: RAN3 acknowledges the issue in SSC mode 3 operation when network slice admission control is performed.

Proposal 6, RAN3 to introduce an SSC mode indication or the related information (e.g. the old PDU session id and/or the left PDU session address lifetime) in NGAP to help the serving gNB to handle the new PDU session of SSC mode 3 in an exceptional manner

Q6: Please provide your view on Proposals.

| Company | Do you agree the proposals. | Comment |
| --- | --- | --- |
| ZTE | Wait for SA2’s progress | The same situation is also apply to UE AMBR if the issue identify. And as far as I know, the same proposal also provide to SA2. Considering SA2 will take care of SSC mode 3, would suggest to wait for SA2’s progress. |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-214819 Introduction of UE Slice MBR (Nokia, Nokia Shanghai Bell)

R3-215127 Discussion on Supporting for UE-Slice-MBR (CATT)

R3-215128 CR to 38.413 for Enhancement of RAN Slicing (CATT)

R3-215225 Analysis of Solutions for S-MBR support (Ericsson)

R3-215253 Supporting network slicing enhancement (Huawei)

R3-215254 Supporting network slicing enhancement (Huawei)

R3-215542 Discussion on Slice MBR (Samsung)

R3-215759 Impact on RAN slicing of UE slice MBR (ZTE)

R3-215760 Impact on RAN slicing of Target NSSAI (ZTE)

R3-215780 Support of Target NSSAI for UE redirection (LG Electronics)

R3-215252 Supporting network slicing enhancement (Huawei)- Move from other agenda