3GPP TSG-RAN WG3 #114	R3-215861

1 - 11 November 2021

Online

Agenda Item:	11.3

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion – Redcap 2- eDRX Aspects

Document for:	Approval

# Introduction

This is the summary document for the following come back:

CB: # RedCap2_eDRX

- Lower/upper bound of eDRX cycle, PTW?

- For NG, extending the existing Paging eDRX Cycle IE for idle? Or Introduce a new NR Paging eDRX information IE? Or introduce new redcap eDRX IE? Adding above information in CN Assistance Information for RRC_inactive IE? Early indication to AMF?

- Whether assistance information for NAS retransmission optimization is needed?

- RAN paging impact?

- F1, F1 paging impact? Early indication from DU to CU? Cell barring information from CU or decided by DU?

- Capture agreements and open issues

- Provide stage2/3 CRs if agreeable

(Nok - moderator)

Summary of offline disc R3-215861

# For the Chairman’s Notes

Propose the following:

Agree TP … .

# First Round

NG Interface

At the last RAN3#113 meeting, the following options were down-selected for the encoding of idle eDRX:

Encode the Idle eDRX Cycle sent in NGAP Paging message with one of the following 3 solutions (still FFS also dependent on SA2 outcome):

Option 1: Introduce one new Redcap eDRX Cycle IE for eDRX < 10.24s and one new Redcap eDRX Cycle IE for eDRX > 10.24s

Option 2: Extend the existing Paging eDRX Cycle IE in TS 38.413 section 9.3.1.154.

Option 3: Introduce only one new Redcap eDRX Cycle IE (for both > 10.24s and < 10.24s).

Since RAN3#113, we have received the LS from SA2 basically confirming the extension of idle eDRX cycle and agreeing on limiting the inactive eDRX to 10.24 seconds.

SA2 would like to provide the following feedback to RAN2:

- 5G System currently supports extended DRX in RRC/CM idle mode in the 5GC/NAS over E-UTRA/NB-IoT (since Rel-16) for eDRX cycles > 10.24s. SA2 has aligned with RAN2 request to support extended DRX in RRC/CM idle mode also for NR for eDRX cycles up to 10485.76 seconds.

- For RRC Inactive, SA2 agreed to support eDRX of up to 10.24s.

- Regarding eDRX extension beyond 10.24s for RRC Inactive, SA2 did not agree to support it in Rel-17 and instead will study potential solutions in Rel-18.

Taking into account this last feedback from SA2 it is time to down-select among the 3 options identified at last RAN3#113.

Q1: which option among the 3 options above do you support for sending over NGAP Paging message the idle eDRX cycle:

| Company | Comment |
| --- | --- |
| Nokia | Option 3. |

At the last RAN3#113 meeting, RAN3 took a working assumption to taken to send the same idle eDRX information which will be agreed as per question 1 also into the CN Assistance for RRC Inactive IE:

WA: need to transfer the above Idle eDRX Cycle for Redcap UEs in NGAP Core Network Assistance Information for RRC_INACTIVE IE.

It is it proposed to move this working assumption into an agreement.

Q2: can we agree to send over NG the idle eDRX information (as pe the result of Q1) also in the NGAP Core Network Assistance Information for RRC_Inactive IE?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |

One company proposes to rename the existing Paging eDRX Information into E-UTRA Paging eDRX Information. See R3-214896.

Q3: Do we need to rename the existing Paging eDRX Information into E-UTRA Paging eDRX Information?

| Company | Comment |
| --- | --- |
| Nokia | No. Seems not needed. This should be clear enough. |

RAN3 receives at this RAN3#114 meeting an LS S2-2107853 from SA2 whereby they inform about SA2 agreement to signal the NR Redcap UE Indication as a new RAT Type. This needs to be signaled from gNB to AMF.

Q4: is it ok to add an NR Redcap Indicator to the NG Initial UE Message to signal the Redcap RAT Type to AMF?

| Company | Comment |
| --- | --- |
| Nokia | In principle OK. |

Moderator’s summary:

Majority of companies think …

Proposal 2: TP...

Xn Interface

For the idle eDRX we have already an existing an existing IE which is shown below:

#### 9.2.3.142	Paging eDRX Information

This IE indicates the Paging eDRX parameters for RRC_IDLE as defined in TS 36.304 [33], if configured by higher layers.

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| Paging eDRX Cycle | M |  | ENUMERATED (hfhalf, hf1, hf2, hf4, hf6, hf8, hf10, hf12, hf14, hf16, hf32, hf64, hf128, hf256, …) | TeDRX defined in TS 36.304 [34]. Unit: [number of hyperframes]. |

We have two options for the Paging idle eDRX:

- Option 1: extend and reuse existing Paging eDRX cycle

- Option 2: introduce a new idle eDRX cycle

Q5: which option do you prefer for the XnAP idle eDRX cycle?

| Company | Comment |
| --- | --- |
| Nokia | Option 2 |

For eDRX Inactive over XnAP, some companies propose to introduce a new Inactive eDRX Cycle (option 1) or to reuse the existing Paging DRX (option 2). Reuse of existing Paging DRX is possible even if it is limited to 10.24s due to the decision of SA2 to limit the inactive eDRX cycle in release 17 to 10.24s.

Q6: which option do you prefer for the XnAP inactive eDRX cycle?

| Company | Comment |
| --- | --- |

F1 Interface- eDRX

Currently on F1 interface there is one Paging DRX but no Paging eDRX:

#### 9.3.1.40	Paging DRX

This IE indicates the Paging DRX as defined in TS 38.304 [24].

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| Paging DRX | M |  | ENUMERATED(32, 64, 128, 256, …) | Unit in radio frame. |

For the eDRX cycle we have the following options:

Option 1: add one new idle eDRX cycle and one new inactive eDRX Cycle

Option 2: add one new eDXR cycle for both idle and inactive

Q7: which option do you prefer for (idle and inactive) eDRX cycle over F1AP?

| Company | Comment |
| --- | --- |

Tdoc R3-215092 proposes to additionally include a RAN Paging DRX over F1 interface in order to cope with the following scenario:

Besides, for RRC_INACTIVE UE, when IDLE eDRX cycle is longer than 10.24s and INACTIVE eDRX cycle is not configured, outside CN PTW, following options are discussed in RAN2 for paging monitoring:

- Option 1: T is determined by the shortest of RAN paging cycle and default paging cycle.

- Option 2: T is determined by RAN paging cycle.

Thus, the RAN paging DRX cycle shall be provided when determine the paging monitoring cycle T. However, the current Paging DRX is defined as the minimum of the RAN UE Paging DRX and CN UE Paging DRX. When CN UE Paging DRX (e.g., 0.32s) is smaller than RAN UE Paging DRX (e.g. 0.64s), the gNB-DU would receive a Paging DRX with 0.32s. Without additional RAN UE Paging DRX provided, the gNB-DU would transmit the Paging messages with T= 0.32s. However, the INACITVE UE monitors the PO with a larger T=0.64s outside CN PTW, which implies a waste on the radio resource. Thus, additional RAN UE Paging DRX shall be provided.

Q8: are you OK to also add a RAN UE Paging DRX for the scenario above described?

| Company | Comment |
| --- | --- |

F1 Interface- Early Identification

For early identification, compared to last RAN3#113 we now have an agreement in RAN1/2 to have an early notification in MSG1 and MSG3 of redcap UE which is received by DU. The question is whether DU should inform immediately CU about this is a redcap UE (e.g. for some optimization of MSG 4) in the F1 Initial UL Message Transfer message i.e. before CU receives the UE capabilities.

Q9: in your view should we add an NR Redcap Indicator in the F1 Initial UL Message Transfer message for early identification of Recap in the CU?

| Company | Comment |
| --- | --- |

F1 Interface- Barring

Some Companies propose to add barring information over F1 from CU to DU (e.g. R3-215092). This is because if new Redcap specific UAC access information is introduced, the corresponding information shall be carried to F1AP procedures, i.e. Network Access Rate Reduction procedure. Some other companies (e.g. R3-215427) think it is not needed because as the CU is in charge of the cells, there is no need for another enhancement for barring since the CU is able to configure / control which gNB-DUs should serve RedCap UEs in which cells.

Q10: in your view is there an impact on F1 interface due to barring?

| Company | Comment |
| --- | --- |

Tdoc R3-215157 proposes to add (cell) Redcap support information in the Served Cell Information. In the view of the moderator this is related to the other come back topic of AI 11.2.

The proposal of the moderator is therefore to not treat this aspect as part of this email discussion.

# Second Round

xxx

# Conclusion

The following is proposed:

Proposal 1: TP...

# References

S2-2106978, Reply LS on Introducing extended DRX for Redcap UEs