3GPP TSG-RAN WG3 #114	R3-215861

1 - 11 November 2021

Online

Agenda Item:	11.3

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion – Redcap 2- eDRX Aspects

Document for:	Approval

# Introduction

This is the summary document for the following come back:

CB: # RedCap2_eDRX

- Lower/upper bound of eDRX cycle, PTW?

- For NG, extending the existing Paging eDRX Cycle IE for idle? Or Introduce a new NR Paging eDRX information IE? Or introduce new redcap eDRX IE? Adding above information in CN Assistance Information for RRC_inactive IE? Early indication to AMF?

- Whether assistance information for NAS retransmission optimization is needed?

- RAN paging impact?

- F1, F1 paging impact? Early indication from DU to CU? Cell barring information from CU or decided by DU?

- Capture agreements and open issues

- Provide stage2/3 CRs if agreeable

(Nok - moderator)

Summary of offline disc R3-215861

# For the Chairman’s Notes

Propose the following:

Agree TP … .

# First Round

NG Interface

At the last RAN3#113 meeting, the following options were down-selected for the encoding of idle eDRX:

Encode the Idle eDRX Cycle sent in NGAP Paging message with one of the following 3 solutions (still FFS also dependent on SA2 outcome):

Option 1: Introduce one new Redcap eDRX Cycle IE for eDRX < 10.24s and one new Redcap eDRX Cycle IE for eDRX > 10.24s

Option 2: Extend the existing Paging eDRX Cycle IE in TS 38.413 section 9.3.1.154.

Option 3: Introduce only one new Redcap eDRX Cycle IE (for both > 10.24s and < 10.24s).

Since RAN3#113, we have received the LS from SA2 basically confirming the extension of idle eDRX cycle and agreeing on limiting the inactive eDRX to 10.24 seconds.

SA2 would like to provide the following feedback to RAN2:

- 5G System currently supports extended DRX in RRC/CM idle mode in the 5GC/NAS over E-UTRA/NB-IoT (since Rel-16) for eDRX cycles > 10.24s. SA2 has aligned with RAN2 request to support extended DRX in RRC/CM idle mode also for NR for eDRX cycles up to 10485.76 seconds.

- For RRC Inactive, SA2 agreed to support eDRX of up to 10.24s.

- Regarding eDRX extension beyond 10.24s for RRC Inactive, SA2 did not agree to support it in Rel-17 and instead will study potential solutions in Rel-18.

Taking into account this last feedback from SA2 it is time to down-select among the 3 options identified at last RAN3#113.

Q1: which option among the 3 options above do you support for sending over NGAP Paging message the idle eDRX cycle:

| Company | Comment |
| --- | --- |
| Nokia | Option 3. |
| Huawei | We slightly prefer Option 2, as RAN2 agrees eDRX feature is optional for any UE (including RedCap and non-RedCap UEs) and for any gNB (either supporting RedCap or not), so we think it’s not RedCap’s exclusive feature and extend the existing one should be enough. In the meanwhile, option 3 is more clear so it’s also acceptable if most companies prefer option 3. |
| Qualcomm | Option 3, except it is not Redcap eDRX, and as we propose (and others) can be generalized to NR |
| Radisys | Option3 |
| Samsung | Option 3 |
| ZTE | Option 3 |

At the last RAN3#113 meeting, RAN3 took a working assumption to taken to send the same idle eDRX information which will be agreed as per question 1 also into the CN Assistance for RRC Inactive IE:

WA: need to transfer the above Idle eDRX Cycle for Redcap UEs in NGAP Core Network Assistance Information for RRC_INACTIVE IE.

It is it proposed to move this working assumption into an agreement.

Q2: can we agree to send over NG the idle eDRX information (as pe the result of Q1) also in the NGAP Core Network Assistance Information for RRC_Inactive IE?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Huawei | Yes |
| Qualcomm | Yes |
| Radisys | Yes |
| Samsung | Yes |
| ZTE | Yes |

One company proposes to rename the existing Paging eDRX Information into E-UTRA Paging eDRX Information. See R3-214896.

Q3: Do we need to rename the existing Paging eDRX Information into E-UTRA Paging eDRX Information?

| Company | Comment |
| --- | --- |
| Nokia | No. Seems not needed. This should be clear enough. |
| Huawei | Yes. If option 3 is taken, we think such renaming clarifies what the existing IE applies for, which is more clear and thus needed. |
| Qualcomm | Yes, we are proposing this and we think this makes the spec much clearer and consistent (see NB-IOT case) |
| Radisys | No not needed |
| Samsung | No clear benefit is identified as long as the new eDRX IE is named as RedCap specific. |
| ZTE | Not needed. |

RAN3 receives at this RAN3#114 meeting an LS S2-2107853 from SA2 whereby they inform about SA2 agreement to signal the NR Redcap UE Indication as a new RAT Type. This needs to be signaled from gNB to AMF.

Q4: is it ok to add an NR Redcap Indicator to the NG Initial UE Message to signal the Redcap RAT Type to AMF?

| Company | Comment |
| --- | --- |
| Nokia | In principle OK. |
| Huawei | OK |
| Qualcomm | In principle ok. |
| Radisys | OK |
| Samsung | OK |
| ZTE | OK |

Moderator’s summary:

Majority of companies think …

Proposal 2: TP...

Xn Interface

For the idle eDRX we have already an existing an existing IE which is shown below:

#### 9.2.3.142	Paging eDRX Information

This IE indicates the Paging eDRX parameters for RRC_IDLE as defined in TS 36.304 [33], if configured by higher layers.

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| Paging eDRX Cycle | M |  | ENUMERATED (hfhalf, hf1, hf2, hf4, hf6, hf8, hf10, hf12, hf14, hf16, hf32, hf64, hf128, hf256, …) | TeDRX defined in TS 36.304 [34]. Unit: [number of hyperframes]. |

We have two options for the Paging idle eDRX:

- Option 1: extend and reuse existing Paging eDRX cycle

- Option 2: introduce a new idle eDRX cycle

Q5: which option do you prefer for the XnAP idle eDRX cycle?

| Company | Comment |
| --- | --- |
| Nokia | Option 2 |
| Huawei | We prefer option 1 with the same reason stated in Q1 |
| Qualcomm | Prefer option 2, but would be ok to take this as more of an FFS / WA in Xn |
| Radisys | Option 2. Please refer to our CR R3-215159 |
| Samsung | Option 2 |
| ZTE | Option 2 |

For eDRX Inactive over XnAP, some companies propose to introduce a new Inactive eDRX Cycle (option 1) or to reuse the existing Paging DRX (option 2). Reuse of existing Paging DRX is possible even if it is limited to 10.24s due to the decision of SA2 to limit the inactive eDRX cycle in release 17 to 10.24s.

Q6: which option do you prefer for the XnAP inactive eDRX cycle?

| Company | Comment |
| --- | --- |
| Huawei | Introduce a new IE for RRC_INACTIVE. First, introducing a separate RRC_INACTIVE is clearer, and we don’t need to have same configuration for RRC_IDLE and RRC_INACTIVE. Second, the minimum eDRX cycle 2.56s is agreed by SA2. Reusing the existing Paging DRX makes the gNB confused on whether it is an eDRX configuration with eDRX cycle = 2.56s or DRX configuration with RAN paging DRX cycle = 2.56s. Third, the method is more future-proof. Although it is agreed to limit the eDRX cycle to 10.24s in this release, there is a large chance to further extend it in Rel 18. If so, the existing paging DRX can’t be reused at that time, and new IE will be introduced anyway. |
| Qualcomm | Prefer slightly to introduce a new IE, but this aspect could perhaps be left open for now until we have better understanding of TS 38.304 changes . |
| Radisys | We prefer using a new single Redcap Paging eDRX information IE over Xn for both RRC_Idle and RRC_Inactive. Please refer to our CR R3-215159. Depending upon the RRC state of the UE the source node shall pass Idle eDRX or Inactive eDRX in the same IE in Xn Paging. We do not see a need to introduce separate IEs for RRC_Idle and RRC_Inactive. |
| Samsung | Option 2 seems to be workable. |
| ZTE | Option 1 As shown in our R3-215789, we would like to introduce a new Inactive eDRX Cycle . Since RRC_INACTIVE eDRX beyond 10.24s is not supported in R17, it is difficult to finally conclude the paging monitoring behaviour of UE in RRC_INACTIVE with RAN PTW configured (cycle>10.24s). Introduce a separate IE for RRC_INACTIVE is probably more extensible for future release. |

F1 Interface- eDRX

Currently on F1 interface there is one Paging DRX but no Paging eDRX:

#### 9.3.1.40	Paging DRX

This IE indicates the Paging DRX as defined in TS 38.304 [24].

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| Paging DRX | M |  | ENUMERATED (32, 64, 128, 256, …) | Unit in radio frame. |

For the eDRX cycle we have the following options:

Option 1: add one new idle eDRX cycle and one new inactive eDRX Cycle

Option 2: add one new eDXR cycle for both idle and inactive

Q7: which option do you prefer for (idle and inactive) eDRX cycle over F1AP?

| Company | Comment |
| --- | --- |
| Huawei | Option 1. Again, we believe introduce separate new IE for IDLE and RRC_INACTIVE is better, e.g., in the case of RRC_INACTIVE UE configured with IDLE eDRX cycle longer than 10.24s, both idle eDRX cycle and inactive eDRX cycle are needed for the PF/PO calculation. This is not only clearer but also more future-proof. |
| Radisys | Option 2. Please refer to our CR R3-215157 We do not see a need to introduce two different IEs for Idle and Inactive |
| Samsung | Option 2. F1 does not differentiate INACTIVE and IDLE for Paging. |
| ZTE | Option 1, agree with Huawei. |

Tdoc R3-215092 proposes to additionally include a RAN Paging DRX over F1 interface in order to cope with the following scenario:

Besides, for RRC_INACTIVE UE, when IDLE eDRX cycle is longer than 10.24s and INACTIVE eDRX cycle is not configured, outside CN PTW, following options are discussed in RAN2 for paging monitoring:

- Option 1: T is determined by the shortest of RAN paging cycle and default paging cycle.

- Option 2: T is determined by RAN paging cycle.

Thus, the RAN paging DRX cycle shall be provided when determine the paging monitoring cycle T. However, the current Paging DRX is defined as the minimum of the RAN UE Paging DRX and CN UE Paging DRX. When CN UE Paging DRX (e.g., 0.32s) is smaller than RAN UE Paging DRX (e.g. 0.64s), the gNB-DU would receive a Paging DRX with 0.32s. Without additional RAN UE Paging DRX provided, the gNB-DU would transmit the Paging messages with T= 0.32s. However, the INACITVE UE monitors the PO with a larger T=0.64s outside CN PTW, which implies a waste on the radio resource. Thus, additional RAN UE Paging DRX shall be provided.

Q8: are you OK to also add a RAN UE Paging DRX for the scenario above described?

| Company | Comment |
| --- | --- |
| Huawei | Yes. The reason to add the RAN UE paging DRX has been captured above. |
| Radisys | No. This issue is not specific to Redcap UE. This may happen for any UE. However as pointed out there is no waste of Radio resources. Once the Paging message is read by the UE at T=0.32s, UE will stop monitoring further. |
| Samsung | No for now. We are not sure why this issue is for RedCap. It seems to be a general issue, if it is valid. |
| ZTE | FFS We can wait RAN2’s further decision. |

F1 Interface- Early Identification

For early identification, compared to last RAN3#113 we now have an agreement in RAN1/2 to have an early notification in MSG1 and MSG3 of redcap UE which is received by DU. The question is whether DU should inform immediately CU about this is a redcap UE (e.g. for some optimization of MSG 4) in the F1 Initial UL Message Transfer message i.e. before CU receives the UE capabilities.

Q9: in your view should we add an NR Redcap Indicator in the F1 Initial UL Message Transfer message for early identification of Recap in the CU?

| Company | Comment |
| --- | --- |
| Huawei | Yes. Early identification of RedCap UE at gNB-CU is beneficial, it can help gNB-CU to generate configurations like PDCP configuration for SRB1. |
| Qualcomm | In principle we see no issue with providing the information that is already available – which should be the case. |
| Radisys | Yes. Early Identification of Redcap UE is agreed in RAN2. Redcap UE indication is needed in Initial UL RRC Message Transfer to inform CU. Please refer our CR R3-215157 |
| Samsung | Yes. The following benefit can be identified: Help gNB-CU make decision on whether accepting the access request or not Before receiving UE capability, help gNB-CU determine the configuration to the UE, e.g., whether configuring CA to the UE or not. Help gNB-CU generates configurations for RedCap UE, e.g., PDCP configuration for SRB1; |
| ZTE | Yes, as shown in our R3-215789, the gNB-DU informs RedCap early indication to gNB-CU via initial UL RRC message transfer |

F1 Interface- Barring

Some Companies propose to add barring information over F1 from CU to DU (e.g. R3-215092). This is because if new Redcap specific UAC access information is introduced, the corresponding information shall be carried to F1AP procedures, i.e. Network Access Rate Reduction procedure. Some other companies (e.g. R3-215427) think it is not needed because as the CU is in charge of the cells, there is no need for another enhancement for barring since the CU is able to configure / control which gNB-DUs should serve RedCap UEs in which cells.

Q10: in your view is there an impact on F1 interface due to barring?

| Company | Comment |
| --- | --- |
| Huawei | This depends on RAN2 discussion about access control mechanism for RedCap. It may be beneficial for CU to provide cell-barring-like information (e.g. 1 Rx barring or 2Rx barring) to DU regarding the load or operating policies. |
| Qualcomm | Should wait for progress in other WGs. |
| Radisys | This is dependent on RAN2. RAN2 has agreed to provide SIB1 barring for Redcap UE and a specific IFRI in SIB1. F1 impacts due to this is FFS at the moment. |
| Samsung | We understand RAN2 progress is needed for this issue. However, in general, we see some benefits, e.g., gNB-CU can make decision on barring RedCap UEs based on, e.g., load situation. Currently, we already have the similar feature to bar IAB node. |
| ZTE | No impact expect here. DU can decide the cell-barring (e.g. 1 Rx barring or 2Rx barring) by itself. |

Tdoc R3-215157 proposes to add (cell) Redcap support information in the Served Cell Information. In the view of the moderator this is related to the other come back topic of AI 11.2.

The proposal of the moderator is therefore to not treat this aspect as part of this email discussion.

# Second Round

xxx

# Conclusion

The following is proposed:

Proposal 1: TP...

# References

S2-2106978, Reply LS on Introducing extended DRX for Redcap UEs