3GPP TSG-RAN WG3 #114-e							R3-215851

1 November – 11 November 2021

Online

Agenda Item:	10.2.1.4

Source:	ZTE (moderator)

Title:	Summary of Offline Discussion on CB: # SONMDT2_UEHistoryInfor

Document for:	Approval

# Introduction

CB: # SONMDT2_UEHistoryInfor

- How to retrieve SN UHI?

- Which node collects SN UHI?

- Correlation of MN and SN UHI

- Correlated MN and SN UHI from MN to SN is benefit?

- SN UHI information content

- Messages for UHI transfer

- Interface impact of SN UHI from UE

- Capture agreements and provide TPs if agreeable

(ZTE - moderator)

Summary of offline disc R3-215851

It is proposed to divide the discussion into two phases:

-	Phase 1: Identify the issues to be discussed in RAN3

Deadline: Please provide your views by 4:00am UTC Friday November 5th

-	Phase 2: Further discussion to capture agreements and open issues

Deadline: TBD pending on the outcome of Phase 1

# For the Chairman’s Notes

[TBD]

# Phase 1 discussion

## How to retrieve SN UHI

In the last meeting, we have discussed seriously on the solutions to retrieve SN UHI. From moderator’s point of view, the detailed signaling design shall be discussed after we reach a consensus on the basic solution. The main controversial point is whether up-to-date SN UHI is needed and how to transfer up-to-date SN UHI. Based on the contributions, now we have 5 options as follows.

Option 1: MN initiates SN modification procedures to retrieve SN UHI before handover[3][10].

If SRB3 is allowed and delta configuration enabled, MN needs to trigger MN-initiated modification procedure before handover. Thus, no extra delay may be introduced to retrieve SN UHI using the same procedure. Some companies argue that if SRB3 is not allowed or delta config is not enabled, the latest SN UHI cannot be provided to target MN after source SN release using this option. However, it is noted that in the RAN2 #115 e-meeting, the following agreements were made. [10] believes that according to the agreements, UE can report the latest SN UHI to source MN if up-to-date SN UHI is need, and thus it is sufficient to use option 1 to retrieve SN UHI.

SN Related MHI Information: 2 RAN2 to confirm that the PSCell transition is part of MHI. 3 PSCell MHI is reported only to PCell. 4 UEInformationResponse message is used to convey the PSCell MHI to the MN. 5 Take Option 1 ‎(PSCell MHI nested within the PCell MHI) as baseline.

Option 2: MN is always aware of the latest SN UHI by subscribing to PSCell changes [9]

[9] believes that supporting MN subscription to PSCell changes has the advantages including: 1) help target MN to make informed decisions about DC and target SN to optimize PSCell selection, and 2) simplify CHO by ensuring up-to-date PSCell information at candidate NG-RAN nodes. However, this option may cause too much X2/Xn signalling, and the latest SN UHI is not always needed.

Option 3: Use new Xn message to transfer SN UHI after source SN release [16]

[16] proposes to transfer SN UHI via a new Xn message after handover preparation procedure, which is simple and clean. However, the main drawback of this option is latency which may delay the Ping pong decision made by target NG-RAN nodes.

Option 4: Hybrid option 1&2 [2][4][6]

[2][4][6] proposes a hybrid option combing option 1 and option 2. If SRB3 is allowed and delta config enabled, SN UHI can be retrieved by the MN-initiated modification procedure. If SRB3 is not allowed or delta config is not enabled, SN UHI shall be included in the SN Modification Required message, so that it can be updated in the MN when the MN requests PSCell change notifications. This solution brings more Xn signalling in exchange for the decrease of handover delay.

Option 5: Hybrid option 1&3 [5]

[5] proposes to use option 1 as baseline, and also use a new Xn message to transfer latest UHI to target NG-RAN nodes. The drawback of this option is the same as option 3, e.g. latency.

Question 1: Companies are kindly asked which option above is preferred to retrieve SN UHI.

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | Option 1, 4 | Option 2 may introduce unnecessary signalling, option 3 and 5 have more specification impacts compared with the other options. We think option 1 is sufficient, but we can accept option 4 as a compromise. |
| Lenovo and Motorola Mobility | Option 1 | For Option 2, it may cause much signalling and resource to transfer latest SN UHI from SN to MN if PSCell changes frequently. For Option 3, new Xn message(s) are introduced to transfer SN UHI after source SN release, which has more spec impact. |
| CATT | Option 4 | Option 2 can be used as a supplementation by supporting MN subscription to PSCell changes. |
| Nokia | 1, possibly 2 | Option 1 is the primary solution that shall work 99% of cases. However, existing signalling enables the MN to be updated concerning PSCell changes, so, epending on the implementation, this mechanism can be reused. |
| Qualcomm | Option 1, 4 | Option 1 is the baseline. In addition to Option 1, we are also OK to support Option 2 i.e., MN to be aware of intra-SN PSCell changes without MN involvement by subscribing to PSCell Changes. SN can then provide a PSCell Change notification to MN via SN Modification Required or a new class-2 message. Maybe we can restrict this to only intra-SN PSCell changes without MN involvement to limit Xn signaling overhead. |
| Huawei | 1 or 5 | We think the usage of SN UHI does not need the real time SN UHI. For the ping pong issue, in our understanding, the ping pong detection is based on the statistics over a long time. Therefore we think the target node does not need the real time SN UHI, i.e. the target node can get the SN UHI after handover. For the assisting target MN in selecting the appropriate SN and in determining whether DC needs to be supported, we think the motivation is to avoid the unnecessary handover. In our understanding, it does not Therefore Option 1 should be the baseline. In case we need statistics also from cases with full reconfiguration, we prefer to combine 1 with 3 which is option 5. We would also like to highlight that 2 and 3 should not be used standalone but always combined with 1. There is no point in using these if the information is already available at the right time. |
| China Telecom | Option 1/4 | We think option1 is the baseline, and we can accept option4 as the supplementary solution if option1 cannot be used, other solutions have more impact on the specification and may cause extra delay. |
| Samsung | 5 | The current description on 1 may bring confusion. At last RAN3#113-e meeting it was agreed that: RAN3 should consider solutions which would not delay HO more than it would have been delayed without UHI. So we suggest to update Option 1 to “In case SN modification procedure is needed without UHI e.g. for delta configuration, the source MN retrieve SN UHI from the SN via SN modification procedure. With this change, we are fine to take Option 1 as baseline. For Option 2, we agree with the analysis from the moderator, too much X2/Xn signaling. Option 3 can be used in case the MN receives the updated SN UHI after source SN release. This is also in line with what we have agreed at last RAN3#114-e meeting: Option 4 has similar issue as Option 2. Based on above, we are fine for Option 5. |

Question 2: Companies are kindly asked to indicate your least favorite option.

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | Option 2, 3, 5 | Same comment to Q1 |
| Lenovo and Motorola Mobility | Option 2/3/5 |  |
| CATT | Option 3,5 | It is too complex for target MN to update UHI when receiving the new updated message. |
| Nokia | 3 (and 5) | Post-release and after HO signalling complicates the solution beyond reasonable limits. Option 2 is acceptable only if the existing signalling is reused to a great extend. |
| Qualcomm | Option 3 and 5 | Similar view as CATT and Nokia. Also, this will mean latest SN UHI might not be available at target MN right after HO. If we are targeting that use case, we might as well come up with a complete solution (via a subscribe mechanism) |
| Huawei | 2,3 4 | (2,3) There is no point in using these if the information is already available at the right time. So we should pick a hybrid solution (4) This will increase signaling if we need to notify at every cell change |
| China Telecom | Option 2/3/5 |  |
| Samsung | Option 2, 4 | The ping pong detection is based on the statistics over a long time. Therefore the target node does not need the real time SN UHI. 2 and 4 bring too much signaling. Usually SN is used for NW capacity issue, so SN could consist of small cells with high frequency. It could be very often that Intra-SN PSCell change occurs. |

## Correlation of MN and SN UHI

We have already agreed to include both MN and SN UHI in the handover request message during inter-MN handover. The remaining issue is whether to transfer correlated MN UHI and SN UHI or separate MN UHI and SN UHI. It seems to be majority view that correlated MN UHI and SN UHI shall be achieved by using a two-dimension structure, where PSCell information is listed within the related PCell information.

MN and SN UHI shall be included in inter-MN handover message i.e. Handover Request message. It is FFS whether MN UHI and SN UHI will be separated Ies or a list of MN UHI containing a list of SN UHI.

According to the contributions, two options are proposed as follows. It is noted in the last meeting, RAN2 has agreed that the PSCell MHI is nested within the PCell MHI in the UE history from the UE. From moderator’s view, it could be better to choose option 1 to keep align with RAN2. Furthermore, additional information needs to be transferred to help target MN correlate the information if option 2 is used.

Option 1: Correlated MN and SN UHI using a nested structure shall be included in the handover request message.

Option 2: Separate MN and SN UHI shall be included in the handover request message. Target MN will correlate these two information.

Question 3: Companies are kindly asked which option above is preferred.

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | Option 1 | Option 1 is simpler since correlation only needs to be performed once, and no additional information is required. |
| Lenovo and Motorola Mobility | Option 1 | It is better for source MN to make the correlation for MN UHI and SN UHI. |
| CATT | Option 1 | We already have a WA to use a two-dimensional structure which is captured in the chairman notes: WA: Correlation of MN UHI and SN UHI could be realized via two-dimensional structure for UHI (PSCells history information are listed within each Pcell in the UHI); it may not be feasible on all interfaces. Besides, we should also align with RAN2 |
| Nokia | Option 2 | SCG UHI will have to be delivered from the MN to the SN and vice versa. So far there is no reason to have them combined (why the SN would send outdated MCG UHI back to the MN???). So, having such “combined” or “embedded” list just for the HO purpose does not seem reasonable. There will also be the question how that coexists with the legacy UHI… So, adding a new SCG UHI IE (with all the information needed to correlate it with the MCG UHI!) and keeping the existing MCG UHI as is seems the best compromise. No idea what are we supposed to “align with RAN2”, if RAN2 does not discuss HO signalling (as far as I know)? The UE history is a totally different story. |
| Qualcomm | See comments | Regarding Nokia’s comment that “SN might end up sending an outdated MCG UHI back to the MN”, can you clarify why/when does this happen? In my understanding, source MN can just send the correlated list of MN and SN UHI which it is maintaining to the target MN in HANDOVER REQUEST. No need of using any outdated MN UHI from the SN, right? Or is there any other scenario you are referring to where SN will have the outdated MN UHI? Also, I think this comes down to the fundamental question: Whether MN UHI should be forwarded from MN to SN and vice versa? But we do understand that the IE structure can be simpler to coexist with legacy UHI if we use an independent list, but nested list just makes correlation easier at the cost of signaling overhead. We are OK to go with an independent list as well if this can help make some progress. |
| Huawei | Option 1 | Agree the comments from ZTE |
| China Telecom | Option 1 | Agree with ZTE. |
| Samsung | Option 2 | Agree with Nokia. Besides that, we still doubt how the correlation is done and whether it is in the MN or in the SN. If the correlation is done in the SN, currently the PCell ID in the message from MN to the SN is optional. If the MN doesn’t send PCell ID to the SN. This means the SN cannot get the relation of PScell and PCell. If we mandate the MN to send the PCell ID to the SN, this is a non-backward compatible change. If the correlation is done in the MN, the MN may not know the up-to-date PScell as well in case of intra-SN PScell change via SRB3. |

# Phase 2 discussion

Based on outcome of phase 1 discussion and on-line discussion, the following open issues may be discussed in the phase 2 discussion.

- Correlated MN and SN UHI from MN to SN is benefit?

- Messages for UHI transfer

- SN UHI information content

- Interface impact of SN UHI from UE

- Stage 2/3 update

# Conclusion, Recommendations [if needed]

If needed

# References

R3-214469	Summary of Offline Discussion on CB: # SONMDT3_UEHistoryInfor

R3-214811	[SON BL CRs, TP to TS 38.423, TP to TS 36.423]  HO delay and non-up-to-date SCG UHI information (Nokia, Nokia Shanghai Bell)	other

R3-214840	Consideration on UE history information (China Telecommunication)	discussion

R3-214915	UE History Information in MR-DC (Qualcomm Incorporated)	discussion

R3-214956	(TP for SON BLCR for 38.423,38.413, 36.423, 36.413 , 37.340, 38.300) UE History Information in MR-DC (Huawei)	other

R3-215068	Enhancement of UE history information in MR-DC scenario (CATT,CMCC)	discussion

R3-215069	(TP on UE history information for 36.413) Addition of UE history information for SN (CATT,CMCC)	other

R3-215070	(TP on UE history information for 36.423) Addition of UE history information for SN (CATT,CMCC)	other

R3-215444	(TP for SON BL CR for TS 38.423, TS 38.413, TS 36.413): UE History Information for Secondary Node (Ericsson)	other

R3-215456	UE History Information in MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)	discussion

R3-215457	(TP for SON BL CR for TS 37.340) Introduce UHI in MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)	other

R3-215458	(TP for SON BL CR for TS 38.423) Introduce UHI in MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)	other

R3-215459	(TP for SON BL CR for TS 36.423) Introduce UHI in MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)	other

R3-215460	(TP for SON BL CR for TS 38.413) Introduce UHI in MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)	other

R3-215461	(TP for SON BL CR for TS 36.413) Introduce UHI in MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)	other

R3-215519	UE History Information in MR-DC (Samsung)	discussion

R3-215520	TP for SON BLCR for 38.423: UE History Information in MR-DC (Samsung)	other

R3-215521	TP for SON BLCR for 36.423: UE History Information in EN-DC (Samsung)	other

R3-215695	(TP to TS 38.413)UE history information in MR-DC (CMCC, CATT)	other

R3-215696	(TP to TS 38.423)UE history information in MR-DC (CMCC, CATT)	other