| 3GPP TSG-RAN3 Meeting #12 | Document | R3-001239 |
| --- | --- | --- |
| Seoul, Korea, 10 - 13 April 2000 |  | e.g. for 3GPP use the format TP-99xxx or for SMG, use the format P-99-xxx |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 25.413 | CR | 83R4 | Current Version: | 3.1.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: | RAN#8 | for approval | x |  | Strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME |  | UTRAN / Radio | x | Core Network | x |
| (at least one should be marked with an X) |
| Source: | Lucent | Date: | 2000-03-27 |
| Subject: | Interaction between Class 2 messages and the RELOCATION REQUIRED message. |
| Work item: |  |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature | X |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | x |
|  |  |  |  | Release 00 |  |
| Reason for change: | In 25.413 it is stated that Class 2 messages shall be ignored if received in RNC after the RELOCATION REQUIRED message has been sent for the Iu connection in question. This CR proposes that Class 2 messages are not ignored. |
| Clauses affected: | 8.6.2 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

## 8.6	Relocation Preparation

### 8.6.1	General

The purpose of the Relocation Preparation procedure is to prepare relocation of SRNS either with involving UE or without involving UE. The relocation procedure shall be co-ordinated in all Iu signalling connections existing for the UE in order to allow Relocation co-ordination in the target RNC. The procedure uses connection oriented signalling.

### 8.6.2	Successful Operation

Figure 1: Relocation Preparation procedure. Successful operation.

The source RNC shall initiate the procedure by generating RELOCATION REQUIRED message. The source RNC shall decide whether to initiate the intra-system Relocation or the inter-system Relocation. In case of intra-system Relocation the source RNC shall indicate in the Source ID IE the RNC-ID of the source RNC and in the Target ID IE the RNC-ID of the target RNC. In case of inter-system Relocation the source RNC shall indicate in the Source ID IE the Service Area Identifier  and in the Target ID IE the cell global identity of the target system. The source RNC shall indicate the appropriate cause value for the Relocation in the Cause IE.

The source RNC shall determine whether the relocation of SRNS shall be executed with or without involvement of UE. The source RNC shall set the Relocation Type IE accordingly to 'UE involved ' or 'UE not involved'.

The source RNC shall indicate in the RELOCATION REQUIRED message the amount of Iu signalling connections existing for the UE by setting correctly the Number of Iu Instances IE included in the Source to Target RNC Transparent Container IE. This container may also include the necessary information for Relocation co-ordination, security procedures and the handling of UE Capabilities. The container may include the RRC context to be relocated within the RRC Container IE.

The source RNC shall send the RELOCATION REQUIRED message to the CN and the source RNC shall start the timer TRELOCprep.

When the preparation including resource allocation in the target system is ready and the CN has decided to continue the relocation of SRNS, the CN shall send RELOCATION COMMAND message to the source RNC and the CN shall start the timer TRELOCcompl.

For each RAB originating from the PS domain,  the RELOCATION COMMAND message may contain Iu transport address and Iu transport association to be used for the forwarding of the DL N-PDU duplicates towards the relocation target. Upon reception of the RELOCATION COMMAND message from the PS domain, the source RNC shall start the timer TDATAfwd.

The Relocation Preparation procedure is terminated in the CN by transmission of RELOCATION COMMAND message.

If Relocation Type IE was set to 'UE involved ' by the source RNC and if the target system does not support all existing RABs, the RELOCATION COMMAND message shall contain a list of RABs indicating all the RABs that are not supported by the target system. The source RNC shall pass this information to the radio protocols.

Upon reception of RELOCATION COMMAND the source RNC shall stop the timer TRELOCprep, RNC shall start the timer TRELOCOverall and RNC shall terminate the Relocation Preparation procedure.

When Relocation Preparation procedure is terminated successfully and when the source RNC is ready, the source RNC should trigger the execution of relocation of SRNS.

In case of intersystem handover to GSM the RNC shall include MS Classmark 2 and MS Classmark 3 IEs received from the UE in the RELOCATION REQUIRED message to the CN.

Interactions with other procedures:

If, after RELOCATION REQUIRED message is sent and before the Relocation Preparation procedure is terminated, the source RNC receives a RANAP message initiating an other connection oriented RANAP class 1 or class 3 procedure (except Iu RELEASE COMMAND, which shall be handled normally) via the same Iu signalling connection, the source RNC shall either:

1.	cancel the Relocation Preparation procedure i.e. execute Relocation Cancel procedure with an appropriate value for the Cause IE, e.g. ‘Interaction with other procedure’, and after successful completion of Relocation Cancel procedure, the source RNC shall continue the initiated RANAP procedure;

or

2.	terminate the initiated RANAP procedure without any changes in UTRAN by sending appropriate response message with the cause value “Relocation Triggered” to the CN. The source RNC shall then continue the relocation of SRNS.

If during the Relocation Preparation procedure the source RNC receives a DIRECT TRANSFER message it shall be handled normally.

If during the Relocation Preparation procedure the source RNC receives connection oriented RANAP class 2 messages (with the exception of DIRECT TRANSFER) it shall decide to either execute the procedure immediately or suspend it. In the case the relocation is cancelled the RNC shall resume any suspended procedures (if any).

After Relocation Preparation procedure is terminated successfully, all RANAP messages (except Iu RELEASE COMMAND message, which shall be handled normally) received via the same Iu signalling bearer shall be ignored by the source RNC.