| 3GPP TSG-RAN-WG3 meeting #14 | Document | R3-001735 |
| --- | --- | --- |
| Helsinki, Finland, 3 –7 July, 2000 |  | e.g. for 3GPP use the format TP-99xxx or for SMG, use the format P-99-xxx |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 25.931 | CR | 001 | Current Version: | 3.0.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: | RAN#9 | for approval | X |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME |  | UTRAN / Radio | X | Core Network |  |
| (at least one should be marked with an X) |
| Source: | CSELT | Date: | 2000-06-28 |
| Subject: | Corrections to a minor mistake present in the spec |
| Work item: |  |
| Category: | F Correction | X | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature |  |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | X |
|  |  |  |  | Release 00 |  |
| Reason for change: | In the Soft Handover examples, since a RL is the first radio link via the DRNC for the UE to be setup, RNSAP message that the SRNC send to the DRNC must be "Radio Link Setup Request” and not the "Radio Link Addition Request". |
| Clauses affected: | 7.10.1 and 7.10.3 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: | Thanks to Xu Mingyan of CHINA.GDT Corp. Ltd for the suggestion. |

<--------- double-click here for help and instructions on how to create a CR.

## 7.10	Soft Handover (FDD)

This subclause presents some examples of soft handover procedures. The following cases are considered:

	Radio Link Addition (Branch Addition);

	Radio link Deletion (Branch Deletion);

	Radio link Addition & Deletion (Branch Addition & Deletion - simultaneously).

Soft Handover applies only to FDD mode.

### 7.10.1	Radio Link Addition (Branch Addition)

This example shows establishment of a radio link via a Node B controlled by another RNC than the serving RNC. This is the first radio link to be established via this RNS, thus macro-diversity combining/splitting with already existing radio links within DRNS is not possible.

Figure 24: Soft Handover - Radio Link Addition (Branch Addition)

1.	SRNC decides to setup a radio link via a new cell controlled by another RNC. SRNC requests DRNC for radio resources by sending RNSAP message Radio Link Setup Request. If this is the first radio link via the DRNC for this UE, a new Iur signalling connection is established. This Iur signalling connection will be used for all RNSAP signalling related to this UE.	
Parameters: Cell id, Transport Format Set per DCH, Transport Format Combination Set, frequency, UL scrambling code.

2.	If requested resources are available, DRNC sends NBAP message Radio Link Setup Request to Node B.
Parameters: Cell id, Transport Format Set per DCH, Transport Format Combination Set, frequency, UL scrambling code.

3.	Node B allocates requested resources. Successful outcome is reported in NBAP message Radio Link Setup Response.
Parameters: Signalling link termination, Transport layer addressing information (AAL2 address, AAL2 Binding Identitie(s)) for Data Transport Bearer(s).

Then Node B starts the UL reception.

4.	DRNC sends RNSAP message Radio Link Setup Response to SRNC.	 
Parameters: Transport layer addressing information (AAL2 address, AAL2 Binding Identity) for Data Transport Bearer(s), Neighbouring cell information.

5.	SRNC initiates setup of Iur/Iub Data Transport Bearer using ALCAP protocol. This request contains the AAL2 Binding Identity to bind the Iub Data Transport Bearer to DCH. 	
This may be repeated for each Iur/Iub Data Transport Bearer to be setup.

6./7.	Node B and SRNC establish synchronism for the Data Transport Bearer(s) by means of exchange of the appropriate DCH Frame Protocol frames Downlink Synchronisation and Uplink Synchronisation, relative already existing radio link(s). Then Node B starts DL transmission.

8.	SRNC sends RRC message Active Set Update (Radio Link Addition) to UE on DCCH.	
Parameters: Update type, Cell id, DL scrambling code, Power control information, Ncell information.

9.	UE acknowledges with RRC message Active Set Update Complete.

### 7.10.2	Radio link Deletion (Branch Deletion)

This example shows deletion of a radio link belonging to a Node B controlled by another RNC than the serving RNC.

Figure 25: Soft Handover - Radio Link Deletion (Branch Deletion)

1.	SRNC decides to remove a radio link via an old cell controlled by another RNC. SRNC sends RRC message Active Set Update (Radio Link Deletion) to UE on DCCH.	
 Parameters: Update type, Cell id.

2.	UE deactivates DL reception via old branch, and acknowledges with RRC message Active Set Update Complete.

3.	SRNC requests DRNC to deallocate radio resources by sending RNSAP message Radio Link Deletion Request.
Parameters: Cell id, Transport layer addressing information.

4.	DRNC sends NBAP message Radio Link Deletion Request to Node B.	
Parameters: Cell id, Transport layer addressing information.

5.	Node B deallocates radio resources. Successful outcome is reported in NBAP message Radio Link Deletion Response.

6.	DRNC sends RNSAP message Radio Link Deletion Response to SRNC.

7.	SRNC initiates release of Iur/Iub Data Transport Bearer using ALCAP protocol.

### 7.10.3	Radio link Addition & Deletion (Branch Addition & Deletion - simultaneously)

This example shows simultaneous deletion of a radio link belonging to a Node B controlled by the serving RNC and the establishment of a radio link via a Node B controlled by another RNC than the serving RNC. This is the first radio link to be established via this RNS, thus macro-diversity combining/splitting with already existing radio links within DRNS is not possible.

This procedure is needed when the maximum number of branches allowed for the macrodiversity set has already been reached.

Figure 26: Soft Handover - Radio link Addition & Deletion (Branch Addition & Deletion - simultaneously)

1.	( 7. See description 1. ( 7. in subclause 7.10.1.

8.	SRNC sends RRC message Active Set Update (Radio Link Addition & Deletion) to UE on DCCH.
Parameters: Update type, Cell id, DL scrambling code, Power control information, Ncell information.

9.	UE deactivates DL reception via old branch, activates DL reception via new branch and acknowledges with RRC message Active Set Update Complete.

10.	( 12. See description 3. ( 7. in subclause 7.10.2.

# Text boxes

### 1.1.3