3GPP TSG-RAN3 Meeting #18 	Tdoc R3-010081

Lidingo, Sweden, 15-19 January 2001

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | 25.433 | CR | CR-334 | ( rev | - | ( Current version: | 3.4.1 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | (U)SIM |  | ME/UE |  | Radio Access Network | X | Core Network |  |
| Title: ( | Editorial Correction in TS 25.433 |
| Source: ( | NBAP Rapporteur |
| Work item code: ( |  |  | Date: ( | 09 January 2001 |
| Category: ( | F |  | Release: ( | R99 |
|  | Use one of the following categories: F (essential correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | In R3-002972 CR294 which was approved at RAN#10, the criticality of RL IE (reject) is proposed to be removed but it was not implemented. |
| Summary of change: ( | The criticality of RL IE is removed. |
| Consequences if ( not approved: | The agreement is not applied |
| Clauses affected: ( | 9.1.52 |
| Other specs ( |  | Other core specifications ( |  |
| affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: ( |  |

How to create CRs using this form:

Comprehensive information and tips about how to create CRs can be found at: http://www.3gpp.org/3G_Specs/CRs.htm.  Below is a brief summary:

1)	Fill out the above form. The symbols above marked ( contain pop-up help information about the field that they are closest to.

2)	Obtain the latest version for the release of the specification to which the change is proposed. Use the MS Word "revision marks"  feature (also known as "track changes") when making the changes. All 3GPP specifications can be downloaded from the 3GPP server under ftp://www.3gpp.org/specs/ For the latest version, look for the directory name with the latest date e.g. 2000-09 contains the specifications resulting from the September 2000 TSG meetings.

3)	With "track changes" disabled, paste the entire CR form (use CTRL-A to select it) into the specification just in front of the clause containing the first piece of changed text.  Delete those parts of the specification which are not relevant to the change request.

### 9.1.52	DEDICATED MEASUREMENT INITIATION REQUEST

| IE/Group Name | Presence | Range | IE Type and Reference | Semantics Description | Criticality | Assigned Criticality |
| --- | --- | --- | --- | --- | --- | --- |
| Message Discriminator | M |  | 9.2.1.45 |  | – |  |
| Message Type | M |  | 9.2.1.46 |  | YES | reject |
| Node B Communication Context ID | M |  | 9.2.1.48 | The reserved value “All NBCC” shall not be used when the Report characteristics type is set to “On-Demand”. | YES | reject |
| Transaction ID | M |  | 9.2.1.62 |  | – |  |
| Measurement ID | M |  | 9.2.1.42 |  | YES | reject |
| Dedicated Measurement Object Type | M |  | 9.2.1.22 |  | YES | reject |
| CHOICE Dedicated Measurement Object Type | M |  |  |  | YES | reject |
| >RL |  |  |  |  | – |  |
| >>RL Information |  | 1..<maxnoofRLs> |  |  | EACH | reject |
| >>>RL ID | M |  | 9.2.1.53 |  | – |  |
| >>>DPCH ID | O |  | 9.2.3.5 | TDD only | – |  |
| >ALL RL |  |  | NULL |  | – |  |
| >RLS |  |  |  | FDD only | – |  |
| >>RL Set Information |  | 1..<maxnoofRLSets> |  |  | – |  |
| >>>RL Set ID | M |  | 9.2.2.39 |  | – |  |
| >ALL RLS |  |  | NULL | FDD only | – |  |
| Dedicated Measurement Type | M |  | 9.2.1.23 |  | YES | reject |
| Measurement Filter Coefficient | O |  | 9.2.1.41 |  | YES | reject |
| Report Characteristics | M |  | 9.2.1.51 |  | YES | reject |
| CFN reporting indicator | M |  | FN reporting indicator 9.2.1.29B |  | YES | reject |
| CFN | O |  | 9.2.1.7 |  | YES | reject |

| Range | Explanation |
| --- | --- |
| MaxnoofRLs | Maximum number of individual RL's a measurement can be started on. |
| MaxnoofRLSets | Maximum number of individual RL Sets a measurement can be started on. |

# Comments

Page: 1
 Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Page: 1
 Enter the CR number here. This number is allocated by the 3GPP support team.

Page: 1
 Enter the revision number of the CR here. If it is the first version, use a "-".

Page: 1
 Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the lastest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

Page: 1
 For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Page: 1
 Mark one or more of the boxes with an X.

Page: 1
 Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Page: 1
 Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Page: 1
 Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. Work item acronyms are listed in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Page: 1
 Enter the date on which the CR was last revised.

Page: 1
 Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "3GPP working methods".

Page: 1
 Enter a single release code from the list below.

Page: 1
 Enter text which explains why the change is necessary.

Page: 1
 Enter text which describes the most important components of the change. i.e. How the change is made.

Page: 1
 Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Page: 1
 Enter each the number of each clause which contains changes.

Page: 1
 Enter an X in the box if any other specifications are affected by this change.

Page: 1
 List here the specifications which are affected or the CRs which are linked.

Page: 1
 Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

Page: 1
 This is an example of pop-up text.

# Text boxes

### 1.1.3