3GPP TSG-RAN WG3 Meeting #18 	R3-010190

Lidingö, Sweden, 15-19 Jan 2001

| CR-Form-v3 |
| --- |
| CHANGE REQUEST |
| ( | 25.413 | CR | 248 | ( rev | - | ( Current version: | 3.4.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | (U)SIM |  | ME/UE |  | Radio Access Network | X | Core Network | X |
| Title: ( | Editorial correction to RANAP Paging Procedure Description |
| Source: ( | Vodafone Group |
| Work item code: ( |  |  | Date: ( | Jan 12, 2001 |
| Category: ( | D |  | Release: ( | R99 |
|  | Use one of the following categories: F (essential correction) A (corresponds to a correction in an earlier release) B (Addition of feature), C (Functional modification of feature) D (Editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | In R3#17 (Chicago), during the RANAP Review questions were asked as to accuracy of the Paging Procedure description. There may be some misleading text present in explaining the function. |
| Summary of change: ( | Minor Updates made to the Paging Procedure Textual description in Ch 8.15. |
| Consequences if ( not approved: | Misunderstanding of the RANAP Paging Procedure. |
| Clauses affected: ( | Ch 8.15. |
| Other specs ( |  | Other core specifications ( |  |
| affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: ( |  |

How to create CRs using this form:

Comprehensive information and tips about how to create CRs can be found at: http://www.3gpp.org/3G_Specs/CRs.htm.  Below is a brief summary:

1)	Fill out the above form. The symbols above marked ( contain pop-up help information about the field that they are closest to.

2)	Obtain the latest version for the release of the specification to which the change is proposed. Use the MS Word "revision marks"  feature (also known as "track changes") when making the changes. All 3GPP specifications can be downloaded from the 3GPP server under ftp://www.3gpp.org/specs/ For the latest version, look for the directory name with the latest date e.g. 2000-09 contains the specifications resulting from the September 2000 TSG meetings.

3)	With "track changes" disabled, paste the entire CR form (use CTRL-A to select it) into the specification just in front of the clause containing the first piece of changed text.  Delete those parts of the specification which are not relevant to the change request.

## 8.15	Paging

### 8.15.1	General

The purpose of the Paging procedure is to enable the CN to request that the UE should contact that CN node. The procedure uses connectionless signalling.

### 8.15.2	Successful Operation

# Figure 1: Paging procedure. Successful operation.

The CN shall initiate the procedure by sending a PAGING message. This message shall contain information necessary for RNC to be able to page the UE, like:

-	CN Domain Indicator.

-	Permanent NAS UE Identity.

-	Temporary UE Identity.

-	Paging Area.

-	Paging Cause.

-	Non Searching Indicator.

-	DRX Cycle Length Coefficient

The CN Domain Indicator IE shall be used by the RNC to identify from which CN domain the PAGING message originates.

The Permanent NAS UE Identity IE (i.e. IMSI) shall be used by the UTRAN paging co-ordination function to check if a signalling connection towards the other CN domain already exists for this UE. In that case, the radio interface paging message shall be sent via that connection instead of using the paging broadcast channel.

The Temporary UE Identity IE (e.g. TMSI) is the temporary identity of the user (allocated by that CN Domain) which can be used in a radio interface paging message. If the Temporary UE Identity IE is not included in the PAGING message, the RNC shall use the Permanent NAS UE Identity instead – assuming no signalling connection exists.

The Paging Area IE shall be used by the RNC to identify the area in which the radio interface paging message shall be broadcast in case no signalling connection, as described above, already exists for the UE. If the Paging Area IE is not included in the PAGING message, the whole RNC area shall be used as Paging Area – provided no signalling connection exists for that UE.

The Paging Cause IE shall indicate to the RNC the reason for sending the PAGING message. The paging cause is transferred transparently to the UE.

The Non Searching Indication IE may be used by the RNC to decide whether the UTRAN paging co-ordination function needs to be activated or not. In the absence of this IE, UTRAN paging co-ordination shall be performed.

If the DRX Cycle Length Coefficient IE may be included in the PAGING message, and if present, the UTRAN shall, when applicable, use it for calculating the paging occasions for the UE.

It should be noted that each PAGING message on the Iu interface relates to only one UE and therefore the RNC has to pack the pages into the relevant radio interface paging message.

The core network is responsible for the paging repetition over the Iu interface.

### 8.15.3	Abnormal Conditions

Not applicable.

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the lastest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. Work item acronyms are listed in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "3GPP working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is an example of pop-up text.