## Slide 1
Context Aware Content Delivery
3GPP TSG-RAN WG3 Meeting # 91 R3-160301 St. Julian's, Malta, 15th – 19th February 2016
Agenda item: 30
Source: CMCC
Document for: Information

## Slide 2: Content
Background
Motivation
  Example of Multimedia issues
Potential Solutions for content delivery
  Move content closer to eNB by caching
  Local breakout
  Example of media caching
Other content delivery issues
  Potential TCP optimization
Further consideration on edge Caching
  Selective RAN caching and video/TCP acceleration

## Slide 3: Background
Voice was major service of mobile network. 3GPP defined voice specific optimizations
  Protocols: SPS, TTI bundling, PCC …
  Architecture: PCC/QoS, CSFB, SRVCC
Streaming video will be the major consumer of mobile internet bandwidth
TCP takes 95% connections and 97% data volume in internet
3GPP did not define optimizations with respect to streaming video and TCP

## Slide 4: Motivation
Proliferation of smart mobile devices and popularity of OTT, APP has created both a unique business opportunity and some network challenges for Mobile Operators:
  Networks are often required to deliver large, high bandwidth files to end users, e.g from streaming media content providers.
  If the available throughput from RAN to the UE falls below the bandwidth required then files are delivered too slowly, resulting in a bad user experience.
  Large numbers of subscribers accessing multimedia content from a particular area can create localized capacity shortfalls.
Operators need to consider service provision based on content delivery

## Slide 5: Example of Multimedia Issues: Issues in Streaming Video
Video is transmitted in same way as regular internet traffic
  Video segment if not prioritized when playout buffer is exhausting
  Video segment is not prioritized or selectively prioritized for better QoE
Video is not accurately adapted per radio channel status
  DASH client selects video adaption set without direct info on radio link capacity and status
Optimization for video transmission over wireless has been discussed by academic world for sufficient long time. It is time to adopt some low hung fruits in 3GPP

## Slide 6: Potential Solutions for content delivery: Move content closer to eNB by caching or Local breakout
By considering content caching closer to eNB or local breakout, operators can easily achieve the following goals:
  Easy delivery of video, audio rich content
  Significantly reduced page load time of your website
  Reduce CN backhaul link constraint
  retaining more customers (they are more satisfied)
  no geographical barriers
  build more interactive website at no cost of losing visitors due to latencies
  Reaching mobile customers with ease

## Slide 7: eNB caching and local breakout scenarios: Content moved closer to eNB by caching
eNB
S-GW
MME
P-GW
EPC
Access
Ring
Core
LIG
PCRF
OCS
Edge Cache
UE
Aggregation
Ring
Reduce end-to-end latency, improve user experience
Ease high load in the backhaul and core network
Benefits
Open issues
Potential solutions
Content delivery path selection
To guarantee service continuity during mobility
Fast cross-vendor deployment
Charging
Lawful interception
UE assists eNB choose the content delivery path rapidly
Mobility procedure enhancement
Post-paid by CP or introduce a new charging node
Support local traffic image storage and forwarding
Standardized or vendor s
pecific interface

## Slide 8: eNB caching and local breakout scenarios: Local breakout
EPC
Routing Decision
mCDN
S1 bearer
Routing
Decision
mCDN
eNB
EPC
IP Packet
IP Packet
Local Network
S1 bearer
Routing Decision
mCDN
eNB
EPC
IP Packet
IP Packet
Local
Network
Protocol
Translation
GTP Packet
Case1：eNB based service re-routing
Problem: not supported by conventional eNBs, both GTP and IP flows should be supported
Potential solutions: Enhanced eNB with routing decision and protocol translation function, however, mobility may easily supported
Case 2: eNB based service re-routing and protocol translation
Problem: not supported by conventional eNB, new logical function entity needs to be deployed, introducing new interfaces
Potential solutions : enhanced eNB, new function definition, interface between eNB and new function, mobility handling procedures
Internet
Internet
address
Translation

## Slide 9: Example of Media caching closer to eNB: Streaming Video Optimization
Horizon Optimization: Move content closer to eNB by caching
Vertical Optimization
  Video-aware RAN optimization
  Radio-aware video optimization
Take SA4/MPEG DASH-IF into consideration

## Slide 10: Other content delivery issues: Issues in TCP
Inaccurate TCP congestion control
  TCP uses packet loss and/or delay spike as congestion signal for congestion control without radio channel capacity and status info
  Leads to low LTE link utilization and/or long delay
RAN is not aware of TCP
  Cannot selective prioritize or protect TCP packets

## Slide 11: Potential TCP Optimizations
Deliver radio info to TCP for accurate congestion control
TCP-aware optimization in RAN

## Slide 12: Further consideration on edge Caching
Multi-level caching in internet, core network and RAN could coexist and work independently
  Internet and core network caching may be supported either without standard change or by SA2
  RAN caching could be defined by RAN3
What to cache in RAN
  Popular video, picture, web news, downloading

## Slide 13: Selective RAN caching and video/TCP acceleration
Enables new business models for MNO
  As secondary acceleration of internet CDN
  As independent CDN provider
Standardization
  Design ideal solution for better performance and lower cost
  Enables multi-vendor interworking
  Enables MNO interworking with content provider and UE
  Builds health eco system

## Slide 14: Q & A