## Slide 1: Summary of offline discussion on User Inactivity Monitoring
NTT DOCOMO, INC.
Draft R3-181405
3GPP TSG RAN WG3 #99 meeting
February 26th – March 2nd, 2018 Athens, Greece

## Slide 2: Tasked work for come back
CB: # 21_UserInactivityMonitoring
- where is user inactivity monitoring located?
- is user inactivity reporting needed?
- merge discussion from 1315, 1193, 1194 as needed and agreeable
- capture comments from online disc
(NTT)
Summary of offline discussion R3-181405

## Slide 3: Location and need of reporting
2 possible locations of user inactivity monitoring: CU(-UP) or DU
User inactivity needs to be known at CU(-CP) to trigger appropriate connection control (e.g. sending UE to suspend, inactive, idle)
  For EN-DC, user inactivity will then be made known to eNB from CU(-CP) via e.g. X2 SENB RELEASE REQUIRED
Need of user inactivity reporting depends on:
  The location of user inactivity monitoring functionality (at CU(-UP) or DU)
  The disaggregated gNB scenario (split CU/DU or split CP-CP/CU-UP/DU)
 | Split CU/DU | Split CU-CP/CU-UP/DU
Monitoring at CU(-UP) | Reporting not needed | Reporting needed on E1
Monitoring at DU | Reporting needed on F1-C | Reporting needed on F1-C
CU
DU
F1-C
DU
E1
CU-CP
CU-UP
F1-C

## Slide 4: Reasons to monitor at CU(-UP) or DU
Reasons provided by proponents to monitor at CU(-UP)
  No reporting is needed for the split CU/DU case
    No signaling required for the split CU/DU case
    It is status quo when only split CU/DU case is considered (since there is no specification impact)
  For lower layer split, user inactivity monitoring will anyways be at CU
Reasons provided by proponents to monitor at DU
  User inactivity monitoring is anyways performed in DU
    E.g. for MAC deactivation control, MAC DRX control, MAC performance monitoring
  Same implementation can address both split CU/DU and split CU-CP/CU-UP/DU
  More precise monitoring of user inactivity is possible
    For UL, DU can also take into account UE buffer status (whereas CU only knows of data over F1)
    For DL, DU can also take into account retransmissions
      But CU can also take it into account since it buffers data until ACKs are received via DDDS
    DU can also take into account radio activity (i.e. DL-SCH/UL-SCH activity)
      But does it really help connection control? Isn’t it just data existence which matters?
Other comments
  Signaling amount in relation to DUs per UE and CP-UPs per UE were mentioned as possible benefits for both options of monitoring location

## Slide 5: Way forward alternatives
Following way forward alternatives were identified
  Don’t specify user inactivity reporting
    Connection control at CU can take into account user inactivity
      For split CU/DU, if monitoring at CU
  Specify user inactivity reporting in E1 interface
    Connection control at CU(-CP) can take into account user inactivity
      For both split CU/DU and split CU-CP/CU-UP/DU, if monitoring at CU(-UP)
  Specify user inactivity reporting in F1 interface
    Connection control at CU(-CP) can take into account user inactivity
      For split CU/DU, if monitoring at CU
      For both split CU/DU and split CU-CP/CU-UP/DU, if monitoring at DU
  Specify user inactivity reporting in both F1 and E1 interfaces
    Connection control a CU(-CP) can take into account user inactivity
      For both split CU/DU and split CU-CP/CU-UP/DU, if monitoring at CU(-UP)
      For both split CU/DU and split CU-CP/CU-UP/DU, if monitoring at DU

## Slide 6: Discussion on Way forward alternatives
All agrees the followings
  gNB should support user inactivity monitoring (at CU(-UP) and/or DU)
  CU(-CP) should be aware of user inactivity
It was discussed that the following alternatives allow freedom of implementation for location of user inactivity monitoring
  Specify user inactivity reporting in F1 interface
  Specify user inactivity reporting in both F1 and E1 interfaces
However, there were comments from several companies that such flexibility is not desirable for the following reasons
  Interoperability issues
    Unless either monitoring at CU(-UP) or monitoring at DU can be mandated
  Vendors may end up having to support both monitoring at CU(-UP) and monitoring at DU

## Slide 7: Suggested Way forward
First, try to see if decision can be reached on the location of user inactivity monitoring
  Allow only at CU(-UP)
  Allow only at DU
  Allow both at CU(-UP) and at DU
If decision on the above can be reached, then the following will follow for user inactivity reporting
  If a. is decided for the location of user inactivity monitoring
    Support user inactivity reporting in E1
  If b. is decided for the location of user inactivity monitoring
    Support user inactivity reporting in F1-C
  If c. is decided for the location of user inactivity monitoring
    Support user inactivity reporting both in F1-C and in E1