## Slide 1: Summary of offline discussion on QoS handling
Deutsche Telekom
R3-181496
3GPP TSG RAN3#99
February 26th – March 2nd, 2018
Athens, Greece

## Slide 2: Tasked work for Come-Back # 63
CB: # 63_QoS handling
- Should we provide QoS flow level info to DU?
- which node decides aggregated QoS -> whether we should provide DRB level QoS info to DU?
- is adm ctrl per flow or per DRB? In CU or DU?
- implications in terms of inter-vendor interoperability?
- any implications w.r.t. ULLC, fast-changing radio environment and centralized CU?
- clarify possible WF
(DT)
Summary of Offline Discussion on QoS Handling in R3-181496

## Slide 3: Point of discussion
As outcome of RAN3 AH-1801 meeting following three alternative solutions were identified (see R3-180606), which were further evaluated for the RAN3#99 meeting:
  Alt.1: CU provides to DU, QoS profile for each flow
    I.e., CU takes QoS profile info for each flow received over NG, and just forwards them as-is to DU
  Alt.2: CU provides to DU, QoS profile for each DRB
    I.e., CU takes QoS profile info for each flow received over NG, determines an “aggregate QoS profile” for each DRB, and forwards them to DU
  Alt.3: CU provides to DU, QoS profile for each flow and DRB
    I.e., Alt.1 plus Alt.2
During the discussion in the regular session on AI 10.10.7 no conclusion was achieved, as each of three solutions was preferred by several companies in RAN3 based on arguments raised in the corresponding tdocs.

## Slide 4: Discussion status: Common understanding / Disagreements / To be discussed
Based on QoS information from 5GC the CU selects an appropriate “aggregated DRB QoS profile” for a DRB in which one or more QoS flows from 5GC UPF will be mapped.
  Note 1: In case of a one-to-one mapping between a QoS flow and a DRB, the “aggregated DRB QoS profile” corresponds to the QoS profile of the corresponding QoS flow.
  Note 2: In case that QoS flows with diverging QoS requirements are mapped to a common DRB, it is FFS how to define the “aggregated DRB QoS profile” (up to vendor-specific implementation and/or by defining policies that can be set by operators?).
  Note 3: Even if allowed according to TS 38.300, the mapping of QoS flows with totally diverging QoS characteristics should be suppressible by suitable policies in the CU.
The CU signals the “aggregated DRB QoS profile” for the DRB to the DU.
This information may be optionally (alt: is) accompanied by the QoS profiles of the QoS flows mapped to that DRB.
  Note 4: Optional as in the case of a one-to-one mapping this information would be redundant.
Admission control is under responsibility of the DU based on DRB level.
Taking the instantaneous resource allocation into account the DU may reject the DRB, may accept the DRB with the “aggregated DRB QoS profile” or may choose another profile, which may be different from CU’s choice.
In the latter case the DU will signal the chosen “aggregated DRB QoS profile” to the CU. This means the DU can trigger the CU with its feedback to map e.g. only a pre-selected number of flows to the DRB.
Has the CU to follow DU’s feedback or can it reject it?

## Slide 5: Next steps
Continue in RAN3#99bis to discuss the required procedures for QoS handling between CU and DU.
Clarify open issues:
  Delivery of QoS info per QoS flow for each flow in the DRB from CU to DU as mandatory or optional feature?
  Is the DU allowed to propose a modified “aggregated DRB QoS profile” back to CU?
  Has the CU to follow DU’s feedback or can it reject it?
  How to define an “aggregated DRB QoS profile”?
Following issues still to be considered (if there is an impact):
  Implications in terms of inter-vendor interoperability?
  Implications w.r.t. ULLC, fast-changing radio environment and centralized CU