3GPP TSG-RAN WG3 Ad-Hoc	R3-101961

Beijing, China, June 29-July 2, 2010

Agenda item:	7.5

Source: 	Qualcomm Incorporated, Ericsson, Nokia Siemens Networks,
	Vodafone, Deutsche Telekom, Huawei, CMCC, Samsung, 
	NTT DOCOMO, Mitsubishi, ZTE

Title: 	Startup procedure for Relay Nodes

Document for:	Discussion and Decision

## 1. 	Introduction

With the introduction of Relays in Rel-10 [1], discussions about how to configure the relay nodes and about relay start-up procedures have started in recent RAN2 and RAN3 meetings, where different options have been considered [e.g. 2-3]. This paper has the intent to provide an overall picture of how the relay start-up procedure could look like, to guide through the various details included in our further contributions [4-5] as well as to help the overall Stage-2 discussion.

A proposed text for updating TS 36.300 [6] and include relay start-up procedure is also provided.

# 2. Text Proposal for Relay CR for TS 36.300

### 4.7.6	Signaling procedures

#### 4.7.6.x	RN startup procedure

Figure 4.7.6.x-y shows a simplified version of the startup procedure for the RN. The procedure is based on the normal UE attach procedure [17] and it consists of the following two phases:

Editor’s Note 1:	It is FFS if the RN is notified over e.g. SIBs before the attach procedure about the presence of DeNBs.

- Phase I: Attach for RN preconfiguration.
The relay node attaches to the E-UTRAN/EPC as UE at power-up and retrieves initial configuration parameters from RN OAM. After this operation is complete, the relay node detaches from the network as a UE.

- Editor’s Note 2:	It is FFS if attach for RN preconfiguration is required or not.

- Phase II: Attach for RN operation.
The relay node connects to a DeNB to start relay operations. For this purpose, the normal RN attach procedure described in section 4.7.6.z is applied. The MME indicates to the DeNB that the RN is authorized to attach as a relay. After the DeNB initiates setup of bearer for S1/X2, the RN initiates the setup of S1 and X2 associations with the DeNB (see section 4.7.4), and begins relay operations.

- Editor’s Note 3:	It is FFS how to select the MME for the RN during attach for RN operation.

- Editor’s Note 4:	It is FFS how the MME selects the DeNB as the S/P-GW of the relay during attach for RN operation.

Figure 4.7.6.x-y: RN Startup procedure

## 3.	Conclusions

RAN3 is kindly asked to discuss the proposed relay start-up procedure and related text proposed as CR to 36.300.

Proposal 1: It is proposed to include the relay start-up procedure described in section 3 of this document in the stage-2 design specification.

## 4.	References

[1] 3GPP TR 36.806 – v2.0.0. (2010-02): Relay architectures for E-UTRA (LTE-Advanced)

[2] R2-102085 – Summary of Email discussion [69#31] LTE: Relay Configuration at start-up / subframe reconfiguration

[3] R3-101604 – On Relay Configuration Principle, Qualcomm Inc.

[4] R3-101938 - Framework for Relay Configuration, Qualcomm Inc.

[5] R3-101939 - Initial Relay Configuration, Qualcomm Inc.

[6] 3GPP TS 36.300 - v 10.0.0 (2010-06) - Overall description – Stage 2