## Slide 1: Way forward on Mobility with NW slicing
NTT DOCOMO, INC.
R3-180562
3GPP TSG RAN WG3 NR Adhoc meeting
January 22nd – 25th, 2018 Sophia Antipolis, France

## Slide 2: Tasked work for come back
CB: # 28_Mobility4Slices
- capture agreements
- Whether to signal from target RAN node list of slices associated with failed PDU sessions?
- Need for explicit indication of non-supported PDU sessions?
(NTT)
WF R3-180562

## Slide 3: capture agreements
The followings were agreed
  The S-NSSAI should be provided by the MN in S-NODE MODIFICATION REQUEST message
  In case target node does not support the same slices as the source node, both Xn and NG HO are possible
  Slices not supported at the target node shall be dropped
  For Xn HO, target RAN node rejects resources for PDU sessions for non-supported slices (in the HO response message)
  Target RAN node signals failed PDU session (AS) resources

## Slide 4: Whether to signal from target RAN node list of slices associated with failed PDU sessions?
Through offline discussion it was identified that the actual question should be as follows:
  Whether to signal from target RAN node cause (or alternatively list of slices) associated with failed PDU sessions?
    NOTE: To be precise, “Whether to signal from target RAN node” means “Whether to signal from handover target RAN node to AMF in PATH SWITCH REQUEST message”
Reasoning/justification to signal cause
  It may help the AMF to take appropriate actions depending on the failure cause (e.g. “associated slice not supported”, “temporarily unable to support associated slice”, “non-slice reasons”)
  Will help to detect misalignment in AMF’s understanding on the supported slice at target RAN node (normally no misalignment, but there can be abnormal cases causing misalignment)
  It is just normal protocol behavior to include cause in a “failed list”

## Slide 5: Whether to signal from target RAN node list of slices associated with failed PDU sessions?
WF Proposal
  Continue discussion in RAN3#99 on whether the reasons captured in this document would justify the introduction of failure case (or alternatively list of slices) for failed PDU sessions in the PATH SWITCH REQUEST message

## Slide 6: Need for explicit indication of non-supported PDU sessions?
This issue has been covered by CB: # 28