## Slide 1: Way Forward on LTE CU DU Aspects
Agenda Item：12.3
Source：Orange, Huawei
3GPP TSG-RAN WG3 NR AdHoc 1801 R3-180602
Sophia Antipolis, France, 22-26 January 2018

## Slide 2
Way Forward
Design new V1 interface to support LTE CU DU architecture, align with F1 interface for the applicable functions/procedures.
V1 interface supports the features applying to both eNB connected to EPC and to ng-eNB connected to 5GC.
  V1 interface align with the F1 interface when the ng-eNB is connected to 5GC
  V1 interface also supports the following LTE features when the eNB is connected to EPC:
    NB-IoT, eMTC
    eDRX, Coverage Enhancements
    MDT/SON for network optimization
    Access Control: ACB/EAB/SSAC and ACDC
    V2X
    Inter RAT Mobility, including mobility to/from UTRAN/ GERAN/CDMA (CSFB/SRVVC/Handover, etc.)