## Slide 1: Title: Shaping filter characteristics including transmitter and link performance
3GPP TSG-RAN WG4#100-e Meeting R4-2112807
Electronic Meeting, 16th –27th August, 2021
Source: Nokia, Nokia Shanghai Bell
Agenda item: 10.6.4
Document for: Approval

## Slide 2: 1- Introduction
This contribution relates to a study item agreed in RAN#91-e, namely “optimizations of pi/2 BPSK uplink power in NR” [1]. In this paper we characterize the net gain of different shaping filters considering transmitter and link level performance. This work is related to the following study item objective:
Identify shaping filter characteristics necessary to enable the new power capability while ensuring good and robust BS receiver performance.
  Justify specification of a pulse shaping filter for this new identified UE power capability if it differs from filter impulse response specification in TS38.101-1 clause 6.4.2.4.1.E
  Identify if necessary changes are needed to EVM equalizer flatness mask requirements to capture necessary filter shaping. Changes to the existing 14 dB p-p baseline to be assessed in relation to any potential gains in UL link performance while still ensuring robust BS receiver performance for all UEs in a cell.

## Slide 3: 2- Discussion
In this paper we characterize the net gain of different shaping filters considering transmitter and link level performance.
Transmitter performance results used in this contribution are shown in [3].
Receiver performance results used in this contribution as shown in [4].
According to the agreed way forward [2], different filters that conform to 38.101-1 Rel-16 are tested to study the transmitter performance. In this document, three different 3-tap filters (namely [-0.2 1 -0.2], [-0.28 1 -0.28] and [-0.335 1 -0.335]) are tested, as well as two triangular windows with different design parameters. For the filters mentioned, the DMRS are also shaped, following the assumption in the current specification that the spectral shaping is transparent to the gNB receiver.
Additionally, the [1+D] filter (which does not conform to 38.101-1 Rel-16) is included in the evaluations with DMRS not shaped (i.e., the filter shape is not transparent to the gNB receiver).

## Slide 4: 2- Discussion
The figure shows the tested filters. The triangular filters are generated in such a way that the slope is the maximum slope that fits the maximum attenuation in the two frequency ranges that separate one half of the allocation (same frequency ranges as the EVM equalizer flatness mask). For the evaluations, the number in brackets corresponds to the attenuation (in dB) of the first and second frequency range.
In the continuation, the filters are referred as:
[-0.2 1 -0.2]  0.2
[-0.28 1 -0.28]  0.28
[-0.335 1 -0.335]  0.335
[1+D]  [1+D]
Triangular window [6 14]  Triang A
Triangular window [6 8]  Triang B
0.335 is the most aggressive 3-tap filter that meets the current spectral flatness requirements, less aggressive 3-tap filters are included too (0.2 and 0.28).
Triang A is the most aggressive triangular window that meets the current spectral flatness requirements, and Triang B is a less aggressive triangular window, with similar frequency shape as the 0.2 3-tap filter.

## Slide 5: 2- Discussion
It must be noted that the [1+D] filter tested requires specifying the shaping filter function when the DMRS are not shaped.
In order to characterize the filters, it is needed to consider both the transmitter performance (i.e., the achievable output power) from our paper [3], and the link level performance obtained in [4]. With that information, it is possible to compute the net gain with respect to a reference filter as:
Where is the output power of the filter being compared against the reference filter, is the output power of the reference filter, is the required SNR to achieve 10% BLER of the reference filter, and is the required SNR to achieve 10% BLER of the filter being compared against the reference filter.
The following slides show the net gain of the filters with respect to the [1+D] filter with DMRS not shaped, for pi/2 BPSK considering the transmitter [3] and link level [4] performance for the following allocations and channels:
2, 4, 8, 16 and 64 PRB
TDL-C 300 ns, TDL-A 30 ns and TDL-D 30 ns
Filters tested:
[-0.2 1 -0.2], [-0.28 1 -0.28], [-0.335 1 -0.335], Triang A [6 14] and Triang B [6 8]
The tested filters assume that the filter is transparent to the gNB, and the DMRS are shaped. For the [1+D], matched filter is used in reception.

## Slide 6: 2.1- Discussion. Net gain. TDL-C 300 ns
For 2 and 4 PRB, [1+D] without DMRS shaped performs better than all the filters in center allocations (0.1-0.2 dB better than the 0.2 filter and 0-0.1 dB better than Triang B).
For 8 and 16 PRB, [1+D] without DMRS shaped is never the best for any allocation. Triang B is the best filter, providing gain for most of the possible allocations within the channel.
For 64 PRB, in central allocations, the performance is the same as Triang B. In edge band allocations, the 0.335 filter provides up to 0.9 dB gain.
For small allocation sizes, it must be noted that less aggressive filters perform better than aggressive filters in central band allocations.
Observation: For allocation sizes ≤ 16 PRB, less aggressive filters perform better than aggressive filters in central band allocations.

## Slide 7: 2.1- Discussion. Net gain. TDL-A 30 ns
For 2 and 4 PRB, [1+D] without DMRS shaped performs better than all the filters in all allocations (0.1-0.2 dB better than the Triang B filter).
For 8 and 16 PRB, [1+D] without DMRS shaped is never the best for any allocation position.
For 64 PRB, in central allocations, the performance is the same as Triang B. In edge band allocations, the 0.335 filter provides up to 0.8-0.9 dB gain.
For small allocation sizes, it must be noted that less aggressive filters perform better than aggressive filters in central band allocations.

## Slide 8: 2.1- Discussion. Net gain. TDL-D 30 ns
For 2 and 4 PRB, [1+D] without DMRS shaped performs better than all the filters in all allocations (0.1-0.2 dB better than the Triang B filter)
For 8 and 16 PRB, [1+D] without DMRS shaped is never the best for any allocation. In central band allocations, Triang B provides gain. 0.335 filter provides up to 1 dB gain in edge band allocations.
For 64 PRB, in central band allocations Triang B provides gain. In edge allocations, Triang A, 0.28 and 0.335 filters provide up to 0.8 dB gain.
For small allocation sizes, it must be noted that less aggressive filters perform better than aggressive filters in central band allocations.

## Slide 9: 3- Conclusions
In most of the simulated cases, Rel-15 approach with suitable shaping filter outperforms [1+D] w/o DMRS shaping with a clear margin. The gain potential for [1+D] w/o DMRS shaping is expected to be negligible compared to the current solution.
Different filters have very different performance in the evaluation cases depending on allocation configuration. The most aggressive filters have up to 0.6-0.8 dB loss with respect to the less aggressive filters in the small allocations (2, 4 PRB in the evaluation) and central band allocations. These results suggest that there should be different spectral flatness requirements for the filters based on the allocation within the channel band. It would be beneficial to have tighter spectral flatness requirements for small allocations in the center of the channel band to optimize the net gain.
Observation 1: In most of the simulated cases, Rel-15 approach with suitable shaping filter outperforms [1+D] w/o DMRS shaping with a clear margin. The gain potential for [1+D] w/o DMRS shaping is expected to be negligible.
Observation 2: For allocation sizes ≤ 16 PRB, less aggressive filters perform better than aggressive filters in central band allocations.
Observation 3: There is not a single solution for all the evaluated cases. Depending on the allocation configuration, different filters (i.e., more or less aggressive) perform differently.
Proposal 1: Keep the Rel-15 approach (i.e. transparent spectral shaping to gNB receiver) in Rel-17 where both DMRS and data are shaped and the actual pulse shaping filter is left for UE implementation
Proposal 2: Keep the current spectral flatness requirements for large PRB allocations (e.g. ≥ 16 PRBs)
Proposal 3: Consider tighter spectral flatness requirements for small PRB allocations (e.g. <16 PRBs) to optimize the net gain

## Slide 10: References
[1] RP-210910, Optimizations of pi/2 BPSK uplink power in NR, Moderator (Huawei)
[2] R4-2108018, WF on Waveform configuration, parameters for link simulations and agreements, Qualcomm
[3] R4-2112806, Transmitter performance for pi/2 BPSK with spectral shaping, Nokia, Nokia Shanghai Bell
[4] R4-2112805, Receiver performance for pi/2 BPSK with spectral shaping, Nokia, Nokia Shanghai Bell