## Slide 1: Views on RAN4 Rel-18: RRM Enhancements
3GPP TSG RAN WG4 Meeting #101-bis-e R4-2200547
Electronic Meeting, 17th – 25th January 2022
Agenda Item: 10
Source: Intel Corporation
Document for: Information

## Slide 2: Introduction
Many candidate objectives were deprioritized in Rel-16/17 discussion and may be further considered to ensure proper 5G networks operation under various practical scenarios
Several additional objectives were identified after the Rel-17 WI scope was stabilized and those can be considered in Rel-18
The work on the definition of RRM requirements shall continue in Rel-18 with the goal to cover additional use cases to ensure proper 5G deployments and operations
Potential scope of Rel-18 items shall balance between RRM “leftovers” (i.e., items deprioritized in previous releases due to TU constraints) and new RRM areas
Chart: Big Discussions in Rel-16 RRM
| Agreed CR numbers
eRRM | 109
NR-U | 76
MR-DC | 54
Pos | 47
CSIRS L3 | 40
eMIMO | 38
Background
Multiple RAN4-led RRM enhancements were defined in the scope of Rel-16 and Rel-17
  Rel-16 NR RRM enhancements WI [RP-201883]
  Rel-16 NR L3 CSI-RS measurements WI [RP-210590]
  Rel-17 NR Further RRM enhancements WI [RP-202874]
  Rel-17 NR MG Enhancements WI [RP-210679]
Many objectives of Rel-16/17 focus on the introduction of the requirements not covered by initial Release 15

## Slide 3: Introduction
Extensive discussion on Rel-18 RRM objectives took place as a part of email thread [RAN94e-R18Prep-22] with the following Final proposals [RP-212682]
Proposal #9-1: for RRM requirements enhancement topic, the following high level working areas can be endorsed
  FR2 RRM enhancements
  General RRM requirement enhancement and leftover
  Measurement gap related enhancement and leftover
Proposal #9-2: companies are encouraged to provide more details on the motivation, benefit and specification impacts for each proposed objective for RRM requirement enhancement in RAN#94-e.
In this contribution we provide views on more detailed proposals relevant to FR2 RRM enhancements General RRM requirement enhancement and leftovers, Measurement gap related enhancement and leftover and FR2 HST relevant RRM enhancements

## Slide 4: Candidate Rel-18 objectives
FR2 enhancements
FR2 delay reduction enhancements
FR2-FR2 DAPS HO requirements
Network controlled gaps for UE Rx beam switching
FR2-2 enhancements & leftovers
General RRM requirements/leftovers
FR1 + FR1 NR-DC RRM requirements
CMTC
RLM enhancements
TCI state switch enhancements
Measurement Gap related enhancements
Per-FR gap UE capability enhancement
NeedForGapInfoNR requirements
MG sharing enhancements
Rel-17 leftovers (MG Enhancements and MUSIM)
FR2 HST enhancements
HST FR2 multi-panel receptions (e.g., reduced number of Rx beams)
HST CA FR2
HST FR2 UE type enhancements
Note 1: Identification of Rel-17 leftovers is confirmed at a later stage (e.g., Q1’2022)
Note 2: Further prioritization of the candidate objectives shall take place to ensure that Rel-18 addresses the most urgent market requests

## Slide 5: FR2 Enhancements
FR2 delay reduction enhancements
Background
FR2 RRM requirements consider the number of UE Rx beams, and this leads to rather long delay of procedures
Practical scenarios require much less delays
Selected RRM requirements in FR2 can be revisited to reduce the delay caused as much as reasonable
Candidate objectives
General measurement delay reduction by assuming reduced number of Rx beams
SCell activation delay reduction in FR2
BWP switching delay reduction in FR2
FR2-2 enhancements & leftovers
Background
Further enhancements in the frequency of above 52GHz are expected to be carried out in RAN WG-s in Rel-18
RRM requirements are expected to be defined for both the leftovers from R17 and newly for R18 enhancements
Some of the deployment scenarios are deprioritized in Rel-17 (R4-2115351), while they still received popularity among operators and vendors
Candidate objectives
RRM requirements for leftover deployment scenarios in Rel-17 incl. FR2-2 NR-DC and FR2-1 - FR2-2 NR CA/DC
Note: Identification of RRM scope due to enhancements in Rel-18 of the FR2-2 frequency bands in other WGs shall further take place

## Slide 6: FR2 Enhancements
Network controlled gaps for UE Rx beam switching
Background
To have awareness of the UE RX beam switching and apply scheduling restrictions accordingly, network can allocate certain time intervals for UE to switch its beam.
The UE will be allowed to change its beam during these configured intervals, and the with this awareness the system performance with very short CP length is boosted
Candidate objectives
Study and define mechanisms to schedule gaps for UE Rx beam switching
FR2 – FR2 DAPS handover
Background
FR2-FR2 DAPS handover requirements are missing in the current RRM spec
For UE with capability of FR2 MR-DC, it is beneficial in terms of mobility performance if they can make use of DAPS handovers
Candidate objectives
RRM requirements for FR2-FR2 DAPS handover: sync conditions, delay and interruption

## Slide 7: General/Leftover Enhancements
CMTC
Background
CMTC concept for L3 CSI-RS based measurements has been proposed since R16
Group consensus is that CMTC is beneficial to both UE and network in terms of efficient measurement configuration for UE mobility
Candidate objectives
CMTC configurations
  CMTC lengths, periodicities and offsets
  Multiple CMTC configurations
CSI-RS measurement requirement updates with CMTC
FR1 + FR1 NR-DC RRM requirements
Background
FR1 + FR1 NR-DC band combinations were introduced in R16 timeframe
A very limited set of RRM requirements was defined in R16: only MRTD/MTTD requirements were defined.
Candidate objectives
Specify RRM requirements for FR1 + FR1 NR-DC
    Number of serving carriers requirement
    PSCell addition and release delay requirement
    PSCell change and conditional PSCell change delay requirements
    Scheduling availability of UE during RLM and BFD
    CSSF for NR-DC
Study possibility of release independence from R16

## Slide 8: General/Leftover Enhancements
TCI state switch enhancement
Background
In Rel-16 TCI switching requirement, there was a time gap where UE is not required to receive DL data; it will have impact on the throughput performance in case the first SSB arrives relatively later
RAN4 is to further discuss if UE behavior can be enhanced to receive DL data during the time gap of Tfirst-SSB
Candidate objectives
Enhancement to maintain the UE reception and transmission during the period (or part of period) of MAC CE based TCI switching
Enhancement to maintain the UE reception and transmission during the period (or part of period) of RRC based TCI switching
RLM enhancement
Background
The second IS/OOS BLER has already been supported in RAN1 since R15. However, it cannot be correctly implemented since no corresponding RAN4 requirements
RAN4 is to specify the second RLM BLER pair for voice traffic
Candidate objectives
Specify the second IS/OOS BLER pair for VoNR service

## Slide 9: Measurement Gap Related Enhancements
NeedForGapInfoNR requirements
Background
RAN2 introduced NeedForGapInfoNR capability in TEI16
RAN4 impact is non-trivial for UEs capable of no-gap measurements
RAN4 consensus is that measurement requirements need to be updated
Candidate objectives
Specify interruption due to retuning the vacant chain
Impacts on RRM measurement requirements with gaps
  CSSF
  Measurement period
  Scheduling restrictions
Study possibility of release independence from R16
Per-FR gap indication enhancement
Background
In Rel-16 RAN4 discussed enhancements in indicating UE per-FR gap capabilities. Per-BC indication of per-FR gap capabilities was proposed by several companies
No final conclusions were reached, and companies indicated interest to continue the work to study UE baseband constraints
Candidate objectives
Enhance indication of UE per-FR gap capabilities
Study Per-BC indication of per-FR gap capabilities impacts
  All DL interruptions involving FR1+FR2 BC
  Delay at activation of multiple DL Scells
  Delay at all kinds of BWP switch on multiple CCs
  Additional delay of measurement reporting upon SRS carrier switch
  Autonomous gaps
Other indication is not precluded

## Slide 10: Measurement Gap Related Enhancements
MG sharing enhancement
Background
MG sharing was design to coordinate MG resource allocation between intra-frequency MOs and inter-frequency MOs
The signaling bit string is quite limited to indicate the MG sharing ratio, and therefore it’s far from enough to adequately cover all the prioritization preference from network operators
Candidate objectives
Enhance network indication of measurement gap sharing
Enhance UE behaviors to cope with enhanced network indication of measurement gap sharing
Rel-17 leftovers
Background
RAN4 consensus in Rel-17 is that the mixture among subtopics and the joint requirements in Rel-17 MG_enh WI are considered in Rel-18
Enhancements of MG in several dedicated use cases are not done completely in Rel-17: e.g., MUSIM dedicated gaps.
Candidate objectives
Joint requirements among pre-configured measurement gaps, multiple concurrent measurement gaps, and network controlled short gaps
Measurement gap enhancements for MUSIM operations
Note: detailed objectives subject to further confirmation

## Slide 11: FR2 HST Enhancements
Background
Support of FR2 multi-panel simultaneous reception was assumed in the scope of Rel-16 eMIMO WI but no RAN4 requirements were defined
FR2 UE capability for simultaneous multi-beam reception was introduced in Rel-16 (simultaneousReceptionDiffTypeD-r16)
Multi-panel simultaneous reception CPEs can be considered for generic FR2 deployments and in application to FR2 HST scenario
  Support of IBM (Independent Beam Management) and CBM (Common Beam Management) framework with simultaneous reception on different component carriers from the co-located and non-col-located TRPs was defined in RAN4 in Rel-16/17
IBM concept implies simultaneous reception on different UE panels using separate beams on different component carriers and requires improved UE baseband and RF capabilities (multiple BB chains and support of multiple antenna panels)
HST FR2 multi-panel reception
Candidate objectives:
Specify enhanced HST RRM requirements for CPE UE with simultaneous multi-panel reception

## Slide 12: FR2 HST Enhancements
HST FR2 CA RRM requirements
Background
HST mounted UE is powerful in terms of RF and BB resources; and does not bother by battery life
Carrier aggregation helps boost performance further for HST mounted UE, but Rel-17 considers only single carrier
Candidate objectives
Specify Carrier Aggregation RRM requirements for mounted HST UE in FR2; at least intra-band CA shall be considered, and inter-band CA could depend on vendor and operator inputs
HST FR2 UE type enhancements
Background
Rel-17 does not allow non-HST to access to the HST FR2 network
Network does not clearly differentiate different types of UE in the network
Candidate objectives
Specify applicable RRM requirements for non-HST UE-s in HST network
Introduce, if necessary, UE capability signaling to ensure clear alignment between UE and network knowledge on applicable RRM requirements to different types of UE-s