3GPP TSG-RAN WG4 Meeting # 101-bis-e                                                      R4-2200695

Electronic Meeting, Jan 17th-25th,2022

| CR-Form-v12.1 |
| --- |
| CHANGE REQUEST |
|  | 38.133 | CR |  | rev | 1 | Current version: | 17.4.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | x | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | draftCR for the interruption of NCSG in NR |
| --- | --- |
| Source to WG: | Intel Corporation |
| Source to TSG: | R4 |
| Work item code: | NR_MG_enh-Core |  | Date: | 2022-1-10 |
| Category: | B |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | There is not any gap interruption requirements when NCSG is activated. |
| Summary of change: | Updated the interruption requirements for NCSG in TS38.133 |
| Consequences if not approved: | The requirements on interruption due to NCSG operations will be missed. |
| Clauses affected: | 9.1 |
|  | Y | N |  |  |
| Other specs |  |  | Other core specifications | TS/TR ... CR ... |
| affected: | X |  | Test specifications | TS 38.533 |
| (show related CRs) |  |  | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

| This CR's revision history: |  |
| --- | --- |

--------------START OF CHANGES--------------

#### 9.1.2c	NCSG

The total number of interrupted slots on serving cells is listed in Table 9.1.2c-1 for all serving cells in NR standalone (with single carrier, NR CA).   The interruptions of NCSG in number of slots are listed in Table 9.1.2c-1 when per-UE NCSG is configured. In case that the UE capable of [per-FR measurement gap] is configured with per-FR NCSG, numbers of interrupted slots on FR2 serving cells are listed in Table9.1.2c-2. There are two interruptions in each NCSG occasion, VIL1 before ML and VIL2 after ML, on all serving cells in NR standalone (with single carrier, NR CA). Each of them has number of interrupted slots captured in Table 9.1.2c-1 and Table9.1.2c-2.

Table 9.1.2c-1: Number of interrupted slots on all serving cells during MGL for NR standalone for per-UE and FR1 NCSG

| NR | Number of interrupted slots on serving cells |
| --- | --- |
| SCS | When MG timing advance of 0ms is applied | When MG timing advance of 0.5ms is applied |
| (kHz) | VIL=1ms | VIL=1ms |
| 15 | 1 | 2 |
| 30 | 2 | 2 |
| 60 | 4 | 4 |
| 120 | 8 | 8 |
| NOTE 1: For Gap Pattern ID 0, 1, total number of interrupted subframes on MCG is MGL subframes when MG timing advance of 0ms is applied, and (MGL+1) subframes when MG timing advance of 0.5ms is applied. NOTE 2: NR SCS of 120 kHz is only applicable to the case with per-UE NCSG. NOTE 3: Non-overlapped half-slots occur before and after the VIL. Whether a UE can receive and/or transmit in those half-slots is up to UE implementation. |

Table 9.1.2c-2: Number of interrupted slots on FR2 serving cells during MGL for NR standalone operation (with single carrier, NR CA) for FR2 NCSG

| NR | Number of interrupted slots on serving cells |
| --- | --- |
| SCS | When MG timing advance of 0ms is applied | When MG timing advance of 0.5ms is applied |
| (kHz) | VIL=0.75ms | VIL=0.75ms |
| 60 | 3 | 3 |
| 120 | 6 | 4 |
| [NOTE 1: For Gap Pattern ID 0, 1, total number of interrupted subframes on MCG is MGL subframes when MG timing advance of 0ms is applied, and (MGL+1) subframes when MG timing advance of 0.5ms is applied.] NOTE 3: Non-overlapped half-slots occur before and after the VIL. Whether a UE can receive and/or transmit in those half-slots is up to UE implementation. |

----------------END OF CHANGES--------------

# Comments

Not sure we still need 15Khz and 30KHz for FR2 NCSG

This part (MCG) is still pending on RAN2 decsion.