## Slide 1: Title: Shaping filter characteristics including transmitter and link performance
3GPP TSG-RAN WG4#101bis-e Meeting R4-2204795
Electronic Meeting, 21st February –3rd March, 2022
Source: Nokia, Nokia Shanghai Bell
Agenda item: 11.4.3
Document for: Approval

## Slide 2: 1- Introduction
This contribution relates to a study item agreed in RAN#91-e, and revised in RAN#94e, namely “Revised SID: optimizations of pi/2 BPSK uplink power in NR” [1]. In this paper we characterize the net gain of different shaping filters considering transmitter and link level performance. This work is related to the following study item objective:
Identify shaping filter characteristics necessary to enable the new power capability while ensuring good and robust BS receiver performance.
  The choice of the filter is up to UE implementations and transparent to network.
  Evaluate possible filter requirement applicable to the identified new UE power capability if achievable
  Identify if necessary, changes are needed to EVM equalizer flatness mask requirements to capture necessary filter shaping. Changes to the existing 14 dB p-p baseline to be assessed in relation to any potential gains in UL link performance while still ensuring robust BS receiver performance for all UEs in a cell.

## Slide 3: 2- Discussion
In this paper we characterize the net gain of different shaping filters considering transmitter and link level performance.
Transmitter performance results used in this contribution are shown in [3].
Receiver performance results used in this contribution as shown in [4].
According to the agreed way forward after RAN4#99e [2], different filters that conform to 38.101-1 Rel-16 are tested to study the transmitter performance. In this document, three different 3-tap filters (namely [-0.2 1 -0.2], [-0.28 1 -0.28] and [-0.335 1 -0.335]) are tested, as well as two triangular windows with different design parameters. For the filters mentioned, the DMRS are also shaped, following the agreement in [1] that the spectral shaping is transparent to the gNB receiver.

## Slide 4: 2- Discussion
The figure shows the tested filters. The triangular filters are generated in such a way that the slope is the maximum slope that fits the maximum attenuation in the two frequency ranges that separate one half of the allocation (same frequency ranges as the EVM equalizer spectrum flatness mask). For the evaluations, the number in brackets corresponds to the attenuation (in dB) of the first and second frequency range.
In the continuation, the filters are referred as:
[-0.2 1 -0.2]  0.2
[-0.28 1 -0.28]  0.28
[-0.335 1 -0.335]  0.335
Triangular window [6 14]  Triang A
Triangular window [6 8]  Triang B
0.335 is the most aggressive 3-tap filter that meets the current spectral flatness requirements, less aggressive 3-tap filters are included too (0.2 and 0.28).
Triang A is the most aggressive triangular window that meets the current spectral flatness requirements, and Triang B is a less aggressive triangular window, with similar frequency shape as the 0.2 3-tap filter.

## Slide 5: 2- Discussion
In order to characterize the filters, it is needed to consider both the transmitter performance (i.e., the achievable output power) from our paper [3], and the link level performance obtained in [4]. The link simulations assume that the receiver is not aware of the used shaping filter [4]. With Tx and Rx results, it is possible to compute the net gain with respect to a reference filter as:
Where is the output power of the filter being compared against the reference filter, is the output power of the reference filter, is the required SNR to achieve 10% BLER of the reference filter, and is the required SNR to achieve 10% BLER of the filter being compared against the reference filter.
The following slides show the net gain of the filters with respect to the [-0.2 1 -0.2] filter with DMRS shaped, for pi/2 BPSK considering the transmitter [3] and link level [4] performance for the following allocations and channels:
2, 4, 8, 16 and 64 PRB
TDL-C 300 ns, TDL-A 30 ns and TDL-D 30 ns
Filters tested:
[-0.2 1 -0.2], [-0.28 1 -0.28], [-0.335 1 -0.335], Triang A [6 14] and Triang B [6 8]
The tested filters assume that the filter is transparent to the gNB, and the DMRS are shaped.
The net gain is illustrated w.r.t. [-0.2 1 -0.2] filter

## Slide 6: 2.1- Discussion. Net gain. TDL-C 300 ns
For 2 and 4 PRB, the two less aggressive filters tested (Triang B and 0.2) show the best performance for all the allocations within the channel.
For 8 and 16 PRB, Triang B is the best filter, providing gain for most of the possible allocations within the channel, except in the edge allocations, where more aggressive filters offer gains of up to 1 dB.
For 64 PRB, in central allocations, the performance is the best for Triang B. In edge band allocations, the 0.335 filter provides up to 1 dB gain.
For small allocation sizes, it must be noted that less aggressive filters perform better than aggressive filters.
Observation: For allocation sizes ≤ 16 PRB, less aggressive filters perform better than aggressive filters in terms of achievable output power and link performance..

## Slide 7: 2.1- Discussion. Net gain. TDL-A 30 ns
For 2 and 4 PRB, the two less aggressive filters tested (Triang B and 0.2) show the best performance for all the allocations within the channel.
For 8 and 16 PRB, Triang B is the best filter, providing gain for most of the possible allocations within the channel, except in the edge (or outer) allocations, where more aggressive filters offer gains of up to 1.3 dB.
For 64 PRB, in central allocations, Triang B offers the best performance, with the rest of the filters offering the same net gain. In edge band allocations, the 0.335 filter provides up to 0.8-1.1 dB gain.
For small allocation sizes, it must be noted that less aggressive filters perform better than aggressive filters.

## Slide 8: 2.1- Discussion. Net gain. TDL-D 30 ns
For small allocation sizes, it must be noted that less aggressive filters perform better than aggressive filters.
For 2 and 4 PRB, the two less aggressive filters tested (Triang B and 0.2) show the best performance for all the allocations within the channel.
For 8 and 16 PRB, Triang B is the best filter, providing gain for most of the possible allocations within the channel, except in the edge (or outer) allocations, where more aggressive filters offer gains of up to 1.4 dB.
For 64 PRB, in central allocations, Triang B offers the best performance, with the rest of the filters offering the same net gain. In edge band allocations, the 0.335 filter provides up to 0.7-1 dB gain.

## Slide 9: 3- Conclusions
The most aggressive filters have up to 0.6-0.8 dB loss with respect to the less aggressive filters in the small allocations (2, 4, 8 PRB in the evaluation) and central band allocations. These results suggest that following the agreements on the WF after RAN4#101e [5], and the SI objectives [1] (objective 3. c) there is a need for different spectral flatness requirements for the filters based on the allocation within the channel band. It would be beneficial to have tighter spectral flatness requirements for small allocations band to optimize the net gain.
Observation 1: The most aggressive filters have up to 0.6-0.8 dB loss with respect to the less aggressive filters in the small allocations Observation 2: For allocation sizes ≤ 16 PRB, less aggressive filters perform better than aggressive filters in terms of achievable output power and link performance.
Observation 3: There is not a single solution for all the evaluated cases. Depending on the allocation configuration, different filters (i.e., more or less aggressive) perform differently.
Observation 4: Based on the previous agreement in RAN4#101bis-e [6], if spectrum flatness requirements are not tightened for small allocations, net gain cannot be guaranteed.

## Slide 10: References
[1] RP-213535, Revised SID: Optimizations of pi/2 BPSK uplink power in NR, Nokia
[2] R4-2108018, WF on Waveform configuration, parameters for link simulations and agreements, Qualcomm
[3] R4- 2200727, Transmitter performance for pi/2 BPSK with spectral shaping, Nokia, Nokia Shanghai Bell
[4] R4-2200726, Receiver performance for pi/2 BPSK with spectral shaping, Nokia, Nokia Shanghai Bell
[5] R4-2120057, WF on ’Optimizations of pi/2 BPSK uplink power in NR’ in Rel-17, Huawei, HiSilicon, Qualcomm, Intel
[6] R4-2202386, WF on Optimisations of Pi/2 BPSK UL Power in Nr, Huawei, HiSilicon, Qualcomm