3GPP TSG-RAN4 WG4 Meeting #102-e	R4-2206512

# Electronic meeting, February 21 – March 3, 2022

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 38.101-2 | CR | 0011 | rev | - | Current version: | 17.4.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | x | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | CR to 38.101-2 on Requirements for coherent UL MIMO |
| --- | --- |
| Source to WG: | Huawei, HiSilicon |
| Source to TSG: | R4 |
| Work item code: | NR_RF_FR2_req_enh2 |  | Date: | 2022-03-01 |
| Category: | F |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | Define the RF requirement for UL coherent MIMO as 40-degree difference of relative phase error and 4dB difference of relative power error when side condition happens. |
| Summary of change: | The requirements for coherent UL MIMO are also applicable to the side condition including DRX on, BWP switching, SRS switching, DL measurement gap, etc. |
| Consequences if not approved: | The coherent gain cannot be guaranteed after the side condition occurring. |
| Clauses affected: | 6.4D.4 |
|  | Y | N |  |  |
| Other specs |  | x | Other core specifications | TS/TR … CR … |
| affected: | x |  | Test specifications | TS 38.521-2 |
| (show related CRs) |  | x | O&M Specifications | TS/TR … CR … |
| Other comments: |  |

| This CR’s revision history: |  |
| --- | --- |

<<< START OF CHANGE >>>

### 6.4D.4	Requirements for coherent UL MIMO

For coherent UL MIMO, Table 6.4D.4-1 lists the maximum allowable difference between the measured relative power and phase errors between different physical antenna ports in any slot within the specified time window from the last transmitted SRS on the same antenna ports, for the purpose of uplink transmission (codebook or non-codebook usage) and those measured at that last SRS. The requirements in Table 6.4D.4-1 apply when the UL transmission power at each physical antenna port is larger than 0 dBm for SRS transmission and for the duration of time window. The requirement is verified with the test metric of EIRP (Link=TX Beam peak direction, Meas=Link angle).

Table 6.4D.4-1: Maximum allowable difference of relative phase and power errors in a given slot compared to those measured at last SRS transmitted

| Difference of relative phase error | Difference of relative power error | Time window |
| --- | --- | --- |
| 40 degrees | 4 dB | 20 msec |

The above requirements apply when all of the following conditions are met within the specified time window:

-	UE is not signaled with a change in number of SRS ports in SRS-config, or a change in PUSCH-config

-	UE remains in DRX active time (UE does not enter DRX OFF time)

-	No measurement gap occurs

-	No instance of SRS transmission with the usage antenna switching occurs

-	Active BWP remains the same

-	EN-DC and CA configuration is not changed for the UE (UE is not configured or de-configured with PScell or SCell(s))

If UE reports to support capability of UL gap for coherent UL MIMO and the preparation time indicated by K2 in DCI for uplink transmission scheduling is larger than [6] slots, then 0.25ms UL gap is allowed to be used before PUSCH transmission and the requirements in Table 6.4D.4-1 can apply when the above conditions are not met within the specified time window.

<<< Skip unchanged sections >>>

<<< END OF CHANGES >>>

# Comments

K2_min_cal should be 1or2 slot longer than Tproc defined by 38.214. We consider [6] slots as reference and this value can be further checked.