3GPP TSG-RAN WG4 Meeting #102-e	R4-220xxxx

Electronic Meeting, 21 February – 3 March, 2022

Title:	LS on R17 NR MG enhancements – Pre-configured MG

Response to:

Release:	Release 17

Work Item:	NR_MG_enh-Core

Source:	RAN4

To:	RAN2

Cc:

Contact Person:

#### Name:	Li Zhang, Rui Huang

E-mail Address:	zhangli164@huawei.com, rui.huang@intel.com

Attachments: -

1. Overall Description:

RAN4 would like to inform RAN2 that RAN4 has reached the following conclusions related to Pre-configured MG during RAN4#102-e.

For PRS measurement with Pre-configured MG:

UE shall inform the network about UE is going to start/stop PRS measurement with the configured Pre-configured MG only if UE has not informed network before Pre-configured MG configuration. It is up to the network decision to activate/deactivate the current Pre-configured MG or to configure other legacy MG to UE.

For signalling-based Pre-configured MG activation and deactivation under CA:

For per-UE Pre-configured MG, UE assumes the Pre-configured MG is ON as long as the Pre-configured MG status for active DL BWP in one of the activated CCs or for one of the deactivated SCCs is ON, and UE assume the Pre-configured MG is OFF only if the Pre-configured MG status for active DL BWP in all activated CCs and for all deactivated SCCs are OFF. For per-FR Pre-configured MG, UE assumes the Pre-configured MG is ON as long as the Pre-configured MG status for active DL BWP in one of the activated CCs or for one of the deactivated SCCs in the same FR is ON, and UE assume the Pre-configured MG is OFF only if the Pre-configured MG status for active DL BWP in all activated CCs and for all deactivated SCCs in the same FR are OFF An additional ON/OFF indication for each SCell is needed to indicate the Pre-configured MG status when the SCell is de-activated.

RAN4 respectfully asks RAN2 to take the above information into account and define signalling support for signalling-based Pre-configured MG activation and deactivation.

2. Actions:

To RAN2:

RAN4 respectfully asks RAN2 to take the above information into account and define signalling support for the signalling-based Pre-configured MG activation and deactivation.

3. Date of Next TSG-RAN4 Meetings:

RAN WG4 Meeting #103-e		May 16 – May 27, 2022			Electronic Meeting

RAN WG4 Meeting #104		August 22 – August 26, 2022		Toulouse, France