3GPP TSG-RAN WG4 Meeting#102-e                               R4-220xxxx

E-meeting,21th Feb – 3rd Mar,2022

Agenda item:	10.5.2.3

Source: 	ZTE Corporation

Title: 	TP to TS 38.106 clause 6.9 ACRR requirement

Document for:	Approval

Introduction

Based on the worksplit, this TP is to introduce the ACRR requirement for FR1 conducted repeater. .

TP to TS 38.106 v 0.0.1

<Start of changes>

# 6.9	Adjacent Channel Rejection Ratio (ACRR)

## 6.9.1	General

Adjacent Channel Rejection Ratio (ACRR) is the ratio of the average gain over a carrier of the repeater in the pass band to the average gain of the repeater over an adjacent channel outside the repeater pass band. The carrier in the pass band and in the adjacent channel shall be of the same type (reference carrier) and both are assumed to have a bandwidth of min{100 MHz, passband BW}.

The requirement shall apply to the uplink and downlink of the Repeater, , where the donor link is maintained via antennas (wireless Repeater).

The requirement is differentiated between uplink and downlink.

The requirement shall apply during the transmitter ON period.

### 6.9.2	Minimum Requirements

For a repeater operating at pass band below 2496MHz, the ACRR requirements in table 6.9.2.1-1 shall apply in downlink. In normal conditions the ACRR for downlink shall be higher than the value specified in the Table 6.9.2.1-1.

Table 6.9.2.1-1: Repeater Downlink ACRR

| Co-existence with other systems | Repeater Class | Channel offset from frequency edge of pass band (MHz) | ACRR limit |
| --- | --- | --- | --- |
| UTRA, E-UTRA, NR | Wide Area repeater | min{100 MHz, passband BW}/2 | 45 |
|  | Medium Range repeater | min{100 MHz, passband BW}/2 | 45 |
|  | Local Area repeater | min{100 MHz, passband BW}/2 | 33 (Note 1) |
| NOTE 1: This requirement does not applicable if the pass band occupies the entire operating band. |

For a repeater operating at pass band above 2496MHz, the ACRR requirements in table 6.9.2.1-1a shall apply in downlink. In normal conditions the ACRR for downlink shall be higher than the value specified in the Table 6.9.2.1-1a.

Table 6.9.2.1-1a: Repeater Downlink ACRR

| Co-existence with other systems | Repeater Class | Channel offset from frequency edge of pass band (MHz) | ACRR limit |
| --- | --- | --- | --- |
| UTRA, E-UTRA, NR | Wide Area repeater | min{100 MHz, passband BW}/2 | 33dB |
|  | Medium Range repeater | min{100 MHz, passband BW}/2 | 33dB |
|  | Local Area repeater | min{100 MHz, passband BW}/2 | [33dB] (Note 1) |
| NOTE 1: This requirement does not applicable if the pass band occupies the entire operating band. |

For a repeater operating at pass band below 2496MHz, the ACRR requirements in table 6.9.2.1-2 shall apply in uplink. In normal conditions the ACRR for uplink shall be higher than the value specified in the Table 6.9.2.1-2.

Table 6.9.2.1-2: Repeater Uplink ACRR

| Co-existence with other systems | Repeater Class | Channel offset from frequency edge of pass band (MHz) | ACRR limit |
| --- | --- | --- | --- |
| UTRA, E-UTRA, NR | Wide Area repeater | min{100 MHz, passband BW}/2 | 33dB |
|  | Local Area repeater | min{100 MHz, passband BW}/2 | 33dB (Note 1) |
| NOTE 1: This requirement does not applicable if the pass band occupies the entire operating band. |

For a repeater operating at pass band above 2496MHz, the ACRR requirements in table 6.9.2.1-2a shall apply in uplink. In normal conditions the ACRR for uplink shall be higher than the value specified in the Table 6.9.2.1-2a.

Table 6.9.2.1-2a: Repeater Uplink ACRR

| Co-existence with other systems | Repeater Class | Channel offset from frequency edge of pass band (MHz) | ACRR limit |
| --- | --- | --- | --- |
| UTRA, E-UTRA, NR | Wide Area repeater | min{100 MHz, passband BW}/2 | 33dB |
|  | Local Area repeater | 5MHz | 20dBc (Note 1, Note 2) |
|  |  | min{100 MHz, passband BW}/2 | 33dBc (Note 1) |
| NOTE 1: This requirement does not applicable if the pass band occupies the entire operating band. NOTE 2: In this case, the channel withi n the passband and the adjacent channel are assumed to have a bandwidth of 10MHz |

<End of change>

# Comments

There is no RRC here, since it is not WCDMA. However the gain should be the average gain over the carrier

For core requirements, they should apply at any gain. Maximum gain is obviously the most stringent case though and so should be used for conformance testing.

Not sure what this means ?

In our understanding, this is not a co-existence requirement, it is a general requirement (like ACLR is). It is an in-band requirement

This is not the channel offset, it is the channel bandwidth. The offset should be half of this (so that the channel is the adjacent channel)

According to WF