## Slide 1
o
New 3GPP Band Allocation
2022
3GPP RAN4 Tdoc R4-2220503
Notes: Grid Modernization
Looking to Private Broadband Networks
How Private LTE Helps Utilities

## Slide 2
Spectrum Allocation
  Anterix is the primary 900 MHz spectrum holder in the US market*.
    DL: 935-940 MHz and UL: 896-901 MHz
Market History
  13 markets currently deployed with LTE in 1.4 & 3 MHz channels to support electric utilities.
  Utilized Network Assigned Duplexing (NAD) in Ue and eNB to support deployments.
    It is a subset of Band 8 with a 39 MHz duplex spacing instead of a 45 MHz gap.
  Over 80 vendors part of Anterix ecosystem
  Anterix has been active in 3GPP working to create support for NR in 3 MHz channels.
3GPP Plan
  Request a new band for LTE and NR that has the proper emission mask and duplex offset.
  Discuss proposal in Nov. Toulouse and submit discussion document to RAN 98e in Dec. 21
  Submit WID in RAN4 March 23
Industry Benefit
  The 900 MHz allocation is the only licensed broadband private network spectrum in the US market and is pushing 3GPP technologies to formerly closed markets.
  Chipset, Ue, module and infrastructure vendors all support creation of a new band to allow for better product support and advanced features such as carrier aggregation.
* https://anterix.com/report-and-order/
New Band Proposal Overview
3GPP RAN4 Tdoc R4-2220503

## Slide 3
Anterix Licenses
Licenses allocated on a per county basis – 3233 in the US
Anterix has the majority of all licenses (dark blue)
Multiple deployments and trials nationwide.
3GPP RAN4 Tdoc R4-2220503

## Slide 4
The 3GPP 900MHz/B8 allocation employs 45MHz duplexing
The FCC 900MHz allocation employs 39MHz duplexing
The BB frequency assignments for these allocations are as follows:
  3GPP Band 8 DL: 925-960MHz UL: 880-915MHz
  U.S. 900MHZ Center Frequency DL: 938MHz UL: 899MHz
U.S. 900MHz vs 3GPP Duplexing Considerations
3GPP RAN4 Tdoc R4-2220503

## Slide 5
3GPP Specification Language Reflecting Support For
Network Assigned Duplexing (NAD) for LTE and 5G
4G LTE
5G NR
The standard provides an OPTIONAL feature to support non-standard duplex offsets (NAD).
It does not have to be supported – thus the necessity for a new band.
This is sent from the base station and it is up to the device to accept this command.
We know multiple devices in 4G LTE do not support this and 5G support is unknown at this point.
3GPP RAN4 Tdoc R4-2220503

## Slide 6
Anterix will be requesting a new 4G LTE and 5G NR band to be assigned for our spectrum allocation.
This will include channel bandwidths:
  LTE: 1.4 MHz, 3 MHz and 5 MHz
  5G: 3 MHz and 5 MHz
Spectrum Bandwidth
3GPP RAN4 Tdoc R4-2220503

## Slide 7
Anterix Active Ecosystem 80+ Innovators Addressing Private Networks for Utilities
* General categorization: several companies address multiple categories.
BSS/OSS
Small Cells
Evolved Packet Core
AMI Meters
Security
Engineering/Consulting
UE/Devices
Solutions
Microgrids
Modules
Testing & Measurement
CBRS
Antenna
PTT Device/Apps
RAN Solutions
In-Building Wireless
Chipsets
Network Monitoring & Management
AR/VR Field Services
RAN Equipment
Smart City/ Smart Lighting
Supplier
Enclosures
3GPP RAN4 Tdoc R4-2220503

## Slide 8
This creation is similar to UIC/RMR railways in Europe (which we support) in creating a new band for their LTE and NR channel allocations.
NAD is not mandatory and very few chipsets support this going forward. This creates a sustainable path to 4G and 5G.
Allows “clean” path for band support in all devices (phones, routers, modules) to enable volume support and advanced features
  High power user equipment (HPUE)
  FCC emission mask for regulatory testing
  Support for TDD/FDD carrier aggregation (CA) and ENDC to commercial bands
  Coupled with the NR bandwidth less than 5 MHz WID, we can have 3 MHz channel support for 5G NR in the band
Industry Benefits for a new band
3GPP RAN4 Tdoc R4-2220503

## Slide 9
Q&A
Feedback on the new LTE and NR band proposal.
Collaboration to work within 3GPP RAN4 in creating a WI
Please feel free to contact me
  Emil Olbrich – eolbrich@anterix.com
3GPP RAN4 Tdoc R4-2220503